Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

IMPLEMENTING THE AGS LANDSLIDE RISK MANAGEMENT GUIDELINES IN A MUNICIPAL PLANNING SCHEME - A CASE STUDY IN THE COLAC OTWAY SHIRE, VICTORIA.

Peter G. Dahlhaus1 and Anthony S. Miner2
1 Dahlhaus Environmental Geology Pty Ltd & University ofBallarat
2 A.S. Miner Geotechnical Pty Ltd

ABSTRACT

The Colac Otway Shire in south west Victoria are in the process of amending their Planning Scheme to include landslide risk assessment for new developments in landslide prone areas. The amendment is primarily intended to limit the Shire’s liability and will require consultants to assess risk using the Australian Geomechanics guidelines on landslide risk management. However data limitations, particularly the paucity of historical information on landslide events, have precluded landslide hazard mapping for all types of landslides and their likelihood of occurrence, at the site-scale required for planning controls. The solution adopted was to extend the Erosion Management Overlay to cover all areas of the Shire in which landslides are credible, and the implementation of a documented process to determine when a landslide risk assessment for any development is required. The process includes reference to existing information stored on a GIS database, a checklist for use in an initial site visit by the Shire, specific requirements for consultant’s reports, and information checking and mediation processes for the Shire. The limited landslide risk management experience of the Shire planners and some small and medium-scale consulting companies has highlighted a local desire for a more prescriptive code.

1. INTRODUCTION

A review of landslide risk management for the Colac Otway Shire in south west Victoria has recently been completed by the authors. The two-year study focused on municipal planning controls for new developments, managed under the Shire’s Planning Scheme and concluded that the past planning procedures did not reflect the current thinking on landslide risk assessment and failed to adequately limit the Shire’s liability. In addressing this shortcoming, the Shire has adopted the Australian Geomechanics Society (AGS) guidelines on landslide risk management, which were published in March 2000 (AGS, 2000). From March 2002, any new development in the area of the Shire mapped as susceptible to landslides requires a risk assessment in accordance with the AGS guidelines.

1.1 COLAC OTWAY SHIRE

The Colac Otway Shire covers over 3,400 km2 in south west Victoria. Centred on the City of Colac. (Figure 1) the northern half of the Shire comprises the Western Victorian Volcanic Plains, and the Otway Ranges and foothills of the Victorian Southern Uplands dominate the southern portion. The average annual rainfall varies from approximately 550 millimetres on the northern plain to over 1900 millimetres on the crest of the Otway Range. Maximum rainfall occurs in late winter and early spring, with the greatest single day total of 167.4 millimetres at Apollo Bay. Primary industries, especially dairy farming and timber harvesting are the dominant land-uses. The past decade has seen an increase in tourism, especially associated with the Great Ocean Road along the spectacular coastline.

Over 900 landslides have been mapped in various studies within the Colac Otway Shire and it is estimated that thousands more, of varying sizes, exist (Figure 1 & Table 1). Landslides vary in area from a few square metres to over 60 hectares and in volume from a few cubic metres to over ten million cubic metres. They are triggered by prolonged and/or intense rainfall, elevated pore-water pressures, manmade changes to the landscape and rare earthquake events. The vast majority of landslides occur in two rock types, viz: the Cretaceous age Otway Group rocks and the Neogene Gellibrand Marl.

Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

| Data Source | Location mapped | No. of landslides | Method used and data | Estimated Accuracy |
| --- | --- | --- | --- | --- |
| Cooney, 1980 | Shire area south of Colac | 702 | 1946- 1950 Aerial photo interpretation, limited field checks, 1980 | ± 200 m |
| Wood, 1982 | Area between Wild Dog Creek and Busty Road | 35 | Detailed field mapping, 1982 | ± 25 m |
| Rosengren, 1984 | Shire of Otway, sites of geomorphological significance | 82 | Field mapping and aerial photo interpretation, 1984 | ± 100 m |
| Tickell, et al., 1991 | Colac 1:50,000 geological map | 72 | Field mapping and aerial photo interpretation, 1986 – 1987 | ± 100 m |
| Edwards, et al., 1996 | Colac 1:250,000 geological map | 10 | Compilation of existing maps, 1996 | ± 250 m |
| Previous geotechnical assessments | Development sites in existing planning control area | 41 | Field observation, 1986 – 1999 | Located to property polygon |
| Dahlhaus & Miner, 2001. McVeigh, 2001 | Colac Otway Shire, selected locations | 15 | Field mapping, 2000 - 2001 | ± 10 m |
| Total | 957 |  |

Table 1	Summary of existing landslide information in Colac Otway Shire

2. GEOLOGY

2.1 LOWER CRETACEOUS OTWAY GROUP

The Early Cretaceous Otway Group rocks that make up the majority of the southern portion of the Shire comprise volcaniclastic sandstones and shales that have been moderately strongly deformed. They are quickly and easily weathered and are regarded as the most landslide-prone of the geological units in southwest Victoria. Landslides occur in both the rock and soil materials, even where the rock is not significantly weathered (Wood, 1982). The Otway Group also exhibits the most voluminous slides of any geological unit.

2.2 TERTIARY SEDIMENTS

A variety of sediments were deposited in the mostly marine conditions that existed in the Otway Basin throughout the Tertiary Period, of which the Narrawaturk Marl and Gellibrand Marl are the most landslide-prone units. Landslides in the Gellibrand Marl have been extensively studied in the neighbouring Heytesbury region (Buenen, 1995; Miner, 1999), where they can occur on slope angles of only 6o. These studies found that in some cases the weathering of the marl resulted in changes to the mineralogy and mechanical properties of the upper regolith. These changes, in conjunction with pedogenic development, can create low-strength layers at shallow depths, on which movement occurs (Dahlhaus & Miner, 1998). Within the Shire landslides up to 47 hectares in area on slopes of 5-15% (3o–9o) are recorded in the Gellibrand Marl (Tickell et al., 199 1)

3. LANDSLIDE HAZARD

3.1 PREVIOUS STUDIES

Of several studies of landslides in the Colac Otway Shire (Table 1) the work carried out by the Geological Survey of Victoria between 1979 and 1990 is the most relevant. This work was conducted initially for the Town and Country Planning Board (Cooney, 1980) and later the Department of Planning (Cooney, 1982b). The initial regional study mapped over 700 landslides by interpretation of aerial photographs (Cooney, 1980). While this study classified many of the larger landslides as dormant, it recognised that many of the active smaller slides occurred within the area of the larger slides, and noted a close association between currently active landslides and previous failures.

Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

The initial broad-scale study was supplemented by a detailed field study of 35 landslides in the valley of Wild Dog Creek (Wood, 1982), regarded as one of the most landslide-prone areas of Victoria. These studies by the Geological Survey ultimately provided the basis of planning controls used by the Ministry for Planning and Environment and the Shire of Otway (Cooney, 1982b, MPE, 1986), and were inherited by the Colac Otway Shire following municipal amalgamation in the early 1990s.

3.2 HISTORICAL RECORD

Extensive research of the historical record confirmed the occurrence of numerous landslides in the Shire, however very few records of exact time and location of events were documented. Only three landslides have been well documented in the published literature:

Lake Elizabeth landslide

The Lake Elizabeth landslide, near Forrest, occurred on the 24th June 1952 following the wettest monthly rainfall on record (Currey, 1952; Cooney 1980; Dahlhaus, 1991). The landslide involved approximately six million cubic metres of rock, with a surface area of about 48 hectares. The slide formed a dam about 35 metres high and 400 metres wide that blocked the East Branch of the Barwon River, forming the 1.6 kilometre long Lake Elizabeth. On the 5th August 1953 the lake overflowed causing the top 26 metres of the landslide dam to fail and a wall of water and mud passed down the river, which overtopped the seven-metre (25 feet) high railway bridge at Barwon Downs, approximately 10 kilometres downstream. Significant damage was sustained to roads and bridges, and many farms were reported as financially ruined, as some had over 20 hectares of dairy pastures under silt. No personal injury was reported.

1952 landslide - Wild Dog Creek Road

A landslide triggered by heavy rainfall during June 1952 occurred at the junction of Wild Dog Creek and Busty Roads. The rock mass failed over a 390 metre section of the slope and the debris flow travelled another 410 metres downhill to block Wild Dog Creek. The dam resulted in some local flooding and deposition of an alluvial terrace. Drilling by Cooney (1982a) revealed that the 9 metre thick depositional fan at the Creek level had been deposited over several events.

1970 Windy Point Landslide

The Windy Point Rockslide on the Great Ocean Road south of Lorne, commenced with the removal of a relatively minor quantity of rock during road maintenance in late 1968. Several subsequent minor rock slides during 1970 and 1971 developed into the movement of up to 150,000 tonnes of sandstone, in large and small discrete blocks, moving down dip on the silty clay slip planes towards the road. The Great Ocean Road was closed between July and December 1971 while a cable anchoring system was designed and successfully installed (Neilson, 1970; Williams & Muir, 1972).

Anecdotal evidence and Observed landslides

Apart from the above three landslides, information is limited in consultant reports, poorly documented newspaper articles and Shire records, anecdotal evidence and casual observations. One active landslide, known as “the big slide” is situated on the eastern side of Wild Dog Creek approximately 5.3 km along Wild Dog Road from the Great Ocean Road. The unstable area extends over 16 hectares from Wild Dog Road to Busty Road and has been mapped into four zones, based on activity (P.J. Yttrup & Associates, 2001). Activity is triggered by heavy and/or prolonged rainfall. Debris flows and debris slides from the lower slopes of this large complex landslide have often closed the road during the past 50 years (Figure 2).

The Great Ocean Road has been subjected to damage from landslides since it was built during the 1930s. Within the
Shire boundary landslide debris is seen in outcrop in many cuttings along the road. Many of these slides remain active,
especially in the Wongarra area, where recent debris flows have impacted on the road. In October 2000 the road was

Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

covered by debris from two flows which occurred following heavy rain (Figure 3). These rapid, wet, debris flows were initiated in the body of an ancient landslide complex and travelled up to 100 metres to the road.

Rock falls are probably the most common form of landslide along the road, usually triggered by rain. However, at Brown’s Creek, anecdotal history records that a dairy was destroyed by a debris flow in 1953. Apparently, the remains of the building were contained in the debris which closed the Great Ocean Road for a time.

Figure 3. Two adjacent landslides that impacted on the Great Ocean Road, October 2000.

3.3 HAZARD PREDICTION

Several previous studies (eg. Joyce & Evans, 1976; Cooney, 1980, 1982b; Wood 1982; Buenen, 1995) attempted to relate landslide activity in south west Victoria to the angle of slope. However, in this study a correlation of landslide occurrence with slope or aspect based on a high resolution (20 x 20 metre) digital terrain model could not be established or justified given the occurrence of sliding on low angled slopes. In addition, anecdotal information and limited observation provides convincing evidence that extreme rainfall is the dominant trigger for landslides in the Colac Otway Shire. However, the paucity of information on the dates of landslide events restricted the opportunity to use the rainfall record to estimate the magnitude of cumulative antecedent rainfall that is likely to trigger landslides, such as has been used elsewhere in Australia (Chowdhury & Flentje, 1998).

Data from previous studies and the historical record limited hazard prediction in that:

- More than 70% of mapped landslides are derived from one study (Cooney, 1980) although the information is given the highest credibility. The landslides were mapped using stereo interpretation of 1:16,000 scale aerial photographs flown between 1946 and 1950. However, only large-scale landslides or those showing strong morphology are able to be recognized and mapped using aerial photographs. Many landslides are obscured by thick forest and vegetation, resulting in a bias towards distribution of mapped landslides on private land compared to Crown Land. Location of these mapped landslides is only accurate to +/- 200 m due to plotting limitations, although some have been recognized in the field and more accurately located during this study. Very few landslides which occurred after 1950 (including the 1951-1953 wet period) were included in Cooney’s study.

- Studies of the mapped landslides are spatially variable. The most detailed and accurate is the Wild Dog Creek Study of 35 landslides (Wood, 1982), which is limited to approximately 0.088% of the Shire, or 0.14% of the area considered susceptible to landslides. Similarly the landslides mapped on the Colac 1:50,000 geological map (Tickell, et al., 1991), covers approximately 17.7% of the Shire, and the Geological Heritage study (Rosengren, 1984) only maps specific sites.

- Apart from those of the Wild Dog Creek study, little information exists on the individual landslides that have been previously mapped. It is not known when they occurred, their style or state of current activity.

Given the paucity of information on landslides and the scale required for planning controls (i.e. site scale), the delineation of landslide hazard for all styles of landslides, including their likelihood of occurrence, was not practicable for the Shire. Hazard mapping requires a sufficient understanding of the interaction between of the preparatory factors and the triggering factors to derive the ‘rules’ for landslide potential at any place in the landscape. The economic and time investment required for site-scale delineation of hazard zones is substantial – possibly several million dollars and many years of data collection, as has been the case in Wollongong Shire (P.Flentje, pers. comm., 2001). This year the Shire has initiated a study for three towns (Wye River, Separation Creek and Kennett River) where the risk is perceived to be higher.

Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

Similarly, the classification of landslide risk for each property in the Shire cannot be attained. Risk is the product of both likelihood and consequence, and the assessment of the level of risk posed to every conceivable development (buildings and works) by each possible style of landslide (slide, flow, creep, fall and topple) and associated consequences on every site in the Shire is not feasible.

4. LANDSLIDE RISK ASSESSMENT – OUTCOMES OF STUDY

Figure 4. The extension (pale grey) to the Erosion Management Overlay covers the area of the Shire in which landslides are credible. The original 1982 landslide control area is shown in dark grey. The extension increases the area for landslide planning control from approximately 100km2 to over 2000km2.

An initial recommendation of this study was that the current Erosion Management Overlay (EMO) of the Colac Otway Shire Planning Scheme be extended to cover the areas of the Shire regarded as susceptible to landslides (Figure 4). The EMO does not represent a hazard map or zone, rather a planning overlay of all areas of the Colac Otway Shire in which landslides are credible. The Shire Council moved to extend the EMO in February 2002 and the process is currently being implemented.

The principal outcome of our study was to implement a process within the Planning Scheme to identify the proposed development sites within the overlay that required a detailed landslide risk assessment by a suitably qualified consultant. It was recognised that certain developments within the EMO overlay will have a very low risk of damage to property and loss of life through landslides and it is unreasonable to impose the additional expense and inconvenience of a landslide risk assessment on the developer. To resolve this matter, a process was recommended (Figure 5) that requires the Shire planners to extract existing landslide and geotechnical information from their GIS and then conduct a preliminary on-site assessment, to determine if the proposed buildings or works requires a Land Stability Assessment (LSA) report to be lodged with an Application for Planning Permit. The checklist procedure for the on-site assessments has been designed to be objective, formal, and transparent, and has been ratified by the Shire Council (Appendix 1). It is emphasised that the checklist procedure is not a landslide risk assessment, but provides a formal and accountable method for the Shire staff to eliminate very low risk developments (eg. the erection of a hay shed on flat land distant from steep slopes). Training the Shire staff in the proper use of the procedures has provided them with limited landscape recognition skills, and an evaluation and continuous improvement program has commenced to modify the procedures where required.

The majority of proposed developments within the EMO will require a landslide risk assessment, to be undertaken by a qualified and experienced professional, in accordance with the AGS (2000) guidelines. The Planning Schedule requires that the assessment be undertaken by a professionally qualified engineering geologist or geotechnical engineer with either (a) five years practical experience in slope stability assessment in the Colac Otway Shire or (b) ten years practical experience in slope stability assessment in areas other than Colac Otway Shire or (c) three years practical experience in slope stability assessment and a postgraduate qualification in a field related to slope stability studies. The landslide risk assessment report is required to state the risk for damage to property (qualitative or quantitative) and the risk of loss of life (quantitative), as well as recommendations whether the development should proceed and the risk treatment required.

Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

5. IMPLEMENTATION OF THE AGS GUIDELINES - ISSUES

Whilst the proposed changes to the EMO have yet to be formally incorporated into the Colac Otway Planning Scheme, the revised process has been implemented in the inte	iod, as the Shire is now in receipt of new information

rim per

relating to landslide risk management and have acted to limit their liability. Implementing the use of the AGS guidelines is a key element of the proposed changes and it has highlighted a number of issues for the Colac Otway Shire (The Regulator), the consultants previously carrying out stability assessments (The Consultants) and the applicants and developers faced with changes to the previous planning scheme (The Client).

5.1 THE REGULATOR - THE COLAC OTWAY SHIRE

Although the Colac	hire covers a lar	of Public Land consi	s revenue base.

Otway S	ge area, the extent	derably reduces it

The provisions for landslide risk assessment were inheri d from the former Shir	municipal

te	e of Otway following

am	tion and few o	current planning staff have sufficient experience with landslide issues. The Shire does not

algama	f the

e	echnical engineer or engineering geologist	specifically deal with the landslide issue. As a result of

mploy a geot	to

these limited internal resources, the Shire is not equipped to handle the more flexible approach to landslide risk assessment as advocated and recommended in the AGS (2000) guidelines.

As previously stated, the Shire’s main focus during the review was to limit their liability and exposure to litigation. In their role as regulator, the Shire demanded a formal process to assess Planning Permit Applications for development in areas susceptible to landslides that was rigid, accountable, unambiguous, transparent, fully documented and legally and socially defensible. By implication, this indicated a preference to transfer liability to the consultant and the client where possible.

Without doubt, the endorsement of the AGS guidelines in the NSW Coroner’s report	Landslide and

on the Thredbo

their distribution to every local government authority in Australia were key factors in the adoption of the AGS
guidelines by the Colac Otway Shire. The Shire planners and Shire Councillors view the AGS (2000) guidelines as the
de facto National code of practice. Even though the Shire has expressed a difficulty in understanding parts of the
guidelines, especially the quantification of risk of loss of e, their planning process requires that the consultants use
lif

this method because it is recommended by the AGS (guidelines), and the use of the guidelines	e key element in

is th

their defensible process.

5.2 THE CONSULTANTS

The experience of the Colac Otway Shire is that the larger multi-national consultants, who may be best qualified to handle the flexible approach of the AGS guidelines, are generally unwilling to do assessments for domestic residences because they are viewed as high risk, low return projects for one-off clients who may default on payment if the result is negative. Consequently there have been very few landslide risk assessments in the Shire by the larger consulting companies over the past decade.

The AGS guidelines acknowledge landslide risk assessment s a relatively new technique. In implementing the revised

i

landslide	nagemen	cess, t	ckly discovere	st mid	ge a	ing companies

risk ma	t pro	he Shire qui	d that mo	-ran	nd smaller consult

did not have extensive experience in landslide risk assessment. It is also true that these same consultants do not have the time	es or experience bas	ment the fl	roach for relativ	ee, high workload

, resourc	e to imple	e xible AGS app	ely low f

projects such as landslide risk assessments for domestic house sites, using the approach published by the AGS. Our experience of the implementation of the AGS guidelines is hat many consultants new to risk assessment are generally

t

poor at implementing the various methods and approaches for determining frequency, vulnerability, runout distances and consequence. Unfortunately, some consultants place less importance on identifying the potential types of hazards and potential consequences and are more importance on compliance with the stated requirements of the Shire.

In the absence o	orical observ	understandi	morphological evol	on provides the

f hist	ations, an	ng of the geo	ution of the regi
best starting point for landslide recurrence data. As an example, the Plio-Pleistocene tectonic history of uplift in the
Otway Ranges and the Quaternary sea level changes indicate that many landscapes are less than 3000 years old,
including the largest coastal landslid	ahlhaus & Miner, 2002). This knowledge can be further refined using

es (D

regional rainfall records, experience, observations and site measurements to provide a reasonable	ate of frequency.

estim

Whilst there may be a belief among some of the larger consultants that the AGS guidelines are too prescriptive, the experience in the Colac Otway Shire indicates many of the smaller consultants would welcome a more definitive st both the Shire planners and the consultants servicing the Shire are comfortab

andard or code. At the present le with the qualitative method (AGS, 2000 - Appendix G) for calculating risk for damage to property. Both would also favour the adoption of a qualitative method of calculation for loss of life such as that suggested by DeAmbrosis (2000).

Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

Although the guidelines provide a number of methods to calculate frequency, the majority of consultants in the Shire rely solely on the visual inspection and observational approach. The paucity of historical data highlights the urgent need for further research on landslide types and sizes, frequency or recurrence, runout distances of different styles of landslides, vulnerability and consequence in the region. Such extensive research programs are only feasible within the realms of universities, research organisations (eg. CSIRO, CRCs) or Shires with a higher revenue base which are serviced by experienced and qualified consultants

5.3 THE CLIENTS – PERMIT APPLICANTS

With the implementation of the AGS guidelines, the Shire reviewed a number of Applications for Planning Permits and requested further information on landslide risk. In these cases, the previous landslide assessments were deemed unacceptable on the basis that they contained insufficient detail to provide the Shire planners with the confidence to issue a Planning Permit, in light of the new guidelines. Whilst applicants accept that new guidelines have been implemented they resent incurring additional substantial costs for a process they do not understand. Consequently some applicants have not proceeded with development due to the additional costs of obtaining an AGS compliant report or costs associated with the revised risk treatment plan for their development. A few applicants have signalled their intent to challenge the Shire’s decision at the planning tribunal although no cases have yet proceeded to arbitration. Despite a number of community consultative meetings held by the Shire to explain the changed planning procedures, some residents - even those in the most landslide prone coastal areas - are still disbelieving of the need for landslide risk assessment. Consequently, there is a suspicion among some of the residents and developers that the Shire is overregulating development.

- CONCLUSIONS

Whilst the introduction of landslide risk management concepts and guidelines for use by regulators, consultants and their clients is strongly supported, our experience suggests that each group has a different perception of the risk and different expectation of the guidelines. Our experience in implementing the AGS guidelines in the Colac Otway Shire suggests that the under-resourced regulator seeking to limit liability desires a prescriptive and definitive code of practice. This would include a standard qualitative risk matrix for both property and for life, which was specific for domestic or light industrial development with definitive guidelines on good and bad hillside building practice. Additionally, the Shire would welcome a clearer explanation of acceptable and tolerable risk and published National standard acceptance criteria. Although excellent guidance on landslide risk assessment has been published (eg. Fell, et al., 2000) the small-scale consulting companies with limited risk management experience still seek explicit standard practices for quantitative assessment of risk. Furthermore, there is an urgent need for detailed information on good hillside development procedures, including building construction, wastewater and stormwater management. Ongoing education of the public, consultants and the regulators is strongly supported, as is the need for targeted landslide research and the dissemination of research findings.

Many municipalities around Australia will be in a similar situation to the Colac Otway Shire, with known hazards but insufficient data to produce hazard maps on site scale or accurately assess frequency, runout distances and assess vulnerability. Like the Colac Otway Shire, some will include the AGS guidelines as part of a rigid and defensible process within the regulatory framework of a Planning Scheme to limit their liability. Further development of the guidelines to take into account their use and user’s expectations is welcomed.

7. ACKNOWLEDGEMENTS

The authors acknowledge the support planning, environment, and GIS staff of the Colac Otway Shire, especially Wendy Briggs, Rob Davis, Rob Hutchison, Steve Mitchell, Greg Slater and Mark Walker. Mr John Bennett (John Bennett & Associates, consulting planners) and Dr Phil Flentje (University of Wollongong) are thanked for their discussions and input to the project. The constructive comments by Prof. Robin Fell were of benefit to the manuscript.

- REFERENCES

AGS 2000. Landslide Risk Management Concepts and Guidelines Australian Geomechanics 35/1, pp.49-92. Australian Geomechanics Society Sub-Committee on Landslide Risk Management.

Buenen B.J. 1995. Soil slope failure processes in the Heytesbury Region. B.App.Sci.(Hons) Geology, research thesis, University of Ballarat (unpubl.) 50p.

Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

Chowdhury R.N. & Flentje P. 1998. Effective urban landslide hazard assessment. Proceedings, 8th International Congress, International Association for Engineering Geology and the Environment, 21-25 September 1998, Vancouver, Canada, Vol.2, A.A. Balkema, pp.871-878

Cooney A.M. 1980. Otway Range landslide susceptibility study - first progress report. Geological Survey of Victoria Unpublished Report 1980/76

Cooney A.M. 1982a. Report on drilling results in the Parishes of Kaanglang, Krambruk and Wongarra, Shire of Otway. Geological Survey of Victoria Unpublished Report 1982/100

Cooney A.M. 1982b. Geological hazards in parts of the Parishes of Kaanglang, Krambruk and Wongarra, Shire of Otway. Geological Survey of Victoria Unpublished Report 1982/105

Currey D.T. 1952. Landslide on the East Barwon. Aqua, 3/11, pp. 18-19

Dahlhaus P.G. 1991. Engineering and environmental geology. in: Introducing Victorian Geology, (Cochrane G.W., Quick G.W., & Spencer-Jones D., eds) Geological Society of Australia (Victoria Division), Melbourne, pp.265- 304

Dahlhaus P.G. & Miner A.S. 2002. A geomorphic approach to estimating the likelihood of landslides in south west Victoria, Australia. Proceedings, 9th International Congress, International Association for Engineering Geology and the Environment, 16-20 September 2002, Durban, South Africa, (in press).

Dahlhaus P.G. & Miner A.S. 1998. Stability of clay slopes in south west Victoria, Australia. Proceedings, 8th International Congress, International Association for Engineering Geology and the Environment, 21-25 September 1998, Vancouver, Canada, Vol.2, A.A. Balkema, pp. 1551-1556

Dahlhaus P.G. & Miner A.S. 2001. Colac Otway Shire Landslide Risk Management. Final Report. Dahlhaus Environmental Geo logy Pty Ltd and P.J. Yttrup & Associates Pty Ltd, 52p.

DeAmbrosis, L. 2000. Letter to the Editor re: Landslide Risk Management Concepts and Guidelines report by AGS

sub-committee, AGS Journal Vol 35. No.1 March 2000. Australian Geomechanics 35/3, pp. 114-116

Edwards J., Leonard J.G., Pettifer G.R., & Mcdonald P.A. 1996. Colac 1:250 000 map Geological Survey of Victoria

Report. 98, Department of Natural Resources and Environment, 168p.

Fell, R., Hungr, O., Leroueil, S. & Riemer, W. 2000. Keynote Lecture- Geotechnical Engineering of the Stability of Natural Slopes, and Cuts and Fills in Soils. Proceedings of GeoEng2000, 19-24 November 2000, Melbourne, Australia. Volume 1: Invited Papers, pp.21-120.

Joyce E.B. & Evans R.S. 1976. Some areas of landslide activity in Victoria, Australia. Proceedings of the Royal Society of Victoria, 88/1, pp.95-108

McVeigh, J.A. 2001. A landslide database for southwest Victoria. B.App.Sci.(Hons) Geology, research thesis, University of Ballarat (unpubl.) 1 1 1p.

Miner A.S. 1999. An investigation of a landslide in Gellibrand Marl in the Heytesbury region, Victoria. M.App.Sci. Geology, research thesis, University of Ballarat (unpubl.) 186p.

MPE 1986. The Rural Land Mapping Project, Shire of Otway, Ministry for Planning and Environment, May, 1986 (reprinted 1987). 85p + appendices.

Neilson J.L. 1970. Landslip problem at 89.1 mile location on Ocean Road, at Windy Point, near Lorne. Geological Survey of Victoria Unpublished Report 1970/12

P.J. Yttrup & Associates. 2001. Big Slide Wild Dog Creek Road. P.J. Yttrup & Associates Pty Ltd Consulting Report No. 13425, for Colac Otway Shire, April 2001.

Rosengren N. 1984. Sites of geological and geomorphological significance in the Shire of Otway. Department of

Conservation, Forests and Lands report ESP No. 399, Department of Conservation, Forests and Lands, 320p. Tickell S.J., Cummings S., Leonard J.G., & Withers J.A.1991. Colac 1:50 0 00 map. Geological report. Geological

Survey of Victoria Report 89, 53p.

Williams A.F. & Muir A.G. 1972. The stabilisation of a large moving rock slide with cable anchors. Proceedings, 3rd South East Asian Soil Mechanics Conference, Hong Kong, November 1972, pp. 179-187

Wood P.D. 1982. Wild Dog Creek, Parish of Krambruk, landslide study. Geological Survey of Victoria Unpublished Report 1982/85

Appendix 1 Preliminary on-site assessment checklist (Colac Otway Shire)

Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

Australian Geomechanics, Volume 37, No.2, May 2002 pages 199-211

# Text boxes

The underlying intent in the recommended procedures for assessing Planning Permits has been to limit the Shire’s liability, whilst providing a fully documented framework for the Shire, consultants and their clients to operate within.

Figure 5. Recommended flowchart for assessing Planning Permit Applications within the EMO.

10

12