For further information contact: Bruce Gill

Primary Industries Research Victoria Department of Primary Industries Tatura

Private Bag 1

Ferguson Road

Tatura

Victoria 3616

Phone: (03) 5833 5330 Fax: (03) 5833 5299 Email: bruce.gill@dpi.vic.gov.au

Published by  Primary Industries Research Victoria

Department of Primary Industries

Tatura Private Bag 1

Ferguson Road

Tatura Victoria 3616

February 2006

Find more information about DPI on the Internet at: www.dpi.vic.gov.au

Disclaimer

The information contained in this report is offered by the State of Victoria, through its Department of Primary Industries, solely to provide information. While the information contained in this report has been formulated with due care by the Department of Primary Industries, the State of Victoria, its servants and agents accept no responsibility for any error, omission, loss or other consequence which may arise from any person relying on anything contained in this paper.

ISBN 1 74146 627 X

© State of Victoria, Department of Primary Industries, 2006

ii

Executive Summary

This report

This report is the final output from a Multi-regional NAP funded project that commenced in 2003 - 2004 financial year. The primary objective of the project was to develop a systematic approach to test the suitability of known dryland salinity priority areas to engineering based salinity control options. A second stage of the project was originally proposed, but has not proceeded. Under this second stage and following the development of a workable site selection process, three sites within Victoria were to be selected for detailed investigation. The ultimate goal was to prove whether innovative salinity and nutrient management technologies can be soundly based, well supported and successful, and thus seed further works in the state. These solutions would then sit alongside agronomic options as a way of treating dryland salinity across the country.

Terminology

In this study, a starting premise is that an 'Innovative Management Technology' (IMT) solution to be applied to a dryland salinity or surface water quality problem will invariably involve collecting and extracting groundwater by an 'engineering' means (ie a groundwater pump, sub-surface drains or surface drainage system). The 'innovation' element is how that water would be used or disposed of. In this report, use of the term 'engineering option' refers to the method of extracting groundwater. This is a necessary precursor to development of any 'innovative technology' system. IMT is an all encompassing term used to cover a comprehensive system of technical management of a salinity problem.

In referring to an 'integrated engineering-agronomic option', the main premise is that the extracted water (and contained salt and nutrient load) is used productively and safely within a production system that can contain the salt load for the long term. Water quality and any assets downstream are thus protected from damage or loss by the operation of the system.

Review of IMT options

The work by SKM (2001b) for the NDSP was the first systematic attempt in Australia to consider the prospects for engineering based dryland salinity solutions. A highlight of this work was the development of a web-based decision support tool and the review of 17 engineering based examples from around Australia. While this work improved the knowledge base upon which IMT solutions might be developed, there has been no apparent increase in applications of such options in dryland areas.

It appears that key reasons why IMT options are not proceeding in dryland areas are that:

- Economics are not favourable

- Social considerations are proving difficult

- Environmental impacts are not being dealt with, and

- Regulatory aspects are not favourable.

In reviewing Victorian examples of engineering based trials, most have focussed only on the extraction process, and monitoring has not shown salinity benefits that can be clearly attributed to the works.

Regulatory Issues

A review of Governance, regulations and legislation undertaken as part of this study identified a range of aspects of any potential IMT schemes that could be subject to regulations. Given that IMT solutions are rare and each one has so far been unique, standard regulatory responses do not exist. Any regulatory response would be dependent upon the scale and design of the proposal. During the feasibility study stage of any IMT option development process, a systematic assessment of regulatory requirements should be undertaken. The proposal would then either be designed to eliminate any need to invoke regulations or be designed to meet existing regulations.

iii

Reference Group and Stakeholder Input

At the commencement of this project, contact was made with a range of stakeholders with the intention of forming a reference group to oversee progress in the project and provide input. A number of meetings were arranged during the earlier stages of the work, and input that helped frame the study was obtained.

This input was valuable in providing examples of priority salinity areas within catchments and in providing context and CMA staff perceptions of locations that might be suitable for IMT options. The work carried out by each CMA to prioritise locations on the basis of salinity risk provided a range of locations upon which this study could consider. The meetings were especially useful where they involved visits to salinity problem sites and helped define the biophysical aspects of the study.

Site Selection Method

Having reviewed the current state of engineering options knowledge and considered the regional picture, the study developed a methodology to systematically assess the suitability of sites for an I MT option.

Underpinning this approach was the assumption that CMAs have already identified priority dryland salinity areas and that sufficient information about each area was available. On this basis, the project team weighed up possible methods of assessment and the relevant criteria.

The site assessment process developed is based on the principle of a filter. This involved developing a series of targeted questions to which “yes” or “no” responses are given based on expert knowledge. The fundamental point of the questions is whether the characteristic is favourable or unfavourable to the development of an IMT option. The development of these questions required the identification of the important factors that determine whether a site has favourable or unfavourable characteristics. These were targeted at four key aspects:

- Knowledge about the site

- Assets at risk (including the value or importance of the assets and degree of risk)

- Hydrogeological conditions

- Intercepted water re-use

An important information source now available to CMAs is the groundwater flow systems concept. This gives a good start to the process by providing ready access to salinity related hydrogeological data. Information on assets and salinity occurrence is variously available and was obtained through CMA discussions and in previous salinity prioritisation work reports.

Sites can be easily ruled out if there is insufficient information. However, a key difficulty encountered in testing of the filter approach was the high level of expert judgement, subjectivity and uncertainty involved in the consideration of the assets at risk, the hydrogeological conditions, the type of control option to select and potential re-use options. This subjectivity in many respects is the Achilles heel of the original intent of the project. It also underpins the reasons why there are so few successful engineering based control options in dryland sites.

Site Filter Tool

Following the development of the site selection tool logic, the chosen questions and process were tested on North Central CMA salinity priority catchments. Through some trial and error, a workable spreadsheet was compiled and this was then tested in Corangamite CMA and Glenelg-Hopkins CMA priority salinity sites. In the Glenelg-Hopkins CMA, the 'sites' were groundwater flow system (GFS) types. This testing showed both positive and negative aspects of the process.

Having tabulated results for the salinity priority areas in each CMA, the project was able to consider the implications and subsequent actions that arise from having identified several sites (or GFS) that have favourable characteristics for an IMT option.

iv

Difficulties of Scale

In considering suitable engineering based options for a sub-catchment, the diffuse nature of dryland salinity discharge and the different scales at which it can be managed are critical issues. Will a single, large scheme be practical? Would a large number of separate, small schemes targeted at each known discharge system be more effective? Is an integrated system of control points at every discharge location possible? Any engineering based scheme will involve works of some sort at one or several locations, however the filter process as applied at the NAP catchment scale was not able to resolve to sufficient detail such sites specific details. To improve resolution at a sub-catchment scale, the filter tool could then be used compare a number of discrete salinity occurrence areas in a favourable sub-catchment with respect to their suitability for IMT options, assuming there is sufficient data to do so.

Selecting 3 Sites for a Stage 2 Study

The project objective was to find three favourable sites for further assessment and business case development. At the outset, this seemed attainable. However, having worked through the logic of the issues and put together a site selection process, the sheer complexity of the task has become apparent.

While there are dryland salinity sites throughout the CMAs that scored favourably in the filter process developed, it was not clear that any of these locations should have additional investment to investigate an IMT option. In this respect, the project has failed to meet its original objective.

However, what has been learned through this process is significant and of great value to CMAs, communities and funding organisations.

What has been found?

Foremost among the findings of value from this project is a clearer understanding of the probability of engineering based solutions for dryland salinity problems being viable in Victoria. The study has also generated a systematic process that contains targeted questions that can be used whenever an engineering based solution is proposed.

The complexity involved in the consideration of IMT solutions in dryland salinity impacted areas makes building a sound 'business case' for their development a significant challenge. The main uncertainties include:

- The practicalities of groundwater extraction

- The availability of suitable disposal or reuse options.

- Uncertainty about future levels of salinity

- Inadequate suitable data at the spatial resolutions required for site assessment. The scenarios where an IMT solution may be favourable are:

- Where there is a well defined asset clearly at risk from salinity

- Engineering systems can intercept water effectively and efficiently

- The intercepted water can be productively and sustainably used

- At the farm scale, where a simple, small-scale salinity occurrence can be treated by a
basic collector system and the water re-used on site to contain the salt or nutrient.

Recommendations

- There is a very low probability that widespread adoption of engineering based solutions for dryland salinity will be justifiable in Victoria.

- At the farm scale, the most likely circumstance where a system could be feasible is that of a small site with simple and favourable hydrogeology. Such a site would have to be amenable to an efficient collection system and an agronomic system that can sustainably contain salt or nutrient on site. Implementation of such systems should aim to achieve multiple outcomes such as biodiversity enhancement.

v

( The only circumstance where an engineering based solution has potential is where a highly valued asset is at substantial direct risk of salinity damage that cannot be more efficiently resolved by other means.

- The existence of potentially viable sites for implementation of engineering options for dryland salinity and water quality management is not precluded by the inability of this project to identify them.

- Data at the catchment scale on dryland salinity and water quality problems is largely inadequate or unsuitable to resolve down to the level necessary to support the catchment wide approach to assessing suitability for IMT options.

- That Stage 2 of this study as originally proposed not proceed.

Acknowledgements

This study was funded under the Multi-Regional Grants program of the National Action Plan for Salinity and Water Quality. It was conceived in a project proposal developed by Michael Morris and

Mark Reid and was successful in attracting funding in part because its focus was on innovative solutions to dryland salinity.

The Project team consisted of Michael Morris, Mark Reid, Bruce Gill, Peter Hekmeijer and David Heislers

Input and discussion with staff from several Victorian CMAs including Corangamite, Glenelg Hopkins, North Central, Goulburn Broken and the Mallee as well as regional DPI staff was valuable in focussing the study on CMA priority salinity problem areas.

Abbreviations

CAS	Catchment and Agricultural Services (of DPI)

CLPR	Centre for Land Protection Research

CMA	Catchment Management Authority

CSIRO	Commonwealth Scientific and Industrial Research organisation

DPI	Department of Primary Industries

DSE	Department of Sustainability and Environment

EOV	End of Valley (salt load targets)

EPA	Environmental Protection Authority

GFS	Groundwater Flow System

GMA	Groundwater Management Area

ICM	Integrated Catchment Management

ICSRP	Integrated catchment salinity risk and prioritisation

IMT	Innovative Management Technologies

LWSMP	Land and Water Salinity Management Plan

L&WMP	Land and Water Management Plan

MDBC	Murray Darling Basin Commission

NDSP	National Dryland Salinity Program

NAP	National Action Plan (for Salinity and Water Quality)

NHT	Natural Heritage Trust

NLWRA	National Land and Water Resources Audit

NRM	Natural Resource Management

PIRVic	Primary Industries Research Victoria

PPA	Pest Plants and Animals

RWA	Rural Water Authority

RCS	Regional Catchment Strategy

SKM	Sinclair Knight Merz

WSPA	Water Supply Protection Area

1.	Introduction

1.1 Project Background

This project was conducted under National Action Plan for Salinity and Water Quality Victorian Multi-Regional grants program with the following objective (from the proposal):

'To develop and impart a greater science-based knowledge of the potential applications (type and location) of engineering/agronomic salinity and nutrient management techniques, in order to better inform, target and stimulate future catchment management investment and policy development. This is completely in accord with the main goal of the NAP, which is to motivate and enable regional communities to use coordinated and targeted action to (a) prevent, stabilise and reverse trends in salinity, particularly dryland salinity, and (b) improve water quality and secure reliable allocations for humans, industry and the environment.'

In establishing the basis for this project and articulating why it has been a valuable investment in dryland salinity management, a recent, comprehensive review (SKM, 2001) described the technical and economic aspects of dryland salinity engineering options and provided case studies from across Australia. A key conclusion from that study was:

'It is considered that further knowledge is needed to assist communities in assessing the impacts, such as salt loads, impact on downstream water quality, and the economic costs of disposal. Part of this should involve establishing procedures, including institutional guidelines, to document the catchment priorities and generate targets for downstream water quality. Decisions need to be clearly made under a structure that provides responsibility and accountability for the assessment of the need for actions and the appropriate implementation.'

Much knowledge about potential management options for dryland salinity already exists. Considerable effort over the past few years has also been invested in developing decision support tools to guide development of engineering solutions for dryland salinity problems. (NDSP website) However, little uptake of engineering solutions in dryland areas has occurred in Victoria. Factors responsible for this limited uptake include:

- engineering options need to be tailored to each site,

- the ideas are new and relatively untested,

- significant technical assessment and expertise may be required for success,

- drought,

- changing farm economics, and

- a sound business case (ie. systematic addressing of the practical and financial aspects of the solution) needs to be established to justify implementation of capital intensive schemes, especially if public investment and social impacts are likely.

This project was therefore very much focussed on testing the potential of engineering approaches to dryland salinity management by working through the issues identified in the conclusion comment (above) from the SKM study. By focussing on a number of catchments in central and western Victoria with substantial dryland salinity problems, the project aimed to identify where innovative salinity and nutrient management technologies could be soundly based, well supported and successful.

The project aimed to develop a consistent and rigorous approach that could be used to take catchment communities through the first step of the process, that is, the identification and prioritisation of potential sites where an engineering based option would be the best solution.

While the overall study focus was on trying to take science and engineering principles to a complete, working solution, it was evident that the science and engineering aspects must favourably converge with social, economic and practical aspects. If one or more of these aspects is unfavourable, then there is significant likelihood that a successful integrated engineering - agronomic option will not result. A possible outcome from this work is a realisation that although engineering based options

10

are possible in theory, there are very few cases in Victoria where all the necessary elements occur in alignment.

1.2 This Report

This report documents the work carried out from October 2003 to June 2005. This is the stage 1 milestone report as described in the Project proposal (Appendix 1).

The main outcomes proposed in the proposal at the completion of stage 1 were:

- Establishment of a project stakeholder reference group

- A review of relevant legislation, regulation, institutional aspects and review of potentially applicable Engineering based innovative management technologies.

- Development of a site selection methodology endorsed by stakeholders.

- Testing of the site selection methodology in identifying potential sites within the participating catchments and documenting the process and results.

- Endorsement of the selected site by the project stakeholders.

A key output attached to this report is the spreadsheet developed to accumulate site information and filter the sites to identify the most prospective ones. A copy of this site selection tool is available by visiting the Victorian Resources Online website:

http://www.dpi.vic.gov.au/dpi/vro/vrosite.nsf/pages/vrohome

1.3 Terminology

In discussing 'innovative technologies', for salinity and water quality management, a starting premise in this study has been that an innovative solution will usually involve collecting and extracting groundwater by an 'engineering' means (ie a groundwater pump, sub-surface drains or surface drainage system). The 'innovation' is in how the extracted water is managed. In general, use of the term 'engineering option' refers to the method of extracting groundwater. This is a necessary precursor to development of any 'innovative technology' system, the overall term used to cover a comprehensive system for technical management of a salinity problem.

In referring to an 'integrated engineering-agronomic option', the main premise is that the extracted water (and contained salt and nutrient load) is used productively and safely within a production system that can contain the salt and nutrient load for the long term. Water quality and any assets downstream are thus protected from damage or loss by the operation of the system.

2. Review of IMT Options 2.1 The national perspective

SKM (2001b) assessed the efficacy of engineering options for the management of dryland salinity nationally. They concluded that there were only a minimal number of case studies that were adequately documented to allow considered assessment of the engineering option. Of the 17 case studies, at least four were taken from designated irrigation areas or where irrigation was the substantive cause of a neighbouring dryland salinity issue.

Many of the case studies were taken from the extensive salinised landscapes of the Western Australian wheat-belt. Pannell (2001) argues that even here, despite the groundswell amongst farmers in deploying predominately deep surface drains to combat salinity, that significant uncertainty remains amongst the farming and scientific communities in regard to the economic and environmental viability of this solution.

Pannell (2001) also suggests that intended broad-scale salinity control solutions, whether of an agronomic or engineering type, are unlikely to achieve their outcome unless this can be achieved through a focus on economics. He emphasises that the most efficient public investment is in strategically targeting the protection of specific assets. Further to this, Pannell (2001) suggests the importance of developing improved methods for productive use of saline land and water and is therefore an advocate of targeted innovative solutions.

In dryland salinity management, numerous engineering based solutions are possible. These are outlined in detail in SKM (2001 b) and can be broadly categorised as:

- Groundwater pumping (single bore, multiple bores, spear points and relief bores)

- Shallow surface drains for recharge control (spoon drains, “W” drains)

- Deep surface drains for watertable management (open drains)

- Sub-surface drainage systems (mole, tile, biopolymer and interceptor drains)

- Construction approaches (construction standards and corrosion resistant materials)

SKM (2001b) also produced the first systematic attempt to spatially classify the landscape at the national scale with respect to possible engineering options. The range of possible engineering solutions were broadly attributed against the classification of Australian Groundwater Flow Systems of Coram (1998). This work was developed as a guide only, because local site conditions control what is technically possible at specific sites. Though this was a significant advancement in placing potential engineering options in a catchment context, it is only when one focuses at the site scale that one understands the full and unique complexity of contemplating an engineering solution.

Guidance about the range of engineering solution choices is embedded in a web based decision support tool found on the NDSP site (http://www.ndsp.gov.au/). This also considers the likely success criteria for a particular engineering option as well as a preliminary assessment of the economic and environmental effects of particular options. The economic evaluation within the decision support tool does not include the environmental cost of disposal (Nolan ITU 2005). It allows simple hydrogeological modelling (spreadsheet based) of an idealised engineering option. SKM (2001 a) state that “If a particular option looks favourable for the local site, salinity managers need to investigate future ways of detailed evaluation which consider the ultimate objectives, the scale, cost and other regional factors such as disposal.”

Apart from this broad contexting of engineering solution efficacy, there are few examples where a systematic approach to dryland engineering solutions have been undertaken at a site level. At the site level, additional considerations quickly emerge that complicate the decision (aside from the technical feasibility of the groundwater extraction technology itself). Four key issues are:

- Economic considerations pertaining to the extraction and then reuse of groundwater. The relationship between groundwater extraction and degree of asset maintenance is often more difficult to estimate and therefore to economically justify in dryland settings. The separation of public and private benefit from public investment can also be obscure.

- Social considerations arise in landscapes where engineering solutions for dryland salinity control are not usual.

12

( Environmental impacts, especially of groundwater disposal

- Regulatory aspects, such as groundwater licensing, planning requirements, disposal constraints, new irrigation development controls.

In contrast, the relative success of engineering solutions in irrigation regions can be put down to a range of reasons:

- Economic factors in the irrigation areas have been generally more favourable and more straightforward to quantify (or the investment that enables it to be done has been made?)

- Hydrogeological conditions are more often suitable and consistent.

- Engineered infrastructure is part of the irrigation landscape.

2.2 The Victorian dryland experience

Engineering solutions to salinity management have a long history in northern Victoria. From the first shallow groundwater pumps in the Shepparton Irrigation region in the early 1970's to the salt interception schemes along the Murray River near Mildura and the Barr Creek pumping and diversion system near Kerang, engineering solutions have been demonstrated and proven to be effective in managing salinity problems. However, these instances have historically been limited to irrigation regions, where large contiguous areas of salinised soils or high watertables have impacted upon often high value agricultural productivity or assets.

In the Victorian dryland, sporadic attempts have been made to strategically install groundwater extraction systems upslope from discharge sites in order to reduce groundwater discharge in dryland areas. Table 1 catalogues a number of examples. Much of the interest in engineering solutions has occurred in the fractured rock aquifers of the Goulburn Broken dryland region. Recent investigations have also occurred along the granite colluvial slopes of the western Victorian uplands. Some activity has also historically occurred in south west Victoria to alleviate high recharge associated with waterlogged landscapes. Some key conclusions that can be drawn from this work are that:

- Many of the trials (particularly the early ones) have focussed on the groundwater extraction potential rather than the issues or opportunities associated with disposal. Apart from the Donald Seaweed Project, none of the trials holistically assessed the technical and economic potential of an IMT solution

- Only one trial, the Donald Seaweed Project, is explicitly linked to an innovative solution, but its focus is more on the productive use of a saline water resource. Trials along the Colbinabbin Range and Dookie Hills were typically linked to vineyard irrigation supply with only a vague possibility of beneficial impact on associated saline land.

- Though justified on the basis of salinity control, few of the Victorian case studies have incorporated any monitoring to assess the impacts on salinity discharge per se’ (as opposed to monitoring of groundwater levels surrounding the extraction site). Notwithstanding, these impacts can be difficult to quantify given other causal factors such as climate.

Of the current activity in Victoria, Goulburn-Murray Water is investigating the options for engineering solutions to reduce salt load contributions from key sub-catchments of the Goulburn Broken dryland region (Nolan ITU 2005). This comprises a hydrogeologically based technical assessment of sub-catchments as well as consideration of:

- Landholder views of technically feasible solutions;

- Capital and operating costs of the engineering option;

- Additional site-specific investigations on the geology, hydrology and water quality; and

- An improved understanding of the potential agronomic options that might work in tandem with the engineering option

The work to date demonstrates the diverse and detailed level of information required to form a business case to justify an engineering related solution in a dryland setting. This further emphasises the many challenges associated with employing such solutions.

Nolan ITU (2005) have been attempting this task at the sub-catchment level in the Goulburn - Broken Catchment. Even in circumstances where a ‘reasonable’ amount of hydrogeological knowledge and data were available, they still expressed the need to have more highly resolved (local scale) information before the technical merits of an engineering option could be quantified for stream salt load management justification.

2.3 Governance, Regulation and Legislation

2.3.1 Governance

It is considered likely that any potential IMT based solution would need to gain the support of a range of agencies and authorities if it was to become a practical reality. In a large operation, this might be approval in a legislative sense. For smaller operations it might have to occur within the guidelines of local planning schemes or to meet new irrigation development guidelines and approvals. It would be desirable that legislative, regulatory or planning requirements be considered in the feasibility study stage of a proposed option so as to add some confidence and certainty to the outcome.

Governance of disposal and drainage issues from IMT developments in Victoria would be expected to be undertaken in the integrated catchment management (ICM) context. Planning and implementation of ICM in Victoria occurs on a regional catchment level with overall policy direction and investment provided at the state level (DSE 2005). The primary tool of integrated catchment management arrangements are the Regional Catchment Strategies (RCSs). These set out a vision for the management of a region’s land and water resources, establish long-term objectives and identify priorities for action and investment amongst the various natural resource management issues. Under the broad policy umbrella provided by the RCSs, detailed action plans for priority land and water resource management issues are developed.

The plans underpinning an RCS address a range of Government policies including Victoria’s Salinity Management Framework, Murray Darling Basin Salinity Management Strategy, New Irrigation Development Guidelines, Memorandum of Understanding for Irrigation Drainage Management and Water Quality, Nutrient Management Strategy for Victorian Inland Waters, SEPP Waters of Victoria and others as required. Land or water action plans must include a detailed analysis of the key issue(s), develop detailed objectives and targets, investigate management options and consider environmental, social and economic benefits and costs of options (DSE 2005).

In the irrigation regions, engineering options have generally developed under the auspice of the relevant regional rural water authority. Typically with State, Federal and/or Murray - Darling Basin funding, engineering options for salinity control have been either large scale (Murray River Interception works), or as part of a well supported, regionally integrated land and water management plan. A good example are the surface water management schemes and groundwater pumping program in the Shepparton Irrigation Region’s Land and Water Salinity Management Plan. Some municipal based urban salinity mitigation systems have also been developed by councils and state agencies (eg Wagga in NSW and the wheat-belt town of Merredin W.A.).

In NDSP (2001) examples of engineering based options for dryland areas have generally developed as trial sites organised by the relevant state agency. Some surface drainage options have been developed and implemented by landholders, primarily in Western Australia. The approval of relevant agencies is not specifically covered in the examples given, but it is very likely that some level of

15

agency support and regulatory approval was required, especially if off site impacts were expected. In NDSP (2004) a note of caution about surface drainage schemes is given:

‘Problems encountered include the highly variable impact of deep drains, managing saline and acidic groundwater flows and soil bio-geochemical changes that can occur where drainage lowers watertables. There is also debate about the need for regional drains and about legal and institutional processes associated with such drainage programs. Requirements for major expenditure on infrastructure further constrain adoption’.

In terms of institutional support for engineering based options, any scheme that has off-site impact or that requires public financial support will require some level of institutional approval if it is to proceed to implementation.

2.3.2 Regulatory or legislative triggers

Innovative management technologies for dryland salinity control will clearly interact with legislation or regulatory guidelines when:

- Site earthworks are undertaken to prepare an engineering solution - potentially invokes the Victorian Planning and Environment Act (1987)

- Groundwater is to be extracted - licensing requirements as specified under the Water Act (1989)

- Extracted groundwater is to be dealt with, as in:

- Disposal to the environment or contamination triggers the Environment Protection Act (1970).

- Disturbance of native vegetation invokes the Victorian Planning and Environment Act (1987).

-	New irrigation developments invoke rural water authorities’ guidelines.

- Additional salt load transport implicates End of Valley Targets and therefore dryland catchments in meeting their MDBC agreements.

Development of small scale salinity management schemes are unlikely to meet much in the way of legislative or regulatory hurdles. Large scale schemes (eg. Pyramid Creek groundwater interception scheme near Kerang currently being implemented) do require significant regulatory approval. The observation of lesser impediment to smaller schemes is drawn from experience with the implementation of salinity and drainage related planning controls in the Shepparton Irrigation Region

A question that arises is the style of development that ought or ought not be controlled. In many respects, no one scheme will be quite like another, so each would need to be assessed individually. For example, a groundwater re-use scheme irrigating salt tolerant trees in an up-slope recharge area to primarily manage a salt affected site should perhaps be treated differently to a normal commercial irrigation development. Strict application of controls and guidelines can stifle innovation and knowledge generation, so some flexibility would be desirable on the part of regulatory authorities.

The Water Act (1989) and Environment Protection Act (1970) would be central to the consideration of IMT developments.

Water Act 1989

A summary of the Victorian Water Act 1989 is taken from the Environment Victoria website:

The Victorian Water Act provides the framework for allocating surface water and groundwater throughout Victoria. It is arguably the most powerful piece of legislation in use in Victoria impacting on rivers, streams and groundwater. The Water Act details the Crown’s entitlements to water and private entitlements to water from all rivers, streams and groundwater systems in Victoria. The Act allows authorities and individuals to use water either through bulk entitlements, providing authorities with bulk amounts of water, or licences or sales water, which allow people to access water for mainly commercial or irrigation purposes. Some licences enable withdrawals of water directly from streams, others from groundwater. Domestic and stock water access is also addressed in this Act. The Water (Irrigation Farm Dams) Act 2002 amended the Water Act 1989 to also cover irrigation and commercial dams on or off waterways. These dams are now required to either be licenced or registered under the Water Act. The environment's access to water in this Act is addressed once all

16

existing water uses are met. The environment is then allocated the "left over" amounts of water to provide its flow.

Environment Protection Act 1970

Invoking State Environment Protection Policy (Waters of Victoria) 2003 and associated Schedules. A summary of the Environment Protection Act 1989 is taken from the Environment Victoria website:

The Environment Protection Act enables the EPA to improve air, land and water environments by managing waters, controlling noise and controlling pollution. It is focussed on protecting the environment through reducing human impact on our air, land and water. Sitting under the Environment Protection Act are State Environment Protection Policies (SEPPs). SEPPs are important as they provide goals and blueprints to protect the environment for the community both now and into the future. The SEPP Waters of Victoria details the uses and values of our water environments (beneficial uses), sets measurements and indicators so we know how well they are being protected (environmental quality objectives) and outlines what needs to be done to protect them (attainment program).

2.3.3 Local planning requirements

Apart from strict legislative and regulatory requirements specified above, local planning processes will need to consider a range of key issues and questions including:

- Will the proposed development require planning scheme approval, usually due to land use change or development impacts off site?

- Will there be any possible impact (real or perceived) on adjoining landowners or further a field that could require or make use of the planning process to gain approval and acceptance?

The permitting of activity on a local basis can be gauged through understanding the requirements of the Victoria Planning Provisions (VPP 2004), administered through the Planning and Environment Act (1987)

Planning and Environment Act (1987)

The Victorian Planning Provisions (VPP) is best considered as a state-wide reference document or template from which planning schemes are sourced and constructed in relation to the Planning and Environment Act 1997. It is a statutory device to ensure that consistent provisions for various matters are maintained across Victoria and that the construction and layout of planning schemes is always the same. The VPP offers a comprehensive set of standard planning provisions and provides a standard format for all Victorian planning schemes. The provisions invoke planning activities that relate to areas of both local and state government responsibility.

Possible scenarios where planning approval might be required include an evaporation basin system, significant water storage, aquaculture pond or other impoundment, diversion drain, tile drain and other works that may need to be assessed through a local planning permit. The requirements to be dealt with by the local planning system will only be known once the design of works is known and assessment of offsite impacts can be gauged. Well designed and innovative schemes developed in association with local communities would likely face little difficulty in meeting the necessary VPP approvals.

Developments of an agricultural nature in the Rural Zones will not generally require any planning approvals. However a large control scheme involving a number of landholders may seek planning approval where the process can help facilitate the development. Possible scenarios arising from this project would need to be tested to decide whether any planning issues might apply. Vegetation clearance controls may apply depending upon scheme design and intent. However, such issues are best dealt with during the early design stage to avoid creating any need for clearance. A useful framework for dealing with potential VPP issues is through the irrigation development guideline approach (see above).

New Irrigation Development Guidelines

New irrigation development regulations apply where surface water transfers to green-field sites are
proposed. New developments reliant on groundwater supply are also being increasingly required to

17

meet these requirements, for instance, in the mid-reaches of the Loddon Valley Deep Lead where guidelines developed by G-MW apply. Not all rural water authorities have irrigation development guidelines currently in place (Tom Maher1 pers. comm.). However, in 2004/05 funding under the White Paper, Securing our Water future Together, the development of Statewide New Irrigation Development Guidelines (DSE 2005) is supported.

As an example, Goulburn-Murray Water facilitate and support the development of sustainable irrigated agriculture through implementation of new irrigation development guidelines (G-MW 2002). These articulate that all parties will do their utmost to ensure that irrigation developments involving the transfer of water entitlement, activation of a previously unused water entitlement or access to groundwater produce minimal on-site and off-site impacts.

Goulburn-Murray Water will not approve the transfer of water entitlements to new developments until the statutory requirements, approved policy and approved standards of the authority and other stakeholder organisations have been met. The various authorities and their roles in this process are outlined in Table 2. These would be relevant to other regions of Victoria. Other authorities possibly to be engaged would be electricity and gas, communications, urban and other rural water businesses.

As far as Goulburn-Murray Water is concerned, applications for transfer of water entitlement must also pass the following checks prior to approval being granted:

- Supply feasibility (including resource assessment on unregulated waterways)

- Channel capacity

- Salinity and drainage criteria

2.3.4 Multi-state salt disposal agreements

End of valley targets for salt loads are either in process, or are now agreed between Victorian CMAs and the Murray - Darling Basin Commission. This process is described in the Murray-Darling Basin Salinity Management Strategy (MDBC 2001). Because each catchment contributes an amount of salt to the combined lower Murray salt load and river salinity levels, agreements are being put in place to prevent rises and to encourage actions that will reduce loads over time. South of the Victorian Great Divide, that same imperative for salt load reduction does not exist, though river health strategies may recognise salinity impacts and the need to limit them (e.g. targets for the Hopkins River in the Glenelg - Hopkins CMA).

In terms of justification for an engineering based option, prevention of salt load impact downstream is theoretically a major consideration. Especially in the Murray-Darling Basin, salt load impact downstream has a recognised cost that must be borne by the community in the area of salt origin. Loads mobilised after 1988 must be paid for to offset costs of interception works on the Lower Murray. If an upper catchment area can install works that prevent a significant salt load, then the economic incentives for the works can be quite positive. In the Murray-Darling Basin there are two major salt reduction schemes (taken from MDBC website) currently under development that need to be financially accounted for:

- Work is currently progressing on the construction of the Waikerie Phase 2a project. This project is estimated to cost $3.4 million and is conservatively expected to intercept (on average) an additional 23 tonnes of salt every day.

- A $10 million project to intercept groundwater entering the Pyramid Creek in Northern Victoria is currently under development. It is anticipated that this scheme will stop about 30,000 tonnes of salt entering the Murray River each year. Negotiations with a commercial salt harvester are proceeding to improve the financial viability of this project for the Basin partner Governments.

As the amounts of salt released by dryland salinity discharge and downstream salt export are generally poorly defined and seasonally controlled, accounting for salt loads as credits would require significant work to quantify and establish. If an engineering based system proposed for a site could prevent a known amount of salt being mobilised down the catchment, the EC credits system of economic justification (as applies to the Murray River schemes) could be a significant factor in supporting such development. However, no scheme has yet been devised in the dryland to test this possibility.

1 Tom Maher (Irrigation development officer, DPI-CAS) May 27 2005.

18

The closest that such a scheme has been to development is at a location on the Goulburn River between Nagambie and Murchison. Here, groundwater with a salt load of about 5000 tonnes per year discharges along a section of the river. Investigations into the feasibility of interception and capture in a re-use scheme concluded that the benefit to cost ratio of diverting the salt load was not favourable, despite the presence of EC credits (S. Feiss, G-MW pers com. and SKM 2004 )

2.3.5 Summary

Regulatory approvals are not considered likely to be a factor that would stifle development of a dryland salinity engineering option. The key proviso is that any proposals would need to be designed from the outset to either minimise cause for regulatory approval or would obtain required clearances at the relevant stages of planning.

As each scheme and site would be unique, the range of normal approvals processes would need to be addressed for any specific aspects for which approvals are required. The key issues would be where off-site impacts are likely or where licensing is required under legislation.

However, given the un-common nature of dryland IMT developments, it would be hoped that that the
merits or otherwise of any IMT proposal that tackles salinity or water quality problems be given some

19

leeway. The potential planning issues that do arise need to be addressed proportionally to the scale of the proposal. Another key criteria that should be assessed during the planning process is the 'net protection of natural resources'. It is likely that any trade-offs arising from an IMT will have some flexibility such that they can be successfully managed.

3. Project Reference Group and Stakeholder Input 3.1 Stakeholder reference group

At the commencement of this project, contact was made with CMAs and regional departmental natural resource management staff (including EPA and Rural Water Authorities). The intention was to form a reference group to oversee progress in the project.

A project inception meeting was arranged and held in October 2003 to inform potential stakeholders of the nature of the study and seek their input.

At this meeting, the following were discussed:

- Background to the project

- How catchment management strategies deal with dryland salinity management

- An overview of engineering techniques

- Saline agronomy and aquaculture options

- Legislative and regulation issues

- Data available for the study.

The main outcome from the meeting was that direct discussions with CMAs were desirable to obtain more detail about how dryland salinity sites are considered with respect to their management and priority within catchment strategies. Other salient points raised to be considered in the study included:

- the processes of engaging 'entrepreneurs' in developing innovative engineering solutions

- ways of managing risks, timeframes and expectations of an IMT solution

3.2 CMA discussions

During November and December 2003, direct discussions were held with five CMAs. One of the main outcomes from these discussions was the recognition that dryland salinity problem areas in each catchment are all quite different in terms of extent, severity, cause and potential treatments. In one respect, this highlighted the potential value of a systematic method for deciding where an engineering option was most favourable.

CMAs use different means of assessment to determine dryland salinity priorities. In most CMAs, the approach has been via a systematic appraisal of sub-catchments (eg. North Central and Goulburn Broken CMA regions), with varying degrees of relation to asset risk. In contrast, the Corangamite CMA has based salinity investment prioritisation on non-catchment defined boundaries drawn around a rasterised assessment of asset risk to salinity. Salinity prioritisation has generally been part of the process of preparing Second Generation Salinity Management Plans required for the accreditation of Regional Catchment Strategies (RCSs) under the National Action Plan for Salinity and Water Quality.

Given the substantial work already completed by CMAs in determining their salinity priority zones, a general principle adopted by this project was to use these as input into the IMT case study selection process. Some discussion of the prioritisation methodologies used in the NAP funded CMA regions and the IMT implications of these is provided below.

3.2.1 North Central CMA

The first GIS data assisted attempt to prioritise salinity investment in Victoria occurred in the North Central CMA (CLPR 2001). The intention behind this was to identify priority areas with the focus on initiating several targeted salinity “implementation” projects under the Natural Heritage Trust (NHT) program.

The priority setting approach, known as ICSRP (Integrated catchment salinity risk and prioritisation) had three major elements:

21

( A GIS-based decision support tool to identify and rank priority sub-catchments using a number of physically based datasets to define salinity hazard.

- An expert based feasibility assessment to determine whether a priority sub-catchment was suitable for a farming systems based implementation or research project.

- A multi-criteria analysis process to assign final priorities of sub-catchments lying within the high risk category.

Recently a more advanced prioritisation tool, ASSALT (as in ASS-assets, SALT-salinity), was developed and prototyped in the North Central CMA region (Clifton and Heislers 2004). ASSALT is based on a more explicit process of spatially referencing salinity hazard and assets to identify risk.

Sub-catchment priorities emergent from CLPR (2001) were the basis of the salinity investment targeted approach adopted in the 2nd generation dryland salinity management plan for the region. Ten targeted sub-catchments have been identified for investment (DPI 2003 - see scanned image, Figure A1, Appendix 2). Individually these reflect:

- An asset base worthy of protection from salinity,

- A groundwater flow system capable of responding to a change in landuse, and

- A perceived capacity of the community to be able to modify their farming systems to achieve more favourable land use change.

Knowing CMAs have already invested significant time into selecting salinity priority sites, it was considered opportune to use these sites as a test bed for development of a site selection methodology.

3.2.2 Corangamite CMA

The prioritisation of salinity investment within the Corangamite CMA region recently occurred through the selection of 13 interim target areas as part of the development of the Corangamite Salinity Action Plan 2003 (Dahlhaus 2003). These areas were delineated for further investigation and development of salinity management strategies. Selection of these was largely underpinned by a rasterised asset-risk assessment process known as GSHARP (Heislers and Brewin 2003). GSHARP comprises the following components:

- The intersection of spatially explicit salinity hazard and asset datasets to generate a rasterised surface of asset risk. Salinity hazard layers included salinity discharge, groundwater depth, groundwater salinity, stream salinity and groundwater flow systems.

- Attention was paid to matching the asset classes with the appropriate salinity hazard product.

- The construction of individual asset risk layers (based on defined asset classes), and, only if required, a summation of these based on expert derived weightings.

Salinity risk to infrastructure and utilities was observed to be clustered in the Moriac area, north of Winchelsea, in an arc from the north-east to south-east of Colac, adjacent the northern and eastern perimeters of Lake Corangamite, Lough Calvert, Derrinallum-Lismore and north and west of Mt Mercer (Heislers and Brewin 2004, see Figure A2 in Appendix 2 - Salinity Hazard rating).

Field verification of the highlighted asset risk zones from the GSHARP output occurred before selection of the interim target areas. The boundaries of these areas were delineated on the broad zone of asset risk rather than interpretation of a physical management boundary such as a surface sub-catchment.

Identified specific regional issues relating to salinity and water quality in the Corangamite CMA encompasses a range of groundwater flow system types in three main landscape systems (northern uplands, basalt plains and southern (Otways) uplands). Urban infrastructure is known to be at risk in several towns including Camperdown, Colac and Derrinallum. Water supplies are thought to be at risk from upland gravel caps containing significant salt stores in the Moorabool target area and increasing salinities are being observed in the Lal Lal reservoir. A different problem with acid sulphate drainage is being observed in the upper Barwon River.

In the Pittong area, possible interception of fresh water upslope of discharge areas has been considered. Unstable soils and aluminium toxicity issues also need to be addressed there. In the Lismore - Derrinallum areas, landholders generally occupy larger farms and interest in managing salinity is likely to be better received there than in areas with smaller holdings closer to Geelong.

22

Groundwater extraction from the basalt aquifer has been previously considered as a way of intercepting saline groundwater that flows from Lake Murdeduke to the Barwon River (Heislers, pers comm). Surface drainage schemes in poorly drained areas have also been developed by landholders. These drains provide improvements in waterlogging conditions and leaching potential, most probably by reducing recharge over winter. The main concern with such unplanned developments relate to lessons learned in Western Australia, where downstream landholders or water-bodies may be put at risk by water quality decline and salt load impacts.

3.2.3 Glenelg-Hopkins CMA

Heislers and Brewin (2003) undertook a salinity asset risk prioritisation for surface water sub-catchments across the Glenelg Hopkins CMA region. The prioritisation process was an advancement on the ICSRP process previously implemented in the North Central CMA. It had the following key characteristics:

- A salinity risk classification was determined for 143 surface sub-catchments defined across the Glenelg-Hopkins region. Asset risk generalised to sub-catchment level was determined for a range of asset classes.

- Salinity hazard datasets comprised salinity discharge, groundwater depth, stream salinity, groundwater flow systems and previously defined salinity investment rankings.

- The ranking of sub-catchments for salinity investment involved summing classes of the key asset risk categories.

This process determined that the highest risk areas were primarily scattered across the central and northern sectors of the GHCMA region. An arc of maximum sub-catchment salinity asset risk occurs from the east Dundas Tablelands through Hamilton, Glenthompson, Maroona then east to Beaufort. The least overall asset risk is attached to sub-catchments along the Victorian-South Australian border and the coastal fringe. Risk was then categorised according to groundwater flow system responsiveness to generate priority areas for salinity management across the region. (see Figure A3 in Appendix 2).

The Glenelg-Hopkins Salinity Plan (GHCMA 2002) recommends the consideration of engineering options if significant assets are at risk from salinity. Apart from the degradation of agricultural land, salinisation has impacted upon a range of assets across the region. Koonongwootong Reservoir has been decommissioned as a result of water supply salinisation. A number of other infrastructure assets including roads and towns such as Lake Bolac, Ararat and Beaufort are known to be impacted. Numerous wetlands across the region have become salinised due to change in hydrological regimes.

3.2.4 Goulburn-Broken CMA

SKM and CLPR undertook salinity prioritisation studies on the 69 sub-catchments of the GoulburnBroken Catchment dryland in the late 1990s (Cheng, 1999, SKM, 1999). These studies scored and ranked the sub-catchments based on an assessment of the severity of salinity risk. Factors included were land salinisation, stream salinity, watertable depth and trend, groundwater salinity and percentage of land cleared. Data availability and quality was also taken into account.

The analysis indicated that high salinity risk catchments mainly occur in the south-west Goulburn and northern and western plains, with medium rated sub-catchments occurring throughout the central region.

However, subsequent work on salt load generation rates (tonnes per hectare yield) has highlighted that the uplands of the south west Goulburn are a priority focus for dryland salinity management (Goulburn Broken Regional Catchment Strategy). This has led to more detailed assessment of the range of options, including engineering based solutions, suited to reducing salt load generation form this area. In this regard Nolan ITU (2005) has undertaken preliminary assessment of engineering solutions in key sub-catchments of the south west Goulburn in addition to others across the dryland plains. Key sub-catchments being considered include Honeysuckle Creek (Plains and Uplands), Lower Broken Plain, Gardiners Creek, Mollisons Creek, Sheep Pen Creek (Plains and Uplands), Sheepwash Creek and Whiteheads Creek.

An analysis of the economics of groundwater pumping in the Goulburn - Broken dryland (SKM, July 2003) for the CMA and Goulburn-Murray Water concluded that if the salinised land reclaimed as a ratio of the groundwater extracted is greater than 0.35 ha / ML /annum, then grant assistance is justifiable. Up to the time of the study, 24 sites had been tested for pumping potential at a cost of

23

$200,470. Five sites were developed at a cost of $60,788 to irrigate 442 ML of water onto about 160 ha of vines and pasture per year. Grants totalling $121,000 were provided for these developments.

Recommendations from the study concluded that further work should focus on quantifying the benefits to the wider community of groundwater interception, and that a suitable case study area would require stream salinity and groundwater monitoring to assess benefits from such pumping and re-use.

3.2.5 Mallee CMA

The key feature of the Mallee CMA area is that significant engineering works already reduce salinity impact along the irrigated fringe of the Murray River. In this example of engineered salinity control, a series of groundwater pumps along the river intercept saline groundwater discharging from the regional groundwater system. The collected water is sent to evaporative disposal basins remote from the river, thus protecting Murray River water quality for downstream users.

In dryland areas, secondary salinity manifestations are often associated with the low-lying areas between dunes. In some cases, the salinity is localised, and sometimes associated with poor surface drainage. However, the Mallee is also dominated by a large regional groundwater system, that together with its flat topography, land-use change, climatic variation and natural, extensive primary salinity, has produced broad salt affected areas after periods of higher rainfall.

Some towns, roads, reserves and wetlands are recognised as being at risk. The communities of Ouyen and Manangatang have a strong appreciation of the potential for salinity degradation of town assets from salinity, protection of which could be considered necessary by engineering based options. Environmental assets at Hattah Lakes and on the Raak Plains have also been identified at risk, though it is important for the distinction to be drawn between primary saline assets and secondary impacted assets.

Where significant local assets such as town infrastructure or sites of high environmental value are at risk, engineering solutions may be justified. However, the potential for more than very localised engineering based solutions for managing salinity in the dryland parts of the Mallee CMA is low. This conclusion is based on the nature of the groundwater systems and the widespread distribution of salinity impacts.

4. Site Selection Methodology 4.1 Requirements of the method

The intention of the site selection methodology was to provide a rapid assessment tool that could be applied to known salinity impacted areas from several NAP catchments. The method was intended to select the most prospective locations for an engineering based solution that could then be considered for a detailed business case analysis. The primary context of this rapid assessment tool was that:

- The areas to be considered were those already identified by the respective salinity prioritisation activities undertaken in different CMA regions (as discussed in Section 3).

- It provided a first level filter and ranking procedure for priority salinity areas on the basis of - knowledge status

- nature of asset protection

- engineering option technical feasibility and groundwater usage options

- No filter was applied to social or economic aspects at this stage in order to keep the appraisal process as simple as possible. Economic criteria and social aspects would be considered later in the business case development stage. In the rapid appraisal process, economic factors play a part in the reasoning (at a qualitative level). For example, the assets questions do include implicit valuing of the assets at risk.

4.2 Method Development Considerations

This section describes the context within which the site selection method was developed. The major factors can be grouped into:

- prior salinity studies supporting site selection

- groundwater flow system information and

- the need for expert judgement

4.2.1	Initial site selection

Identification of salt affected areas in most catchments has occurred at varying levels of sophistication over recent years. Primarily, this identification process has been based on mapped groundwater discharge and surface water salinity readings that indicate salinity problems are present. These data allow ready identification of sites where treatment or management options are desirable. However, much more information is needed about each site in order to develop a sufficiently detailed understanding of them if it is desired to select sites where an engineering based solution is the necessary option.

Progressively better understanding of sites has developed as Catchment Management Authorities and agencies have developed and implemented catchment wide land and water management plans. Tools and processes have also been developed to prioritise sub-catchments to allow decisions on funding and treatment to be made. In the Goulburn Broken catchment for example, all sub-catchments were ranked in order of salinity severity, the objective being to help guide investment decisions by the CMA and funding bodies (Cheng, SKM, 1999).

It is also recognised now that as salinity is now just one of many themes in catchment management investment plans, treating salt affected areas also requires consideration against other land and water management needs. Prioritisation based on salinity severity alone can therefore be improved if additional benefits of treatment actions, such as enhanced water quality, biodiversity and soil erosion control, can be included in considerations of investment choice.

A number of assessment methods have been evolving as CMAs have sought to prioritise programs under their control. Based on the use of spatial data, such tools as ICSRP have been developed (CLPR 2001). Its main purpose has been to develop an objective, transparent, repeatable and automated process to delineate areas for targeting of government investment in salinity management. Subsequent enhancement of this method produced a newer version called GSHARP (Geospatial salinity hazard and asset risk prediction) that has been used in the Corangamite catchment (Heislers and Brewin, 2004). The evolution in this case has been to improve the ability to include assets at risk.

Further work again in the North Central CMA has focussed on how to incorporate into the priorities ranking the concept of assets at risk from salinity. This approach, called ASSALT (Clifton and Heislers, 2004) operates in three main steps:

- Development of an integrated asset exposure index that reflects the likelihood of a particular asset being exposed to salinity and/or shallow watertables, its vulnerability to that exposure and the relative value of the exposed asset.

- Assessment of where in the landscape that intervention to protect assets from salinity is likely to be effective, and

- Assessment of the priorities for investment, given potentially competing interventions.

In most catchments, work to date has amassed a large but variable amount of data on salinity affected locations. This has been largely to serve planning needs (ie. for Regional Catchment Strategy development). The existing information therefore provides a starting point for this project by identifying the known high risk and asset impacting salinity sites that are most favourable for an engineering based solution.

4.2.2 Use of Groundwater Flow Systems

Prior to each CMA developing Regional Catchment Investment Plans (RCIPs), the National Dryland Salinity Program developed a systematic process of groundwater and dryland salinity mapping. Called the Groundwater Flow Systems Framework (Coram et al 2000, Walker et al 2003), this tool provided the information and methodology for each CMA to greatly improve understanding of salinity

26

processes and occurrence. The maps and summarised technical data for the range of groundwater flow systems within each catchment provide a valuable starting point for considering where an engineering or technical salinity management option might be feasible.

4.2.3 Expert Judgement

In attempting to define the suitability of a site for an IMT solution, use of qualitative data and subjective judgements have proved unavoidable. Across the range of potential factors that need to be taken into consideration, many are not quantitative measures (eg. the value of an environmental asset) or exhibit high variability within the mapped units (eg. groundwater salinity or aquifer characteristics). The conclusion from this was that any system developed would have to rely on expert judgement for many criteria. As a result, a significant amount of subjectivity would arise.

Two strategies were used to reduce subjectivity. The first was to seek agreement from a number of stakeholders and experts familiar with the locations and technical issues to lend weight to the decision made for each parameter. The second was to sum the resulting answers so as to minimise reliance on individual responses.

It also became apparent that the nature of the criteria being considered and the objective of the exercise tended to favour trying to filter sites out by making a 'yes' or 'no' judgement about each criteria. To do this, the overall question 'Are the characteristics of the location favourable, or not favourable to an engineering option?' could be considered as the defining question.

An alternative approach of trying to score each criterion (say from 1 to 10) requires more judgement on the part of the assessor. It may also generate significantly more debate among stakeholders as to why a particular value is chosen and could detract from the overall objective. How the values derived are subsequently summed and what, or if, any weighting factor should be applied to reflect their relative importance would also add further complication.

It was therefore decided by the project team that the site selection process should operate as a filter (or sieve) system using a 'yes' or 'no' response to the selected criteria. The chosen method provides a list of sites that have a differing number of the key characteristics that are either favourable or unfavourable for an engineering option. Those sites with more criteria marked favourably would then be considered the best prospects for more detailed assessment through the stage 2 process (see Figure 1).

4.3 Site Selection Criteria

The following section describes how sites can be compared with respect to their suitability for an engineering based salinity and water quality improvement solution. The key criteria for comparison fall into the following three categories:

- Asset evaluation

- Groundwater collection feasibility

- Groundwater usage options

Figure 2 indicates that assets should be considered first on the basis that an underlying justification for addressing a salinity problem must be found before proceeding further. The groundwater collection feasibility aspects are also a vitally important factor in the feasibility of an engineering option. Considering them second in the sequence is really only a matter of practicality, as both are essential. An engineering based option would be untenable if either of these two aspects were unfavourable.

In contrast, groundwater usage options need to be considered only if it is worthwhile diverting the water to protect assets and if the groundwater conditions can support a practical usage option. There is also considerable flexibility to tailor the re-use options to fit the circumstances that apply at the site. However, it is also possible that at some sites, a viable re-use or disposal option cannot be found, thus preventing development of an IMT solution.

Criteria have been identified under each of these categories, with a description of their importance in determining whether a site has good or poor prospects for an engineering based option. For example, under groundwater collection feasibility, the criteria that determine or influence the overall ability to extract groundwater and cause discharge zone reduction are listed. The assessment of each site then involves assessing the data for each site and concluding whether the conditions are favourable or not favourable. The consideration of the three criteria categories for each site then results in a list of sites where conditions are more favourable than others.

4.3.1 Asset Evaluation

A key premise upon which this study was based is that there are dryland salinity and water quality problem areas where the impact is sufficiently high that significant capital expenditure to limit the impacts in a short timeframe can be justified. An example of this might be where saline discharge has a large impact on a town water supply and significant effort to intercept and effectively use the problem groundwater may be justified in order to protect the water supply.

The range of potential asset classes worthy of protection might be:

- Water Supply - either town supplies in the immediate vicinity or end of valley target obligations.

- Built assets - urban areas, infrastructure in high watertable areas, high value land etc.

- Environmental features - wetlands, reserves, river systems at risk of saline impacts.

- Farm productivity - lost production from affected areas

In considering the potential factors that make an innovative solution necessary to protect assets,
some measure of the economic impacts has to be made. In assessing the relative importance of

28

each potential site, it is necessary to consider the size and significance of the assets and the scale of the impact. In the example of a water supply system, the size of the dependant population centre, the salt load and alternate water supply or treatment costs help give some indication of the significance of the impact. Clifton and Heislers (2004) discussed issues of salinity and asset risk assessment in the development of the ASSALT salinity priority setting process. One measure of this was derived as the product of susceptibility to salinity and the probability of the event occurring.

Ownership is another aspect to consider in assessing assets at risk. This includes determining what proportion of individual or public assets are being impacted on. If treating a salinity problem requires public funding, (that will result in predominantly private benefit), then the public investment has to be carefully targeted to ensure capture of the catchment scale and community wellbeing aspects as well.

The downstream salt load impacts and possible credits received through salt capture are another form of asset that should be taken into account at each site. For sites in Victoria and NSW draining to the Murray River, capture of salt load has a defined value through the Salt Disposal Entitlements scheme. A higher salt load site would have greater justification with respect to impact on downstream assets.

Table 3 lists the main asset classes considered to be important in helping to decide whether an engineering solution is favourable or not.

A more detailed assessment of the economic impacts of salinity problem areas and the justification for investment in a control option would subsequently form part of the detailed business case analysis. For this site selection filter, the process initially only needs to distinguish sites that have significant high value features at risk.

Heislers and Brewin (2003) undertook work for the Glenelg Hopkins CMA and discussed the treatment of assets with respect to salinity prioritisation methods. A key conclusion was that asset valuation is a contentious issue, as assets tend to be accorded different value by different stakeholders. Heislers and Brewin (2003) also decided to avoid detailed comparison of asset values, and only included a partial weighting of asset values (for example a highway compared to an unsealed road). With respect to water resource assets, limited detail of water asset mapping meant that assessing saline site impacts on downstream extractable water supplies was also inherently

29

difficult. It was also highlighted that ‘the prioritisation process could ultimately accept any imposed relative asset value matrix’.

4.3.2 Groundwater Collection Feasibility

McAuley and Brinkley (2003), tabulated engineering options with respect to groundwater flow systems, based on their work carried out for the NDSP (SKM, 2001). The approach was developed on the basis that a groundwater diversion system capable of exerting control over the discharging groundwater could be matched to the geological and hydrogeological conditions of the range of dryland salinity conceptual models generated in the GFS study (Coram et al, 2000). That groundwater can be intercepted in some substantial way is fundamental to the success of any engineering based option.

The range of criteria and sub-criteria used to assess the extraction potential and their rationale is listed in Table 4. These criteria form the basis for development of the questions used in the filter tool. Where insufficient information existed to address the question, the site was assumed to be unsuitable with respect to that criterion.

4.3.3 Usage Options

The ability to productively use any collected groundwater or to safely store the salt load is an important consideration. Key criteria are:

30

( Groundwater salinity – the ability of the site to accept groundwater for irrigation, in terms of the biophysical and farm system, treatment and re-use, blending needs, crop tolerance and soil suitability, desalination treatment.

- Water use economics - Water re-use benefits and costs, farming system economics, water storage or disposal costs.

- Community - Community awareness, willingness to take actions.

- Planning - Regulatory issues, eg. Groundwater licensing, off site impacts

Groundwater salinity seems to be the most important factor influencing usage options at sites. If groundwater is of low salinity, the prospects for safe and acceptable usage being found are significantly higher than for more saline groundwaters.

However, complicating factors could be :

- The volume of groundwater that needs to be pumped to provide control. A low volume of high salinity water may be easier to deal with than a large volume of moderate salinity water.

- Location. Proximity to natural salt lakes could make saline water disposal potentially favourable.

- Chemistry. A high iron content, pH or arsenic content could restrict usage options.

- Improving desalination technology at lower cost could change the options matrix.

- Whether there is sufficient data to make a groundwater usage decision for a site.

- Whether the risks involved with higher salinity usage options can be tolerated.

4.4 Site Filter Tool Developed

The above criteria (in tables 3 to 5) were developed into a series of questions addressing the logic of the site selection process described above and represented in Figure 2. By answering these questions systematically, each site can be favourably or unfavourably assessed for each criterion. By working through the questions for the sites under consideration, the accumulated results begin to differentiate sites in terms of the number of favourable and unfavourable responses given. This then reveals those sites where an engineering based solution is both more feasible and more desirable.

In the development of the filter questions, it became apparent that some questions provide useful
background information about a site, while other questions are more critical because they have a
strong influence on the potential viability of a site. To reflect this, the filter tool site selection process

31

has distinguished critical and non-critical questions, in order to give greater weight to what are considered to be the more significant questions. For these critical questions, an explanation' in the spreadsheet includes a threshold description to assist users to define when a 'yes' or 'no' condition should be entered. Where the question is deemed critical, a brief explanation about the reasoning behind the decision can also be included in the spreadsheet to add additional qualitative support where sites have similar scores.

Overall, if the answer to a filter question is 'yes', then the relevant characteristic of that site is favourable towards a detailed consideration of an engineering based solution.

The spreadsheet filter tool starts with a series of general site information questions that help build a picture of the location. While this step was not envisaged in development of the logic diagram, it was found to be necessary when the filter tool was applied to the NCCMA priority salinity locations. Without basic site information, the process to consider whether it would be suitable or not cannot be commenced. For example, without mapped salinity extent or bore data, it is impossible to address subsequent questions.

The questions under the general site information section, have been included in table 6, below. Questions relating to Assets and Groundwater Extraction are listed in tables 7 and 8 respectively.

Tables 6, 7 and 8 have been implemented in a spreadsheet, with explanations at each step to assist users to respond consistently. The classification of questions into “critical” and “non-critical” provides some guidance on the relative importance of each question. The classification has been based on the project team’s experience and knowledge, using a number of subjective criteria. These included:

- Whether a negative response to the question would preclude an engineering based option;

- Whether the question was merely useful supporting information; and

- The likelihood that the circumstance the question related to would actually occur in practice.

Review by a stakeholder reference group of the decisions made would be a useful step to improve confidence that the ranking of suitable sites is reasonable.

A copy of the 'Site Filter' spreadsheet can be obtained from the Victorian Resources Online website (http://www.dpi.vic.gov.au/dpi/vro/vrosite.nsf/pages/vrohome). Instructions for using the tool are incorporated into the spreadsheet.

4.5 Issues of Scale.

The initial filter tool was developed using the NCCMA priority sites to test the concept (see Section 3.2.1 and Appendix 2, Figure A1). These priority sites are sub-catchments of between 10,000 and 70,000 hectares in size. However, the salt affected land mapped in each sub-catchment is only a few percent of their total area. These mapped salt affected areas contribute significantly to the overall salinity risk status of each sub-catchment.

In considering suitable engineering based options for a sub-catchment, the diffuse nature of dryland salinity discharge and the different scales at which it can be managed are critical issues. Will a single, large scheme be practical? Would a large number of separate, small schemes targeted at each known discharge system be more effective? Is an integrated system of control points at every discharge location possible?

The filter process can help resolve this issue by treating each potential scheme and scale separately. It is plausible that the filter process could be applied to identify most suitable sub-catchments and then reapplied within these to identify the most suitable sites within the most suitable sub-catchments.

In theory at least, the same process could be used again to focus on the next scale down. The main limitation would be the availability of sufficient detailed information within sub-catchments to enable judgements on the filter tool criteria to be made.

5 Catchment Assessments 5.1 North Central CMA

The starting point for identifying potential IMT sites in the North Central catchment was to take previously identified salinity affected areas and develop responses to the filter questions, based on readily available information and an assessment of the groundwater flow systems for each area. Key information on priority NCCMA catchments and the process of selection was obtained from several sources. (Karena 2003, Karena 2004, Clifton and Heislers 2004). Information about specific dryland salinity areas was obtained from readily available knowledge held by the project team in Bendigo.

The filter spreadsheet was applied to ten targeted salinity areas in the NCCMA (see appendix 2, figure A1). Table 9 provides a summary of the filter question responses for the 10 sub-catchments and highlights clear differences between sub-catchments in the number of 'yes' responses to the filter questions.

The three catchments of Bet Bet Creek, Bulabul and Natte Yallock had the highest number of positive responses to critical questions. Looking in detail at this result, it is important to consider which questions were not favourably responded to. Where a no response is given, this deficiency may be more significant at some sites than others.

In the case of Bet Bet Creek, the only critical criterion yielding a negative response was whether there is infrastructure of significance impacted by the salinity occurrence. At a few sites, there are likely to be some roads and possibly some fringe areas of Lexton at risk. However, the assessment at this stage is not compromised by this possibility and a more detailed review would be required to confirm or change the filter results on such aspects.

In the Bulabul catchment, there were no assets of significance identified as threatened by salinity. The other key negative responses were in regard to whether there was likely to be a safe re-use or disposal option and whether groundwater systems were suitably responsive to pumping or drainage. Clearly the scale of implementation would have a major influence on groundwater system response, and while local scale systems could be suitable at specific sites, there is doubt that geological conditions would be consistently favourable at a whole of catchment scale.

For the Natte Yallock catchment, there was no estimate of the annual salt load available, though it is
thought to be high. There was also no significant infrastructure impact identified, nor whether a

37

suitable pumping or drainage groundwater response would be manifest. Without an estimate of salt load leaving the catchment, the potential impact of engineering options on downstream irrigation and on end of valley salt loads is unknown. As with the Bulabul catchment, there is some doubt about the availability of suitable groundwater response to drainage adjacent to saline areas due to the generally unfavourable hydrogeological conditions across the area.

This assessment of the North Central CMA priority salinity catchment has highlighted that even on relatively large, priority salinity sub-catchments about which we know a great deal, there are insufficient suitable data available to make even preliminary assessments of potential engineering options with confidence.

5.2 Corangamite CMA

The starting point for identifying potential IMT sites in Corangamite CMA was to take identified salinity affected areas and develop responses to the filter questions using readily available information and assessment of the groundwater flow systems for each area. Key information was obtained from several reports on salinity prioritisation work for the catchment (Dahlhaus 2003, Dahlhaus et al 2002, Heislers and Brewin 2004, Clark 2004). The ICSRP summed salinity hazard for sub-catchments map (from Heislers and Brewin, 2004) is shown in Appendix 2, figure A2.

Approximate priority areas were identified for the catchment by Dahlhaus (2003) and from discussions with the CMA (Tim Corlett) in the form of approximate circles drawn around priority salinity areas on maps. To describe the key characteristics for these areas for data entry onto the filter spreadsheet the key information needed was:

- the nature of the groundwater system responsible for the salinity problem at each location, and

- the salinity manifested at each site.

This information was available in a range of forms (Dahlhaus et al 2002, Heislers and Brewin 2004, Clark 2004). Populating the filter spreadsheet with responses to the questions required a significant effort to gather and collate sufficient suitable data. The vaguely defined priority areas compounded this difficulty, and as a result, the focus was placed on those parts of the catchment of known saline discharge to the surface. This resulted in two of the original interim salinity management target areas identified by Dahlhaus (2003) not being assessed in the filter spreadsheet because the salinity discharge in these two areas is not shown on the salinity discharge mapping layer.

The results of the application of the filter to priority sites in Corangamite is shown in Table 10.

The three locations with the highest number of positive responses to critical and non-critical
questions were the Lismore, Upper Woady-Pittong, and Moriac locations. Reviewing where each of

38

these three received a negative responses highlights key obstacles to developing an IMT solution in these areas.

In the Lismore location, the failures on critical questions were in relation to there being no salt load data and an end of valley impact that is probably very low. The location has several different, yet interacting groundwater flow systems. The current understanding of the groundwater and salinity processes is presently poor and insufficient to draw conclusions on groundwater control feasibility.

In the Upper Woady-Pittong location, the main failures were in relation to assets at risk. The salt loads released to streams have an unquantified downstream impact, so although the impact on the Barwon River via the diversion scheme from Lake Corangamite may benefit through a reduction in salinity, this has not been quantified. The other critical failure was in groundwater extraction feasibility. In deeply weathered granitic terrain such as the Upper Woady-Pittong location, the presence of suitable pumping aquifers is considered unlikely.

The third ranked location fails on five critical questions, but has a higher proportion of non critical questions favourably returned. As with the Lismore site, there is no salt load data and no significant end of valley impact documented. There are also no known infrastructure or environmental assets at risk. The groundwater - salinity conceptual understanding has also not been strongly defined for this location, where the roles of each GFS and their interaction may be complex.

A conclusion that can be drawn from this filtering exercise in the Corangamite CMA region is that despite using a systematic approach to ensure that all questions were addressed using consistent guidelines, decisions were rarely clear cut.

In addressing the questions relating to assets, the approach taken was to consider whether there are critical assets in the region that could conceivably be protected or restored by an engineering based option. Apart from the difficulty of ascribing value to the range of assets involved and the subjectivity of the risk assessment, the Corangamite CMA region is a naturally high salinity landscape with much uncertainty in distinguishing primary and secondary salinity. Given that assets at risk is a key driver for engineering based options, this makes it difficult to confidently identify locations where works might be needed or justified.

The issue of scale is again very significant. Although a single occurrence of saline discharge could feasibly be treated with an engineering solution at a catchment scale, treating a large number of small and isolated sites could be extremely difficult to implement. As shown by the salinity discharge mapping (as seen in Heislers & Brewin, 2004), there are hundreds of known discharge sites in the region which could potentially need to be assessed and treated individually.

5.3 Glenelg-Hopkins CMA

As with the North Central and Corangamite CMAs, the initial approach in the Glenelg-Hopkins CMA was to identify salinity priority areas. Heislers and Brewin (2003) conducted a salinity prioritisation process in the Glenelg-Hopkins CMA that overlaid susceptible asset classes on salinity discharge mapping to highlight sub-catchments having the greatest need for intervention actions. The resulting priority rating table identified over 60 (of 143) sub-catchments as having the top 2 of six available priority ratings. A copy of this priority ranking for the catchment is shown in Appendix 2.

In attempting to apply the IMT filter approach in the Glenelg-Hopkins CMA, the available data were not sufficient to enable assessment of even the 28 highest ranked sub-catchments at the sub-catchment scale. Assessment in the Glenelg-Hopkins CMA region was feasible only at levels of greater spatial aggregation. A different approach was therefore trialled, based on groundwater flow system (GFS) units.

This is a different approach to that taken in the North Central and Corangamite CMA areas, where the focus was on locations. Working through the data available in Dahlhaus et al (2002a), it was possible to make judgements on the questions addressed in the filter spreadsheet and derive a ranking table for the 13 GFS types selected. The results are presented in Table 11.

39

The most favourable GFS types were the Volcanic Plains Basalt and West Dundas Tablelands. For the Volcanic Plains Basalt, the two critical questions unfavourably answered were with respect to an estimate of salt load and whether the site had a significant end of valley impact. Given the extensive area of this GFS type, this is not unexpected.

The West Dundas Tablelands also appear favourable under this assessment. Key critical question failures included estimates of salt load and the significance of impacts on infrastructure.

Using the GFS categories in the filter spreadsheet was a valuable exercise for exploring the suitability and flexibility of the developed concepts and method. The overall results are reasonable from a hydrogeological point of view. However, it highlights some limitations of the process. For example, the assets at risk section was developed for use with specific locations and their probable downstream impact. For extensive areas such as the Volcanic Plains Basalt groundwater flow system, the question cannot be adequately answered.

This is once again reflects issues associated with scale. For example, assessment of a specific sub-catchment where the majority of salinity occurs within this priority GFS type may enable identification of specific downstream impacts on assets. At this scale, it is quite conceivable that there could be a number of known salinity problem sites within a region that are all underlain by that GFS. The filter spreadsheet could be used to help decide which location has the best prospects for investigation and development of a solution.

Overall, it proved difficult to meaningfully answer the filter questions at the GFS scale. On a hydrogeological basis at this scale, it made sense that some GFS types would be more amenable to groundwater extraction than others. However, the more spatially specific questions relating to assets and measured salt loads could not be handled adequately by the filter process at this scale. The filter method would have more value if used to separate out significant salinity occurrences within a GFS type, provided sufficient suitable data exist for the assessment. On this basis, appraisal of the West Dundas Tablelands, looking in more detail at known and relatively well-studied salinity occurrences, could help identify feasible engineering based options.

40

5.4 Selecting 3 sites for more detailed appraisal.

An objective of this project was that it would identify three sites that would have clear opportunity for adoption of engineering solutions that could then be progressed to the development of business cases for implementation. At the commencement of this study, this objective seemed reasonable. However, having worked carefully through the logic of the issues and developed a site selection process, the sheer complexity of the task has become apparent.

The Bet Bet Creek catchment in the North Central CMA, the Lismore area in the Corangamite CMA and the Volcanic Plains Basalt and West Dundas Tablelands GFS in the Glenelg-Hopkins CMA scored highest in each CMA, using the filter process developed. However, the project was not able to identify specific sites, development proposals, nor local support at specific locations to warrant further investment in the development of business cases. In this respect, the project has failed to meet its original objective.

Nevertheless, the project has made a contribution to our knowledge of this topic. Foremost is a clearer understanding of the probability of viable engineering based solutions for dryland salinity in Victoria. Scenarios where an IMT solution may be favourable are provided in the conclusions section of this report.

7 Conclusions

The concept of applying IMT based solutions to dryland salinity problems holds significant attraction for communities and natural resource managers. This is because of the desire to effect a more rapid reduction in salinity related losses than land use change or agronomy based programs can achieve. The success of engineering solutions in irrigation regions also provides further optimism that these options can be applied in dryland areas.

However, SKM (2001) and the assessment of Victorian examples presented here (see Table 1.) indicate that there are few, if any unqualified successes for engineering solutions in dryland areas. Most of the engineering solutions of significant scale lie in irrigation areas where groundwater extraction is generally more favourable, the economic gains are more obvious and engineered infrastructure is already a common part of the operating environment.

Many of the documented dryland case studies are taken from the extensive salinised landscapes of the Western Australian wheat belt. Even there, significant uncertainty remains amongst the farming and scientific communities in regard to the economic and environmental viability of adopting engineering solutions (Pannell 2001).

This lack of clear evidence for the successful application of engineering solutions in dryland areas suggests that whilst their application is not technically impossible, there are significant issues to be addressed.

This project planned to test whether innovative engineering based solutions were feasible in the Victorian context. The first step was to develop a systematic approach for identifying and ranking sites most suited to IMT solutions. A systematic process to assess and compare a set of key factors for known salinity problem areas has been developed. However, while the process developed seems sound, the outcomes have not been as clear as initially hoped for. The reasons for this conclusion are explained below.

7.1 The inherent complexity of dryland IMT solutions

The complexity involved in the consideration of IMT solutions in dryland salinity impacted areas makes building a sound 'business case' for their development a significant challenge. The main uncertainties include:

- The practicalities of groundwater extraction and whether there is sufficient hydrogeological understanding of a site. Though a technical solution may be feasible, the ultimate constraint may be the very high cost of investigating a site, designing a workable solution, implementing it and then operating and maintaining it for a long period of time.

- Suitable disposal or reuse options. In most instances, this will have to occur on-site, given the need to prevent downstream salt load or in-stream water quality impacts. Once again the limitation may not be a technical one, but rather one of economic efficiency.

- Uncertainty about future salinity, which is the result of ongoing dynamic processes. . The current dry climatic phase we have been experiencing has lowered watertables throughout the state and reduced salinity risk and occurrence. The uncertainty that climate change may make salinity risk diminish in the future makes significant dryland salinity investment decisions more difficult. Under both scenarios of changed climatic conditions and widespread agronomic changes impacting on recharge and discharge zones, the need for an engineering option to bring forward a solution in a reasonable time is now less certain.

- Inadequate suitable data at the spatial resolutions required for site assessment. Although it was initially envisaged that a systematic, objective process for selecting the most favourable sites could be developed, it has been unavoidable in practice that a very large degree of subjectivity has dominated the process. This has been inevitable given the dependence on judgements being made about poorly defined and hidden natural systems. The high costs of obtaining hydrogeological data at a suitable resolution for decision making is a common constraint. Removing subjectivity in the site selection process would require very significant investment in more detailed data acquisition across large areas.

.

42

7.2 The importance of high value assets

Sound reasons for an IMT solution are more likely to occur if there is a local, well-defined public asset requiring protection. Rather than focussing on the poorly defined threat of dryland salinity (in all its forms), protection of a recognised asset can provide a focus to enable better targeted effort. The advantages of the asset protection focus and justification include:

- An economic risk profile can be generated for an asset that can help define the starting point for how much money might be justifiably spent developing an engineering solution.

- A well defined asset presents a realistic and attainable target for an engineering solution and for defining its performance criteria.

Pannell (2001) has argued that investment in salinity mitigation would be most efficient if strategically targeted at the protection of specific assets and further suggested the importance of developing improved methods for making more productive use of saline land and water, given that disposal downstream would probably be limited in many dryland landscapes.

7.3 The Role of Scale

Ultimately, any technical option needs to place works on the ground in specific locations. However the scale of dryland salinity and the widely dispersed nature of discharge sites very quickly renders assessment of treatment options at individual sites infeasible. Sufficient data at the scales required for assessment are not available in most cases. This is compounded by the range of scales at which an engineering option might need to be implemented, from localised intervention at small sites to very large, whole of catchment works.

7.4 Favourable Scenarios

The project has been successful in clarifying the circumstances where an engineering based solution is more likely to be viable. Successful engineering solutions must satisfy the following criteria:

- Protect a well defined asset of high value that is under direct and unequivocal threat from salinity processes or water quality impacts. In these situations the downstream benefits of reducing saline base flow in streams can provide strong justification for public investment.

- Use engineering systems that intercept water effectively and efficiently.

- Be able to productively and sustainably use the intercepted water.

- At the farm scale, involve simple, small scale salinity problems where a basic collector system (such as tile drains, mole drains, surface interception drain) and pump with an on-site re-use system can be developed to manage the water within the property boundaries. These solutions can have greater benefit where landholders can integrate them with other beneficial catchment works (for example biodiversity improvement and shelter belt establishment) to achieve multiple outcomes.

8 Recommendations

The following recommendations arise from the project:

- This study has highlighted the very low probability that widespread adoption of engineering based solutions for dryland salinity will be justifiable in Victoria.

- At the farm scale the most likely circumstance where a system could be feasible is that of a small site with simple and favourable hydrogeology. Such a site would have to be amenable to an efficient collection system and an agronomic system that can sustainably contain salt or nutrient on site. Implementation of such systems should aim to achieve multiple outcomes such as biodiversity enhancement.

- The only circumstance where an engineering based solution has potential is where a highly valued asset is at substantial direct risk of salinity damage that cannot be more efficiently resolved by other means.

- The existence of potentially viable sites for implementation of engineering options for dryland salinity and water quality management is not precluded by the inability of this project to identify them, which has largely been the result of inadequate suitable and extensive data sets.

- That Stage 2 of this study as originally proposed not proceed.

References

ASCM (1993) Lurg Upper: Groundwater survey and recommendations. Report by Australian Salinity and Catchment Management.

Cheng X (1999) Goulburn-Broken Dryland catchment prioritisation: upland sub-catchments. Centre for Land Protection Research Technical Report no. 58, Department of Natural Resources and Environment, Victoria

Cheng X (2004) Assessment of the impact of groundwater pumping at Everton Upper. Centre for Land Protection Research Technical Report no. 39, Department of Primary Industries, Victoria

Clarke, R.M. (2004) Victorian Salinity Monitoring: Reassessment of six reference discharge
monitoring sites in the Corangamite Region. CLPR Research report No. 43.

Clifton C and Heislers D (2004) ASSALT: An asset-based salinity priority setting process. Report by SKM and DPI-PIRVic for the North Central CMA.

CLPR (2001) The development and application of an integrated catchment salinity risk and prioritisation process (ICSRP). Discussion document for the North Central CMA Region.

Coram JE, Dyson PR, Houlder PA and Evans WR (2000) An evaluation Framework for Dryland salinity. Australian Groundwater Flow systems contributing to dryland salinity. Report to National Land and Water Resources Audit, Bureau of Rural Science.

Coram JE, ed. (1998) National Classification of Catchments for land and river salinity control. RIRDC Publication no. 98/78, Rural Industries Research and Development Corporation.

Dahlhaus P (2003) Process for the initial selection of target areas for salinity management. Background report for the development of the Corangamite Salinity Action Plan. Report produced by Dahlhaus Environmental Geology Pty Ltd.

Dahlhaus P, Heislers D and Dyson P (2002b) Groundwater Flow Systems. Report no. CCMA 02/02 for the Corangamite Catchment Management Authority.

Dahlhaus P, Heislers D and Dyson P (2002a) Groundwater Flow Systems. Report no. GHCMA 02/02 for the Glenelg Hopkins Catchment Management Authority.

DPI (2003) The North Central Dryland Salinity Targeted Approach. Brochure produced by DPI for the community on the North Central CMA region.

DSE (2005) Sustainable Irrigated Agriculture and Land Management Initiative: 2004/05 funding guidelines.

DSE (2004) Securing our Water Future Together, Victorian Government White Paper, Department of Sustainability and Environment

GHCMA (2002) Salinity Action Plan (draft) – protecting our future naturally. Background report for the Glenelg Hopkins CMA RCS.

45

Heislers D and Brewin D (2004) Corangamite salinity hazard and asset risk assessment. Background report for the Glenelg Hopkins Salinity Plan. DPI-CLPR Research Report no. 6 for the CCMA.

Heislers D and Brewin D (2003) Salinity prioritisation in the Glenelg Hopkins Region. Background report for the Glenelg Hopkins Salinity Plan. DPI-CLPR Research Report no. 23. for the GHCMA.

Hekmeijer P and Hocking M (200 1) Feasibility of groundwater pumping from granite slopes. Produced for the Wimmera CMA. CLPR Technical Report no. 71.

Hocking et al. (2004) The feasibility of groundwater extraction from granitic terrain as a means of salinity mitigation – upper Hopkins region. Internal technical report for the Glenelg Hopkins CMA.

Karena, J, (2003) The North Central Dryland Salinity Targeted Approach. (brochure) Department of Primary Industries, Victoria for the North central CMA. (ISBN 1 74106 706 5)

Karena, J., (2004) Success of the North Central Dryland Targeted Salinity Program. (brochure) Department Of Primary Industries, Victoria for the North Central CMA. (ISBN 1 74146 270 3)

McAuley C and Brinkley A (2003) Engineering Options in a Catchment Framework. Sinclair Knight Merz conference paper presented at PURSL 2003. Yepoon, Qld Conference proceedings.

MDBC (2001) Basin salinity management strategy 2001-2015. Published by the Murray Darling Basin Ministerial Council

NDSP 2004 (or Powell, J) Dryland Salinity: On-farm Decisions and Catchment Outcomes. A guide for Leading producers and Advisors. Land and Water Australia.

Nolan ITU (2005) Targeting Engineering Options in the Goulburn-Broken Dryland for
Salinity Control: Stage 1 and 2 Report. Produced for Goulburn Murray Water.

Pannell D (2001) Public funding for environmental issues: where to now? Sustainability and Economics in Agriculture (SEA) Working Paper 01/12

SKM (2004) Salt Inflows to the Goulburn River between Goulburn Weir and Murchison
STAGE 3 INVESTIGATION 2003/2004". Report for Goulburn-Murray Water

SKM (2003) R562: Dryland Upland Groundwater Pumping Development – Economic
Analysis of Upland Groundwater Pumping. Report for Goulburn-Murray Water

SKM (2002) R562-Upland FEDS: Dryland Upland Groundwater Pumping Development Progress Report. Report for Goulburn-Murray Water.

SKM (2001 b) Assessment of the efficacy of engineering options for the management of dryland salinity. Research report produced for the National Dryland Salinity Program, Land and Water Australia.

SKM (2001a) R562-Tatong Dryland Salinity Study: Site-Data Validation and Report on findings. Report for Goulburn-Murray Water.

SKM (1999) Goulburn-Broken Dryland catchment prioritisation: plains sub-catchments. Study carried out for Goulburn - Murray Water and the Goulburn-Broken Salinity Management Plan Working Group.

46

SKM (1997) Glenelg sub-surface drainage investigation. Report for the Department of Natural Resources and Environment.

Victorian Water Act (1989) Act no. 80/1989 incorporating amendments as at July 2004

VPP (2004) Victorian Planning Provisions. Available from http://www.dse.vic.gov.au/planningschemes/VPPs/

Walker G, Gilfedder M, Evans R, Dyson P and Stauffacher M (2003) Groundwater Flow Systems Framework: Essential tools for planning salinity management. Summary report (based upon Coram et al, 2000.) for the Murray Darling Basin Commission.

Appendix 1. Project Proposal

Appendix 2 - Catchment Salinity Priority Maps

Figure A1 - North- Central CMA Figure A2 - Corangamite CMA Figure A3 - Glenelg - Hopkins CMA

# Text boxes

vi

7

8

9

11

13

14

20

24

25

27

32

33

34

35

36

41

43

44

47

48

49

60

61