Goulburn Broken Dryland Regional Development Project

Land Use and Climatic Suitability Criteria

June 2000

Centre for Land Protection Research

PO Box 3100

Bendigo Delivery Centre, 3554

Ph: (03) 5430 4444

Fax: (03) 5430 3304

Email: clpr@nre.vic.gov.au

Copyright ( Department of Natural Resources & Environment 2000

This publication may be of assistance to you but the State of Victoria and its employees do not guarantee that the publication is without flaw of any kind or is wholly appropriate for your particular purposes and therefore disclaims all liability for any error, loss or other consequence which may arise from you relying on any information in this publication.

Agriculture Victoria

Centre for Land Protection Research

Cnr Midland Hwy & Taylor St,

Epsom 3551

(Postal:  PO Box 3100

Bendigo Delivery Centre, 3554)

Ph: (03) 5430 4444

Fax: (03) 5430 3304

Email: clpr@nre.vic.gov.au

Table of Contents

Biophysical Suitability Analysis And The MLF Method		2

Components, Factors and Critical Values				2

Wine Grapes

Late Maturing								4

Early Maturing								6

Vegetables

Warm Climate								8

Cool Climate								10

Wildflowers										12

Meat Goats									12

Firewood and/or Pulp

Sugar Gum									13

Eurabbie									14

Mugga									15

Broombush									16

Southern Blue Gum							17

Red Ironbark								18

References										19

Goulburn Broken Dryland Regional Development

Biophysical Suitability Analysis Using The MLF Method.

The MLF (Most Limiting Factor) Method as used in this study identifies biophysical factors that are critical for production or the protection of the environment.  The biophysical factors are assessed in relation to the level at which they become limiting to plant growth or protection of the environment.  The approach ultimately assigns a suitability rating based upon the most limiting factor.

The MLF methodology for the identification of horticultural biophysical suitability is based on the method for determining land capability developed by the United States Department of Agriculture.  The land capability approach has been extensively used in Victoria over the last 30 years to facilitate land use planning at the local government level.

The MLF is a “rules combination” method. This approach deals with the interdependence of landscape factors (or factor interdependence)  (Hopkins, 1977, pp. 394 - 395).  The combination of landscape attributes (soil, vegetation, slope, drainage, etc.) that occur in the landscape unit is considered, and different units are given the same suitability rating if they have similar landscape attribute levels.  The values derived for units are based upon expert knowledge of the key factors (attributes) and the level at which they become critical.  All factors are considered to have equal weight with respect to their impact upon growth or the environment.  The simplicity of the approach allows the technique to be applied via a GIS platform or manually.

Components, Factors and Critical Values.

The biophysical suitability for horticultural production has been determined based upon three ecosystem components:

- Climate	Is the crop in question suited to the rainfall, temperature and frost susceptibility within the land?

- Landscape	Will growing the crop result in unacceptable water erosion on the land?  Will the natural landscape features of the land result in drainage problems, or impede machinery operations?

- Soil	Are the inherent soil conditions suitable for growing the crop/pasture?

The climate, land and soil components have each various elements or factors; and for each factor, critical values are identified and used to rate the suitability for different types of horticulture.  The factors are rated for their limitation to plant growth, or potential for environmental degradation, according to a three class rating system (Table1).  The most limiting factor determines the class.

Table 1   Class definitions used for the Most Limiting Factor biophysical suitability methodology.

| Class | Description | Definition |
| --- | --- | --- |
| 1 | High | High probability of the climate, land and soil being suitable for commercial horticulture production with respect to plant production and protection of the natural resource base. |
| 2 | Moderate | Moderate probability of the climate, land and soil being suitable for commercial horticulture production with respect to plant production and protection of the natural resource base. |
| 3 | Low | Low probability of the climate, land and soil being suitable for commercial horticulture production with respect to plant production and protection of the natural resource base. |

The rationale for assigning critical values to each of the factors is based on: (a) plant production, and (b) protection of the natural resource base, with the aim of identifying economically and environmentally sustainable land use and management options.

# Wine Grapes

Cabernet sauvignon is used as the benchmark variety for late maturing wine grape suitability.

Factors and critical values used for determining the biophysical suitability for late maturing wine grapes:

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Mean cumulative days of frost during spring (Sept, Oct and Nov) | < 10 | 10 - 15 | > 15 |
| Mean monthly rainfall during flowering (Nov and Dec) | < 75mm in Nov and < 75 mm in Dec | < 75mm in Nov or < 75 mm in Dec | > 75mm in Nov and > 75 mm in Dec |
| Mean monthly rainfall during ripening (Mar and Apr) | < 75mm in Mar and < 75 mm in April | < 75mm in Mar or < 75 mm in April | > 75mm in Mar and > 75 mm in April |
| Branas Index | < 5000 | 5000 - 6000 | > 6000 |
| Heat Degree Days | >1500 | 1350 - 1500 | <1350 |
| Landscape |  |  |  |
| Slope (%) | 0.5 - 15 | < 0.5 and 15 - 25 | > 25 |
| Soil |  |  |  |
| Surface pH | 5.5 – 8.0 | 4.5 – 5.5 and 8.0 – 8.5 | < 4.5 and > 8.5 |
| Sub-surface pH | 6.0 – 8.0 | 5.0 – 6.0 and 8.0 – 9 | < 5.0 and > 9 |
| Surface texture | Loam, Sandy Loam, Silty Loam, Sandy Clay Loam, Clayey Loam, Loamy Sand Clay Loam Sandy, Silty Clay Loam, Light Clay, Clayey Sand Light Medium Clay | Sand, Medium Clay, Medium Heavy Clay | Heavy Clay |
| Sub-surface texture | Loam, Sandy Loam, Silty Loam, Sandy Clay Loam, Clayey Loam, Loamy Sand Clay Loam Sandy, Silty Clay Loam, Light Clay, Clayey Sand Light Medium Clay, Medium Clay, Medium Heavy Clay | Heavy Clay Sand |  |
| Surface soil sodicity | No (ESP < 6%), Slight (ESP 6 -15%) | Yes (ESP > 15%) |  |
| Sub-surface soil sodicity | No (ESP < 6%), Slight (ESP 6 -15%) | Yes (ESP > 15%) |  |
| Useable soil depth (cm) | 30 - 60 | > 60, 10 - 30 | < 10 |
| Surface soil drainage | Moderately well drained (4), Well drained (5) | Rapidly drained (6), Imperfectly drained (3) | Poorly drained (2), Very poorly drained (1) |
| Sub-surface drainage | Moderately well drained (4), Well drained (5) | Rapidly drained (6), Imperfectly drained (3) | Poorly drained (2), Very poorly drained (1) |

# Wine Grapes

Pinot-Noir, Merlot, Chardonnay and Sauvignon Blanc are used as the benchmark varieties for early maturing wine grape suitability.

Factors and critical values used for determining the biophysical suitability for early maturing wine grapes:

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Mean cumulative days of frost during spring (Sept, Oct and Nov) | <10 | 10 - 15 | >15 |
| Mean monthly rainfall during flowering (Nov and Dec) | < 75mm in Nov and < 75 mm in Dec | < 75mm in Nov or < 75 mm in Dec | > 75mm in Nov and > 75 mm in Dec |
| Mean monthly rainfall during ripening (Mar and Apr) | < 75mm in Mar and < 75 mm in April | < 75mm in Mar or < 75 mm in April | > 75mm in Mar and > 75 mm in April |
| Branas Index | < 6500 | 6500 - 7000 | > 7000 |
| Heat Degree Days | 1150 - 1600 | 1600 - 1900 | < 1900 and > 1150 |
| Landscape |  |  |  |
| Slope (%) | 0.5 - 15 | < 0.5 and 15 - 25 | > 25 |
| Soil |  |  |  |
| Surface pH | 5.5 – 8.0 | 4.5 – 5.5 and 8.0 – 8.5 | < 4.5 and > 8.5 |
| Sub-surface pH | 6.0 – 8.0 | 5.0 – 6.0 and 8.0 – 9 | < 5.0 and > 9 |
| Surface texture | Loam, Sandy Loam, Silty Loam, Sandy Clay Loam, Clayey Loam, Loamy Sand Clay Loam Sandy, Silty Clay Loam, Light Clay, Clayey Sand Light Medium Clay | Sand, Medium Clay, Medium Heavy Clay | Heavy Clay |
| Sub-surface texture | Loam, Sandy Loam, Silty Loam, Sandy Clay Loam, Clayey Loam, Loamy Sand Clay Loam Sandy, Silty Clay Loam, Light Clay, Clayey Sand Light Medium Clay, Medium Clay, Medium Heavy Clay | Heavy Clay Sand |  |
| Surface soil sodicity | No (ESP < 6%), Slight (ESP 6 -15%) | Yes (ESP > 15%) |  |
| Sub-surface soil sodicity | No (ESP < 6%), Slight (ESP 6 -15%) | Yes (ESP > 15%) |  |
| Useable soil depth (cm) | 30 - 60 | > 60, 10 - 30 | < 10 |
| Surface soil drainage | Moderately well drained (4), Well drained (5) | Rapidly drained (6), Imperfectly drained (3) | Poorly drained (2), Very poorly drained (1) |
| Sub-surface drainage | Moderately well drained (4), Well drained (5) | Rapidly drained (6), Imperfectly drained (3) | Poorly drained (2), Very poorly drained (1) |

Vegetables

Assuming a rotation of broccoli, sweet corn, capsicums and leeks (warm climate).

Factors and critical values used for determining the biophysical suitability for vegetables (warm climate):

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Average monthly maximum temperature (oC)(Nov to Mar inclusive) | > 25 | 20 - 25 | < 20 |
| Frost free days (Oct to Mar inclusive) | > 120 |  | < 120 |
| Landscape |  |  |  |
| Slope (%) | < 6 | 6 – 10 | > 10 |
| Soil |  |  |  |
| Surface pH | > 6.0 | 5.0 – 6.0 | < 5.0 |
| Sub-surface pH | > 6.0 | 5.0 – 6.0 | < 5.0 |
| Surface texture | Loam, Sandy Loam, Silty Loam, Sandy Clay Loam, Loamy Sand, Fine Sandy Loam, Loam Fine Sandy, Clay Loam | Clay Loam Sandy, Silty Clay Loam, Light Clay, Sand, Clayey Sand, Medium Clay, Heavy Clay |  |
| Sub-surface texture | Loam, Sandy Loam, Silt Loam, Sandy Clay Loam, Clay Loam, Loamy Sand, Sandy Clay, Fine Sandy Loam, Light Clay, Loam Fine Sandy, Silty Clay Loam, Silty Clay | Sand, Heavy Clay, Heavy Medium Clay |  |
| Surface soil sodicity | No (ESP < 6%) | Slight (ESP 6 -15%) | Yes (ESP > 15%) |
| Sub-surface soil sodicity | No (ESP < 6%), Slight (ESP 6 -15%) | Yes (ESP > 15%) |  |
| Useable soil depth (cm) | > 50 | 45 – 50 | < 45 |
| Surface/Sub-surface drainage | Moderately well drained (4), Well drained (5), Rapidly drained (6) | Imperfectly drained (3) | Poorly drained (2), Very poorly drained (1) |
| Coarse fragments (%) | < 15 | 15 - 30 | > 30 |

Vegetables

Assuming a rotation of Crucifiers (broccoli, cauliflower, chinese cabbage or bok choy), lettuce and leeks (cool climate).

Factors and critical values used for determining the biophysical suitability for vegetables (cool climate):

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Average monthly maximum temperature (oC)(Dec to Mar inclusive) | > 25 | 20 - 25 | < 20 |
| Average monthly maximum temperature (oC) (Nov) | > 21 | 18 - 21 | < 18 |
| Frost free days (Oct to Mar inclusive) | > 120 |  | < 120 |
| Landscape |  |  |  |
| Slope (%) | < 6 | 6 – 10 | > 10 |
| Soil |  |  |  |
| Surface pH | => 5.5 | 5.3 – 5.5 | < 5.3 |
| Sub-surface pH | > 5.4 | 5.0 – 5.4 | < 5.0 |
| Surface texture | Loam, Sandy Loam, Silt Loam, Sandy Clay Loam, Loamy Sand, Fine Sandy Loam, Loam Fine Sandy | Clay Loam Sandy, Silty Clay Loam, Light Clay, Sand, Clayey Sand, Clay Loam, Medium Clay, Heavy Clay |  |
| Sub-surface texture | Loam, Sandy Loam, Silt Loam, Sandy Clay Loam, Loamy Sand, Fine Sandy Clay Loam, Fine Sandy Loam, Loam Fine Sandy | Clay Loam Sandy, Silty Clay Loam, Loamy Clay, Sand, Clayey Sand, Clay Loam, Heavy Clay, Light Clay, Medium Clay, Silty Clay |  |
| Surface soil sodicity | No (ESP < 6%) | Slight (ESP 6 -15%) | Yes (ESP >15%) |
| Sub-surface soil sodicity | No (ESP < 6%), Slight (ESP 6 -15%) | Yes (ESP >15%) |  |
| Useable soil depth (cm) | > 50 | 45 – 50 | < 45 |
| Surface/Sub-surface drainage | Moderately well drained (4), Well drained (5), Rapidly drained (6) | Imperfectly drained (3) | Poorly drained (2), Very poorly drained (1) |
| Coarse fragments (%) | < 15 | 15 - 30 | > 30 |

Wildflowers

Factors and critical values used for determining the biophysical suitability for wildflowers:

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Mean cumulative days of frost during spring (Sept, Oct and Nov) | < 10 | 10 - 15 | > 15 |
| Maximum temperature of hottest month (Feb) | < 40 | > 40 |  |
| Soil |  |  |  |
| Surface pH | 5 - 7 | 4 - 5 and 7 - 8.5 | < 4 and > 8.5 |
| Salinity (discharge site) | absent | present |  |
| Useable soil depth (cm) | > 50 | < 50 |  |
| Soil drainage (surface & sub-surface) | Moderately well drained (4), Well drained (5), Rapidly drained (6) | Imperfectly drained (3) | Poorly drained (2), Very poorly drained (1) |

Meat goats

Factors and critical values used for determining the biophysical suitability for meat goats (boer):

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Average annual rainfall | > 600 | < 600 |  |
| Soil |  |  |  |
| Salinity (discharge site) | absent | present |  |
| Soil drainage (surface & sub-surface) | Moderately well drained (4), Well drained (5), Imperfectly drained (3), Rapidly drained (6) | Poorly drained (2) | Very poorly drained (1) |

# Sugar Gum (Eucalyptus cladocalyx)

Product: Wood			Use: Firewood

Factors and critical values used for determining the biophysical suitability for sugar gum:

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Average number of frosts (Sept. - Dec.) | < 15 | 15 - 20 | > 20 |
| Average annual rainfall (mm) | 600 - 1000 | 450 - 600 | < 450 |
| Average maximum temperature of hottest month (oC) | 23 - 33 | 33 - 35 | < 23 and > 35 |
| Average minimum temperature of coldest month (oC) | > 3 | 2 - 3 | < 2 |
| Landscape |  |  |  |
| Slope (%) | < 32 | 32 - 58 | > 58 |
| Site drainage | Moderately well drained (4), Well drained (5), Imperfectly drained (3) | Rapidly drained (6) | Poorly drained (2), Very poorly drained (1) |
| Soil |  |  |  |
| Surface texture | Loam, silty loam, sandy clay loam, clayey loam, loamy sand clay, silty clay loam, light clay, clayey sand, light medium clay, medium clay, heavy clay |  | Fine sandy loam, Loam fine sandy, loamy sand, sand |
| Useable soil depth (cm) | > 45 | 35 - 45 | < 35 |

Eurabbie (Eucalyptus globulus ssp. Bicostata)

Product: Wood			Use: Firewood

Factors and critical values used for determining the biophysical suitability for eurabbie:

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Average annual number of frosts | < 25 | 25 - 70 | > 70 |
| Average annual rainfall (mm) | > 700 | 600 - 700 | < 600 |
| Average maximum temperature of hottest month (oC) | < 29 | 29 - 30 | > 30 |
| Average minimum temperature of coldest month (oC) | 0 - 3 | 3 - 4 | < 0 and > 5 |
| Landscape |  |  |  |
| Slope (%) | < 32 | 32 - 58 | > 58 |
| Elevation (ASL) | < 800 | 800 - 1050 | > 1050 |
| Soil |  |  |  |
| Surface texture | Loam, silty loam, sandy clay loam, clayey loam, clay loam sandy, silty clay loam, light clay, light medium clay, medium clay | Heavy clay, Loamy sand, sandy loam | Sand, clayey sand |
| Useable soil depth (cm) | > 45 | 35 - 45 | < 35 |

Mugga (Eucalyptus sideroxylon s.s.)

Product: Wood			Use: Firewood

Factors and critical values used for determining the biophysical suitability for mugga:

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Average annual rainfall (mm) | > 700 | 550 - 700 | < 550 |
| Average maximum temperature of hottest month (oC) | 29 - 31 | 27 - 29 and 31 - 33 | < 27 and > 33 |
| Average minimum temperature of coldest month (oC) | 2 - 3 | 0 - 2 and 3 - 4 | < 0 and > 4 |
| Landscape |  |  |  |
| Slope (%) | < 32 | 32 - 58 | > 58 |
| Soil |  |  |  |
| Surface texture | Sand, loamy sand, sandy loam, fine sandy loam, light sandy clay loam, loam, loam fine sandy, silty loam, sandy clay loam, clay loam, silty clay loam, fine sandy clay, sandy clay, silty clay, light clay |  | Heavy clay, medium clay |

Broombush (Melaleuca uncinata)

Product: Foliage & branches	Use: Brush fencing

Factors and critical values used for determining the biophysical suitability for broombush:

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Average annual rainfall (mm) | 450 - 550 | 550 - 600 | < 450 and > 600 |
| Average maximum temperature of hottest month (oC) | > 29 | 27 - 29 | < 27 |
| Average minimum temperature of coldest month (oC) | > 3 | 2 - 3 | < 2 |
| Landscape |  |  |  |
| Slope (%) | < 34 |  | > 34 |
| Soil |  |  |  |
| Surface texture | Sand, loamy sand, sandy loam, fine sandy loam, light sandy clay loam, loam, loam fine sandy, silty loam, sandy clay loam, clay loam, silty clay loam, fine sandy clay, sandy clay |  | Light clay, medium clay, heavy clay, silty loam, silty clay |
| Sub-surface texture | Light sandy clay loam, loam, loam fine sandy, clay loam, silty clay loam, fine sandy clay, sandy clay, light clay, medium clay, heavy clay, silty clay |  | Sandy clay loam, fine sandy loam, silty loam, loam fine sandy, sand, sandy loam, sand, loamy sand |

Southern Blue Gum (Eucalyptus globulus ssp. globulus)

Product: Wood			Use: Firewood &/or pulp

Factors and critical values used for determining the biophysical suitability for southern blue gum:

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Average annual number of frosts | < 25 | 25 - 40 | > 40 |
| Average annual rainfall (mm) | > 800 | 700 - 800 | < 700 |
| Average maximum temperature of hottest month (oC) | 23 - 27 | 27 - 29 | < 23 and > 29 |
| Average minimum temperature of coldest month (oC) | > 3 | 2 - 3 | < 2 |
| Landscape |  |  |  |
| Elevation (m) ASL | 0 - 450 | 450 - 600 | > 600 |
| Slope (%) | < 32 | 32 - 38 | > 58 |
| Soil |  |  |  |
| Useable soil depth (cm) | > 100 | 80 - 100 | < 80 |

Red Ironbark (Eucalyptus tricarpa)

Product: Wood			Use: Firewood &/or pulp

Factors and critical values used for determining the biophysical suitability for red ironbark:

|  | Critical value |
| --- | --- |
| Factor | High probability of being suitable | Moderate probability of being suitable | Low probability of being suitable |
| Climate |  |  |  |
| Average annual rainfall (mm) | 500 - 600 | 700 - 1000 and 450 - 500 | > 1000 and < 450 |
| Average maximum temperature of hottest month (oC) | 27 - 30 | 25 - 27 | < 25 |
| Average minimum temperature of coldest month (oC) | 2.5 - 3.5 | 2 - 2.5 | < 2 |
| Landscape |  |  |  |
| Slope (%) | < 32 | 32 - 38 | > 58 |
| Soil |  |  |  |
| Surface texture | Sand, loamy sand, clayey sand, sandy loam, fine sandy loam, light sandy clay loam, loam, loam fine sandy, silt loam, sandy clay, light clay, medium clay, heavy clay | Sandy clay loam, clay loam, silty clay loam, fine sandy clay loam |  |

REFERENCES

Hopkins, L., (1977), “Methods for generating land suitability maps: a comparative evaluation”, Journal of the American Institute of Planners, Vol. 43, pp. 386 – 400.

# Text boxes

Land and Climatic Suitability Criteria

Goulburn Broken Dryland Regional Development Projects

June 2000