## A Report on residential Land capability and agricultural land suitability in the SHIRE of CAmpaspe

March 1998

M. Bluml, N. Baxter, J. Williamson, M.Morris

Technical Report No. 35

ISBN No.	0 7306 9231 0

ISSN No.	1038 216X

Prepared by

| Centre for Land Protection Research | Institute for Sustainable Irrigated Agriculture |
| --- | --- |

Further Information This report has been prepared to assist with land use planning in the Shire of Campaspe. The information in the report has been derived from existing land resource information and limited field examination and verification. The scale of mapping adopted has necessitated some generalisations from the information collated. While the land capability/suitability classes indicate the likely performance of land for residential land use or an agricultural enterprise, site specific information will still be required for on-site planning. The precision of mapped boundaries is affected by the scale of the map. Any enlargement of the map will distort information and is unlikely to improve its accuracy. The complete set of maps which accompany this report can be viewed at the Shire of Campaspe Municipal Office. This publication may be of assistance to you, but the State of Victoria and its employees do not guarantee that the publication is without flaw of any kind or is wholly appropriate for your particular purposes and therefore disclaims all liability for any error, loss or other consequence which may arise from you relying on any information in this publication.

CONTENTS

SUMMARY	vi

USER GUIDE 	viii

1.	INTRODUCTION	1

1.1	Purpose of study	2

1.2	Project objectives	2

2.	LAND CAPABILITY/SUITABILITY ASSESSMENT	3

2.1	Methodology and constraints	3

2.2	Land capability/suitability assessment tables	3

3.	DETAILED LAND SYSTEM DESCRIPTIONS AND CAPABILITY CLASSES	19

3.1	Active floodplains - Murray and Campaspe Rivers	19

3.2	Corop wetland complex	24

3.3	Prior stream alluvial plain	30

3.4	Treeless alluvial plain 	36

3.5	Knowsley low undulating sedimentary hills	42

3.6	Rushworth low undulating sedimentary hills	47

3.7	Myola East low undulating sedimentary hills	52

3.8	Mount Camel rolling low volcanic hills	58

5.	ACKNOWLEDGEMENTS	63

6.	REFERENCES	63

APPENDIX A.   Guidelines and referral documents	64

APPENDIX B.   Responses to overcome identified limitations	65

APPENDIX C.   Specific notes to accompany land capability/suitability assessment tables	67

APPENDIX D.   Physical and chemical laboratory results	75

APPENDIX E.   Land capability/suitability class tables	79

GLOSSARY	97

LIST OF FIGURES

Figure 1.1 Location of the Shire of Campaspe	1

LIST OF TABLES

i.i	Summary of land capability/suitability classes	vii

2.1	Land suitability classes for agriculture	5

2.2	Land capability classes for broadacre effluent disposal (feedlots), septic tanks and secondary roads	6

2.3	Land suitability assessment for irrigated rice production	7

2.4	Land suitability assessment for irrigated cropping (e.g. cereals, oilseed, legumes)	8

2.5	Land suitability assessment for irrigated perennial pasture (dairying)	9

2.6	Land suitability assessment for irrigated perennial horticulture (stone fruits, pome fruits)	10

2.7	Land suitability assessment for irrigated tomato production	11

2.8	Land suitability assessment for irrigated farm forestry > 40 ha (Bluegum, Eucalyptus globulus)	12

2.9	Land suitability assessment for dryland olive production	13

2.10	Land suitability assessment for dryland viticulture	14

2.11	Land capability assessment for broadacre effluent disposal (ground absorption) for feedlots	15

2.12	Land capability assessment (ground absorption) for septic tanks	16

2.13	Land capability assessment for secondary (gravel) roads	17

2.14	Land capability assessment for low density residential and rural living development	18

Summary

Land use and land management practices will continue to change.  If the community is concerned about the long-term sustainability of various forms of  land use, then the physical limitations imposed by the land, the various processes of land degradation, and the possibility of off-site impacts, must be recognised.  Once the physical limitations for a particular land use are identified, steps can be taken to match that particular land use with a suitable land type(s), develop and implement relevant management practices (ie. Victorian Code of Cattle Feedlots), and overcome or minimise the potential long-term  impacts of land and water degradation.

The Shire of Campapse through it’s Integrated Strategy Plan (1996), has recognised the need for a land capability/suitability study to assist in achieving sustainable agricultural and rural residential development throughout the Shire.  In addition, this report will be listed as a reference document in the new planning scheme for the Shire of Campaspe.  The report will therefore become a statutory part of the planning scheme.

For the purpose of this report, land capability and land suitability assessments are concerned with the physical constraints imposed by the landform and soils.  No social or economic criteria were considered in this report.  Land capability assessments have five capability classes and refer to land  utilised for rural residental/urban development, while land suitability assessments have three suitability classes and refer to land utilised for agriculture.

Land capability/suitability classes have been determined for each land system and land component within the Shire of Campaspe (Please refer to Table i.i below, in conjunction with the Shire of Campapse Land Systems Map).  For greater planning detail, please refer to Section Three of this report.

TABLE  i.i  Summary of land capability/suitability classes

| Land system | Land suitability class | Land capability class |
| --- | --- | --- |
| Name and component | Rice | Irrigated cropping | Irrigated perennialpasture | Irrigated perennial horticulture | Irrigated tomatoes | Irrigated farm forestry | Dryland olives | Dryland viticulture | Broadacre effluent (Feedlots) | Septic tanks | Secondary roads | Low density | Rural living |
| Murray and Campaspe active floodplains | 1 | iii | ii | ii | iii | ii | ii | iii | iii | v | v | iv | v | v |
|  | 2 | ii | iii | iii | iii | ii | iii | iii | iii | v | v | v | v | v |
|  | 3 | i | iii | iii | iii | ii | iii | iii | iii | v | v | v | v | v |
|  | 4 | iii | ii | ii | iii | i | ii | iii | iii | v | v | v | v | v |
| Corop wetland complex | 1 | ii | iii | iii | iii | ii | iii | iii | iii | iv | iv | iv | v | iv |
|  | 2 | ii | iii | iii | iii | ii | iii | iii | iii | iv | iv | iv | v | iv |
|  | 3 | iii | iii | iii | i | i | iii | i | i | ii | ii | ii | ii | ii |
|  | 4 | ii | ii | ii | iii | ii | iii | iii | iii | iv | iv | iv | v | iv |
| Prior streams alluvial plain | 1 | i | iii | iii | iii | i | iii | iii | iii | v | v | iv | v | iv |
|  | 2 | i | iii | iii | iii | ii | iii | iii | iii | v | v | iv | v | iv |
|  | 3 | ii | ii | ii | ii | ii | ii | ii | ii | iv | iv | iv | iv | iv |
|  | 4 | iii | i | ii | ii | i | ii | ii | ii | iv | iv | iii | iv | iii |
|  | 5 | iii | i | i | i | i | i | i | i | ii | ii | iii | iii | iii |
| Treeless alluvial plain | 1 | i | iii | iii | iii | ii | iii | iii | iii | v | v | iv | v | iv |
|  | 2 | i | iii | iii | iii | ii | iii | iii | iii | v | v | iv | v | iv |
|  | 3 | ii | iii | iii | iii | ii | iii | iii | iii | v | v | iv | v | iv |
|  | 4 | iii | ii | ii | ii | ii | ii | ii | ii | ii | ii | iv | v | iv |
|  | 5 | iii | ii | i | ii | ii | ii | ii | ii | ii | ii | iv | iv | iv |
| Knowsley low sedimentary hills | 1 | iii | iii | iii | iii | iii | iii | iii | iii | iv | iv | iii | iv | iii |
|  | 2 | iii | iii | iii | ii | ii | iii | ii | ii | ii | ii | iii | iii | iii |
|  | 3 | iii | iii | ii | iii | ii | iii | iii | iii | ii | ii | iv | iv | iv |
| Rushworth low sedimentary hills | 1 | iii | iii | iii | iii | iii | iii | iii | iii | v | v | iii | v | iv |
|  | 2 | iii | iii | iii | ii | ii | iii | ii | ii | iii | iii | iii | iii | iii |
|  | 3 | iii | iii | ii | iii | ii | iii | iii | iii | iv | iv | iv | iv | iv |
| Myola east low sedimentary hills | 1 | iii | iii | iii | iii | iii | iii | iii | iii | iv | iv | iv | iv | iv |
|  | 2 | iii | iii | ii | ii | ii | iii | ii | ii | iii | iii | iii | iii | iii |
|  | 3 | iii | iii | ii | iii | ii | iii | iii | iii | iv | iv | iv | iv | iv |
|  | 4 | iii | iii | iii | iii | iii | iii | iii | iii | iii | iii | ii | iii | ii |
| Mt Camel rolling low volcanic hills | 1 | iii | iii | iii | iii | iii | iii | iii | iii | v | v | v | v | v |
|  | 2 | iii | iii | iii | ii | ii | iii | ii | ii | iii | iii | iv | iv | iv |
|  | 3 | iii | ii | ii | iii | ii | ii | iii | iii | iv | iv | iv | iv | iv |

\

### USER GUIDE

Procedure for applying land capability/land suitability information

1.	Introduction

The Shire of Campaspe is situated in northern Victoria adjacent to the Murray River (see Figure 1.1).  The Shire is predominantly rural and supports a wide range of conventional dryland and irrigated agriculture.  In particular, broadacre cropping, mixed farming and grazing in dryland areas, with dairying, broadacre cropping and intensive horticulture in irrigated districts.  More recently, other agricultural enterprises have been established such as piggeries, feedlots and vineyards.

Figure 1.1 Location of the Shire of Campaspe

The Shire of Campaspe has a range of landforms and soils that are capable of sustaining a wide variety of agricultural pursuits. A large opportunity therefore exists for the expansion of existing or emerging agricultural enterprises, which have the potential to provide a major regional development stimulus.

The continued development of existing and new agricultural enterprises is seen as fundamental to the future well being of the Shire.  Therefore, in further developing the agricultural sector, the Shire has acknowledged that it must be sustainable agricultural development.  This has been highlighted in the Shire of Campaspe - Integrated Strategy Plan (1996).  The Objective Statement for agriculture is listed below:

Viable and sustainable agriculture is seen as fundamental to the existing and future well being of the Shire and its residents.  The Shire encourages traditional and emerging agricultural activities and practices that:

- are ecologically sustainable;

- incorporate best management principles;

- introduce diversity and productivity improvements; and

- will assist in the development of value adding enterprises.

Sustainable agricultural development requires that each agricultural enterprise be suited to the particular climate, landform and soil type so that optimum production can be achieved without causing on-site or off-site land and/or water degradation.

A number of local policies were established in the Integrated Strategy Plan to support the sustainable development of agriculture in the Shire.  The implementation of these specific agricultural policies will now occur through the Shire’s new planning scheme.  The planning scheme will incorporate these policies, and have additional overlays and provisions to encourage appropriate land use and management.

A number of actions were recommended in the Integrated Strategy Plan to assist in achieving the Shire’s agricultural objective and policies.  The preparation of a land capability study was one of these actions.  The intent of a land capability study is to provide base information on the nature of the land, and the likely performance of various land types, given a range of land use activities.  This information can underpin many land use and management decisions made by the municipality, both now and in the future.  There is a long list of costs associated with inappropriate land use and management.  Planning schemes developed with access to land capability information have now overcome many of the recurring planning mistakes which led to land and water degradation.  Common benefits obtained through utilisation of the land capability information include:

- Reduced  nutrient movement to surface and ground waters;

- Reduced soil erosion and other forms of land degradation and more insidious loss of environmental quality;

- Reduced costs to the community through unwise investment and prematurely obsolete infrastructure; and

- Minimisation of agricultural lands lost to less productive competing uses.

1.1	Purpose of the Study

This report aims to provide the Shire of Campaspe with a key reference document to support land use planning and management.  In particular the report will enable the following:

- a comprehensive comparison between competing land uses;

- identification of suitable agricultural enterprise/land type combinations;

- identification of areas capable of supporting emerging agricultural enterprises;

- determination of best practice management for preferred land use/land type combinations; and

- determination of the susceptibility to land degradation of various land use/land type combinations.

1.2	Project Objectives

The objectives of the study are listed below.

1.	To map and describe freehold land in the Shire of Campaspe.  The Shire will be mapped at 1:100 000 scale.  This will involve identifying land components (including geology, soil types, topography, climatic zones) and other features relevant to the assessment of the land.

2.	To determine land capability classes for low density residential development based on standardised rating tables for:

- septic tank effluent disposal; and

- secondary (gravel) roads.

3.	To prepare standardised planning responses to overcome or manage the physical limitations identified for the following residential land use activities:

- septic tank effluent disposal; and

- secondary roads.

4.	To determine the land suitability of a selected range of alternative agricultural land uses in dryland and irrigation areas, these include:

- broadacre effluent disposal (feedlots);

- rice;

- irrigated cropping (cereals, oilseeds, legumes);

- irrigated pasture (dairying);

- irrigated horticulture (stone fruits, pome fruits, viticulture, olives);

- irrigated tomatoes;

- irrigated agroforestry;

- dryland olives; and

- dryland viticulture.

.

2    LAND capABILITY/SUITABILITY ASSESSMENT

For the purpose of this report land capability and land suitability assessments are concerned with the physical constraints imposed by the land. The only distinction being that land capability is related to land utilised for residental/urban development, while land suitability is related to land utilised for agriculture. No social of economic criteria have been included in the land capability/suitability assessments.

Land capability/suitability assessment is a rational and systematic method of determining the ability of land to sustain a range of specified uses without causing significant long-term degradation.

The objectives of land capability/suitability assessments are:

i)	to assist land managers and land use planners to identify  areas of land with physical constraints for a range of specified land uses;

ii)	to identify management requirements that will ensure a specified land use can be sustained without causing significant on-site or off-site land and water degradation.

iii)	to promote both productive and sustainable development of rural land and industries.

To achieve these objectives, it is necessary to know the physical characteristics of the land, and understand the effects that a specified land use may have on the land and the water derived from it.

In land capability/suitability assessment, recurring land systems (landform patterns eg. low undulating hills) and components (landform elements eg. crests) are mapped, and the dominant landform, soil and climate characteristics are recorded. This information is then analysed to determine the ability of each land component to sustain a specified land use given standard management practices.

The ratings provided by a land capability/suitability assessment are not intended to restrict development of land, but rather to identify the principal constraints of that land for a specified land use.  It is a matter for the land manager or land use planner to decide if the cost of overcoming the constraints is justified. Where particularly severe physical constraints exist, the planning authority has the option of excluding land from that use, or permitting the use only under strict management conditions.  The placement of conditions on development permits is quite a proper exercise of planning responsibility.

2.1   Methodology and constraints

Due to the scale of mapping adopted for this study (1:100 000) and the inherent variability within some landscapes, it is possible that unrepresentative areas will occur within the land components mapped.  In some cases, these areas may have a capability class exceeding that of the relevant land component.

The climate, landform and soils information presented in this study therefore represent the most common climate, landform and soil conditions identified within each land component.  This information has been collated from both field investigation and a range of technical publications.  These publications are referred to in the general text and Reference section of the report.

The land systems map prepared for this study is based upon the Victorian land systems coverage and soil association mapping held by the Department of Natural Resources and Environment.

Due to mapping restrictions, land components are not represented over the entire land systems map.  Where this has occurred, the capability/suitability class for the most common land component has been used as a default class for the entire land system.

The following procedure has been adopted for this study:

i)	Natural resource information from existing technical publications was compiled.

ii)	The broad land systems and land components were mapped utilising a range of methods including: interpretation from aerial photos, digital elevation models, radiometrics, existing map sources and field verification.

iii)	The land system/land component boundaries were entered into a Geographic Information System where the data was combined with base-map information on roads, contours and streams to produce a final base map of the study area.

iv)	Representative landform and soils information was collated from relevant technical publications for each land component.  The potential for land degradation in each map unit was also determined.

v)	Where gaps in landform and soils information existed, detailed field examination was undertaken.

vi)	Land suitability assessment tables were developed for each agricultural land use specified, while existing land capability assessment tables were used for effluent disposal and secondary roads.

vii)	Land capability/suitability classes were determined for each land component by comparing climatic, landform and soils information against each of the land capability/suitability assessment tables.

viii)	Where physical limitations were identified within land components, a standardised planning response was developed in conjunction with municipal staff to overcome or suitably manage the specified land uses.

2.2   Land capability/suitability assessment tables

The land capability/suitability assessment tables presented in Section 2 contain landform, soil and climatic parameters which strongly influence the ability of the land to sustain a desired land use.  There has been no attempt to rank these parameters in order of importance.

The parameters have been further divided to give three land suitability classes for land uses related to agricultural development (refer to Table 2.1), or five land capability classes related to low density residential development (refer to Table 2.2).

Capability/suitability classes are determined by comparing the parameters set out in the land capability/suitability assessment tables (refer Table 2.3 - 2.14) against the specific landform or soil conditions identified for each land component (refer to Section 3).  The most limiting capability/suitability class identified in each assessment table will determine the overall class for the desired land use activity.

The land capability/suitability assessment tables are only concerned with the physical aspects of the land and soil.  The overall land capability/land suitability class does not include the socio-economic aspects of development.  If the land capability class is v (very poor capability) or the agricultural land suitability class is iii (unsuited), this rating should override the socio-economic considerations.  If the land capability class is i - iv (very good to poor) and the agricultural land suitability class is i - ii (suited to generally suited), any socio-economic considerations outlined in the planning scheme or appropriate code of practice should still be considered.

Table 2.1   Land suitability classes for agriculture.

| CLASS | SUITABILITY | DEFINITION |
| --- | --- | --- |
| i | Suitable | Suited, with no major limitations to production and/or environmental damage given best management practice, and provided the development complies with the appropriate Code of Practice and the Planning Scheme. |
| ii | Generally suitable | Suited, but with some major limitations that increase the risk of production loss and/or environmental damage given best management practice, and provided the development complies with the appropriate Code of Practice and Planning Scheme. Management prescriptions are commonly required to overcome the major production and/or environmental limitations and ensure sustainable land use. |
| iii | Not suitable | Unsuited - due to severe limitations that significantly increase the risk of production loss and/or environmental damage. Best management practice and current technology cannot commonly overcome these limitations. Development should not occur without a detailed site assessment to determine whether the major production and/or environmental limitations can be overcome. |

Table 2.2   Land capability classes for broadacre effluent disposal (feedlots), septic tanks and secondary roads.

| CLASS | CAPABILITY | DEFINITION |
| --- | --- | --- |
| i | Very good | Very high capability for the specified use; standard design and management techniques are satisfactory. |
| ii | Good | High capability for the specified use; standard design and improved management techniques are satisfactory |
| iii | Moderate | Moderate capability for the specified use; moderate land degradation hazard and/or engineering difficulties present; improved design and management techniques are required for development to take place. |
| iv | Poor | Low capability for the specified use, high land degradation hazard and/or considerable engineering difficulties present; extensively modified design and management techniques are required for development to take place. |
| v | Very poor | Long term land degradation hazard and/or severe engineering difficulties present; normally unsatisfactory for development unless specialised design and management techniques exist. These limitations are frequently too expensive to overcome with current technology. |

Table 2.3   Land suitability assessment for irrigated rice production .

| PARAMETERS INFLUENCING | LAND SUITABILITY RATINGS |
| --- | --- |
| RICE PRODUCTION | Class 1 | Class 2 | Class 3 |
| Landscape | Slope (%) (assumes flood irrigation) + | 0 - 0.5 | 0.5 - 1.0 | > 1.0 |
| Soil | Electrical conductivity (dS/m ECe)** | < 3.8 | 3.8 - 8.6 | > 8.6 |
|  | Estimated subsoil permeability | Very slowly permeable | Slowly permeable | Moderately, highly, very highly permeable |
|  | Depth of sodic, heavy - medium clay in the top 3.6 m of the profile (m)*,++ | > 3.0 | - | < 3.0 |

+ Slope classes beyond the scope of the study, further information required

** Saturation extract

* 1997/98 GMW Guidelines for land suitability assessment for rice growing

++ Available information restricted to 1.5 - 2.0 metres, further on-site information is required

Note:	The above table has been developed from regional data to provide a general assessment of land suitability and does not provide sufficient information for the evaluation of specific sites.

Additional site specific factors that would require consideration prior to development may include:

- site size and layout;

- access to services and utilities;

- availability and quality of irrigation water;

- access to surface and/or subsurface drainage;

- water table conditions and groundwater quality;

- soil factors such as pH, organic matter content, nutrient status, sodicity, etc;

Table 2.4   Land suitability assessment for irrigated cropping (e.g. cereals, oilseed, legumes).

| PARAMETERS INFLUENCING | LAND SUITABILITY RATINGS |
| --- | --- |
| IRRIGATED CROPPING PRODUCTION | Class 1 | Class 2 | Class 3 |
| Landscape | Slope (%) (assumes furrow irrigation)*,+ | 0.5 - 0.25 | 0.25 - 0.05 | > 0.5 < 0.05 |
|  | Site drainage | Well drained, moderately well drained, imperfectly drained | Poorly drained | Very poorly, rapidly drained |
| Soil | Depth of topsoil (cm) | >10 | <10 | - |
|  | Depth to hard rock (m) | >1.0 | 1.0 - 0.5 | < 0.5 |
|  | Proportion of stones and boulders (%) | <10 | 10 - 40 | > 40 |
|  | Susceptibility to surface crusting | Low | Moderate, high | - |
|  | Depth to seasonal watertable (m) | > 2.0 | 2.0 - 1.0 | < 1.0 |
|  | Total amount of water available to plants (mm) | > 150 | 150 - 30 | < 30 |
|  | Electrical conductivity (dS/m ECe)** | < 3.8 | 3.8 - 8.6 | > 8.6 |
|  | Estimated subsoil permeability | Highly, moderately, slowly permeable | - | Very slow, very highly permeable |

* From Irrigation and Drainage Practice, p55

+ Slope classes beyond the scope of the study, further information required

** Saturation extract

Note:	The above table has been developed from regional data to provide a general assessment of land suitability and does not provide sufficient information for the evaluation of specific sites.

Additional site specific factors that would require consideration prior to development may include:

- site size and layout;

- access to services and utilities;

- availability and quality of irrigation water;

- access to surface and/or subsurface drainage;

- water table conditions and groundwater quality;

- soil factors such as pH, organic matter content, nutrient status, sodicity, etc;

Table 2.5   Land suitability assessment for irrigated perennial pasture (dairying).

| PARAMETERS INFLUENCING | LAND SUITABILITY RATINGS |
| --- | --- |
| IRRIGATED PASTURE PRODUCTION | Class 1 | Class 2 | Class 3 |
| Landscape | Slope (%) (Assumes checkbank flood irrigation)* | 0.06 - 1.0 | 0.1 - 2.0 | < 0.06 >2.0 |
|  | Site drainage | Well, moderately well, imperfectly drained | Poorly drained | Very poorly, rapidly drained |
| Soil | Depth of topsoil (cm) | > 5 | < 5 | - |
|  | Depth to seasonal watertable (m) | > 2.0 | 2.0 - 1.0 | < 1.0 |
|  | Total amount of water available to plants (mm) | > 150 | 150 - 50 | < 50 |
|  | Electrical conductivity (dS/m ECe)** | < 3.8 | 3.8 - 8.6 | > 8.6 |
|  | Estimated subsoil permeability | Highly, moderately, slowly permeable | - | Very slowly, very highly permeable |

* From Irrigation and Drainage Practice, p40

** Saturation extract

Note:	The above table has been developed from regional data to provide a general assessment of land suitability and does not provide sufficient information for the evaluation of specific sites.

Additional site specific factors that would require consideration prior to development may include:

- site size and layout;

- access to services and utilities;

- availability and quality of irrigation water;

- access to surface and/or subsurface drainage;

- water table conditions and groundwater quality;

- soil factors such as pH, organic matter content, nutrient status, sodicity, etc.

Table 2.6   Land suitability assessment for irrigated perennial horticulture (stone fruits, pome fruits).

| PARAMETERS INFLUENCING | LAND SUITABILITY RATINGS |
| --- | --- |
| PERENNIAL HORTICULTURE PRODUCTION | Class 1 | Class 2 | Class 3 |
| Landscape | Slope (%) (Assumes microspray/trickle irrigation) | < 20% | - | > 20% |
|  | Site drainage | Well, moderately well drained | Imperfectly drained | Poorly, very poorly, rapidly drained |
|  | Susceptibility to gully erosion | Low | Moderate , high | - |
|  | Susceptibility to sheet/rill erosion | Low | Moderate, high | - |
| Soil | Depth of topsoil (cm) | > 10 | < 10 | - |
|  | Depth to hard rock (m) | > 1.0 | 1.0 - 0.5 | < 0.5 |
|  | Depth to seasonal watertable (m) | > 2.0 | 2.0 - 1.0 | < 1.0 |
|  | Electrical conductivity (dS/m ECe)** | < 3.8 | 3.8 - 8.6 | > 8.6 |
|  | Estimated subsoil permeability | Highly, moderately permeable | Slowly permeable | Very slowly , very highly permeable |

** Saturation extract

Note:	The above table has been developed from regional data to provide a general assessment of land suitability and does not provide sufficient information for the evaluation of specific sites.

Additional site specific factors that would require consideration prior to development may include:

- site size and layout;

- access to services and utilities;

- availability and quality of irrigation water;

- access to surface and/or subsurface drainage;

- water table conditions and groundwater quality;

- soil factors such as pH, organic matter content, nutrient status, sodicity, etc;

Where access to irrigation and drainage infrastructure is unavailable, please refer to Table 2.9 for dryland  olive production and Table 2.10 for dryland viticulture production.

Table 2.7   Land suitability assessment for irrigated tomato production.

| PARAMETERS INFLUENCING | LAND SUITABILITY RATINGS |
| --- | --- |
| TOMATO PRODUCTION | Class 1 | Class 2 | Class 3 |
| Landscape | Slope (%) (trickle or microspray irrigation)*,+ | < 20 | - | > 20 |
|  | Susceptibility to gully erosion | Low | Moderate - high | - |
|  | Susceptibility to sheet/rill erosion | Low | Moderate - high | - |
| Soil | Depth of topsoil (cm) | > 5 | < 5 | - |
|  | Depth to hard rock (m) | > 1.0 | 1.0 - 0.5 | < 0.5 |
|  | Proportion of stones and boulders (%) | <10 | 10 - 40 | > 40 |
|  | Depth to seasonal watertable (m) | > 2.0 | 2.0 - 1.0 | < 1.0 |
|  | Susceptibility to surface crusting | Low | Moderate, high | - |
|  | Total amount of water available to plants (mm) | > 150 | 150 - 50 | < 50 |
|  | Electrical conductivity (dS/m ECe)** | < 3.8 | 3.8 - 8.6 | > 8.6 |

* From TomCHECK Management Guidelines, pp2-3.

+ Slope classes beyond the scope of the study, further information required

** Saturation extract

Note:	The above table has been developed from regional data to provide a general assessment of land suitability and does not provide sufficient information for the evaluation of specific sites.

Additional site specific factors that would require consideration prior to development may include:

- site size and layout;

- access to services and utilities;

- availability and quality of irrigation water;

- access to surface and/or subsurface drainage;

- water table conditions and groundwater quality;

- soil factors such as pH, organic matter content, nutrient status, sodicity, etc;

Table 2.8   Land suitability assessment for irrigated farm forestry > 40 ha (Bluegum, Eucalyptus globulus).

| PARAMETERS INFLUENCING | LAND SUITABILITY RATINGS |
| --- | --- |
| IRRIGATED FARM FORESTRY | Class 1 | Class 2 | Class 3 |
| Landscape | Slope (%) (assumes flood irrigation)+ | > 0.2 | 0.2 - 0.05 | < 0.05 |
|  | Site drainage | Well, moderately well, imperfectly | Poorly | Very poorly, rapidly drained |
| Soil | Depth of topsoil (cm) | > 5 | < 5 | - |
|  | Depth to seasonal watertable (m) | > 3.0 | 3.0 - 1.0 | < 1.0 |
|  | Depth to hard rock (m) | > 150 | 150 - 80 | < 80 |
|  | Electrical conductivity (dS/m ECe)* | < 4.0 | 4.0 - 6.0 | > 6.0 |
|  | Estimated subsoil permeability | Highly, moderately, permeable | Slowly permeable | Very slowly, very highly permeable |

+ Slope classes beyond the scope of the study, further information required

* Saturation extract

Note:	The above table has been developed from regional data to provide a general assessment of land suitability and does not provide sufficient information for the evaluation of specific sites.

Additional site specific factors that would require consideration prior to development may include:

- site size and layout;

- access to services and utilities;

- availability and quality of irrigation water;

- access to surface and/or subsurface drainage;

- water table conditions and groundwater quality;

- soil factors such as pH, organic matter content, nutrient status, sodicity, etc;

Table 2.9   Land suitability assessment for dryland olive production.

| Parameters influencing | Land SUITABILITY Ratings |
| --- | --- |
| olive production | Class 1 | Class 2 | Class 3 |
| Landscape | Slope (%) | < 20 | - | > 20 |
|  | Site drainage | Well, moderately well drained | Imperfectly drained | Poorly, very poorly, rapidly |
|  | Susceptibility to gully erosion | Low | Moderate - high | - |
|  | Susceptibility to sheet/rill erosion | Low | Moderate - high | - |
| Soil | Topsoil depth (cm) | > 10 | < 10 | - |
|  | Depth to hard rock (m) | > 1.0 | 1.0 - 0.8 | < 0.8 |
|  | Total amount of water available to plants (mm) | > 150 | 150 - 50 | < 50 |
|  | Depth to seasonal watertable (m) | > 2.0 | 2.0 - 1.0 | < 1.0 |
|  | Electrical conductivity (dS/m ECe)* | < 1.5 | 1.5 - 3.0 | > 3.0 |
|  | Estimated subsoil permeability | Highly, moderately permeable | Slowly permeable | Very slowly, very highly permeable |

* Saturation extract

Note:	The above table has been developed from regional data to provide a general assessment of land suitability and does not provide sufficient information for the evaluation of specific sites.

Additional site specific factors that would require consideration prior to development may include:

- site size and layout;

- access to services and utilities;

- availability of supplementary water supply;

- access to surface and/or subsurface drainage;

- water table conditions and groundwater quality;

- soil factors such as pH, organic matter content, nutrient status, sodicity, etc.

It is recommended that commercial vineyards or orchards not be established without access to a supplementary water supply for irrigation.  Throughout the growing season, evapotranspiration exceeds rainfall in the Shire of Campaspe.  As a result crops need to use water stored in the soil profile.  In most seasons, water stored in the soil profile and rainfall during the growing season would be insufficient to meet the needs of the crop.  Therefore, the risk of crop loss due to water deficits would be high in most seasons.

Table 2.10   Land suitability for dryland viticulture.

| Parameters influencing | Land SUITABILITY Ratings |
| --- | --- |
| viticulture | Class 1 | Class 2 | Class 3 |
| Landscape | Slope (%) | < 20 | - | > 20 |
|  | Site drainage | Well, moderately well | Imperfectly drained | Poorly, very poorly, rapidly drained |
|  | Susceptibility to gully erosion | Low | Moderate - high | - |
|  | Susceptibility to sheet/rill erosion | Low | Moderate - high | - |
| Soil | Topsoil depth (cm) | > 10 | < 10 | - |
|  | Depth to hard rock (m) | > 2.0 | 1.0 - 2.0 | < 1.0 |
|  | Depth to seasonal watertable (m) | > 2.0 | 2.0 - 1.0 | < 1.0 |
|  | Total amount of water available to plants (mm) | > 150 | 150 - 50 | 50 |
|  | Electrical conductivity (dS/m ECe)* | < 1.5 | 1.5 - 3.0 | > 3.0 |
|  | Estimated subsoil permeability | Highly , moderately permeable | Slowly permeable | Very slowly, very highly permeable |

* Saturation extract

Note:	The above table has been developed from regional data to provide a general assessment of land suitability and does not provide sufficient information for the evaluation of specific sites.

Additional site specific factors that would require consideration prior to development may include:

- site size and layout;

- access to services and utilities;

- availability of supplementary water supply;

- access to surface and/or subsurface drainage;

- water table conditions and groundwater quality;

- soil factors such as pH, organic matter content, nutrient status, sodicity, etc.

It is recommended that commercial vineyards or orchards not be established without access to a supplementary water supply for irrigation.  Throughout the growing season, evapotranspiration exceeds rainfall in the Shire of Campaspe.  As a result crops need to use water stored in the soil profile.  In most seasons, water stored in the soil profile and rainfall during the growing season would be insufficient to meet the needs of the crop.  Therefore, the risk of crop loss due to water deficits would be high in most seasons.

Table 2.11   Land capability assessment for broadacre effluent disposal (ground absorption) for feedlots.

| Parameters influencing | Land capability ratings |
| --- | --- |
| BROADACRE EFFLUENT DISPOSAL | Class 1 | Class 2 | Class 3 | Class 4 | Class 5 |
| Landscape | Slope (%)* | < 3 | 3 - 10 | 11 - 20 | 21 - 32 | > 32 |
|  | Flooding risk* | Nil | Low | Moderate | High | Very high |
| Soil | Depth to seasonal watertable (m) | > 2.0 | 2.0 - 1.5 | 1.5 - 1.0 | 1.0 - 0.5 | < 0.5 |
|  | Depth to hard rock/impermeable layer (m) | > 1.5 | 1.0 - 1.5 | 1.0 - 0.75 | 0.75 - 0.5 | < 0.5 |
|  | Estimated subsoil permeability* | Highly permeable | Moderately permeable | - | Slowly permeable | Very slowly, very highly permeable |

* See Appendix C

Note:	10 mm/day is equivalent to disposing of 1000 l/day along a 0.5 x 200 m trench

Table 2.12   Land capability assessment (ground absorption) for septic tanks.

| Parameters influencing | Land capability ratings |
| --- | --- |
| SEPTIC TANK EFFLUENT DISPOSAL | Class 1 | Class 2 | Class 3 | Class 4 | Class 5 |
| Landscape | Slope (%)* | < 3 | 3 - 10 | 11 - 20 | 21 - 32 | > 32 |
|  | Flooding risk* | Nil | Low | Moderate | High | Very high |
| Soil | Depth to seasonal watertable (m) | > 2.0 | 2.0 - 1.5 | 1.5 - 1.0 | 1.0 - 0.5 | < 0.5 |
|  | Depth to hard rock/impermeable layer (m) | > 1.5 | 1.0 - 1.5 | 1.0 - 0.75 | 0.75 - 0.5 | < 0.5 |
|  | Estimated subsoil permeability* | Highly permeable | Moderately permeable | - | Slowly permeable | Very slowly, very highly permeable |

* See Appendix C

Note:	Areas capable of absorbing effluent from a standard anaerobic, all-waste, septic tank connected to a single family dwelling (approximate output of 1000 litres per day).

10 mm/day is equivalent to disposing of 1000 l/day along a 0.5 x 200 m trench

Table 2.13   Land capability assessment for secondary (gravel) roads.

| Parameters Influencing | Land capability ratings |
| --- | --- |
| SECONDARY ROADS | Class 1 | Class 2 | Class 3 | Class 4 | Class 5 |
| Landscape | Slope (%) | 0 - 1 | 2 - 5 | 6 - 10 | 11 - 30 | > 30 |
|  | Site drainage* | Rapidly drained | Well drained | Moderately, imperfectly drained | Poorly, very poorly drained | - |
|  | Flooding risk* | Nil | Low | Moderate | High | Very high |
|  | Susceptibility to sheet / rill erosion* | Very low | Low | Moderate | High | Very high |
|  | Susceptibility to gully erosion* | Very low | Low | Moderate | High | Very high |
|  | Susceptibility to slope failure* | Very low | Low | Moderate | High | Very high |
| Soil | Depth to seasonal watertable (m) | > 5 | 5 - 2 | 2 - 1 | 1 - 0.5 | < 0.5 |

* See Appendix C

Note:	Areas capable of being used for the construction of earthen roads for light vehicles without sealed surfaces or concrete drainage and kerbing.

Table 2.14   Land capability assessment for low density residential and rural living development.

| LOW DENSITY RESIDENTIAL DEVELOPMENT (0.4 ha - 2.0 ha) | RURAL LIVING DEVELOPMENT (2.0-40 ha) |
| --- | --- |
| Secondary roads | No change to capability class | Secondary roads | No change to capability class |
| Septic tanks | No change to capability class | Effluent disposal | Improve rating by one class if major limitation is due to permeability, drainage and depth to hard rock. No change to rating class if another criteria is the major limitation present |

Rural residential development involves a range of land uses including effluent disposal, secondary roads, building foundations and earthen dams.  For this study, land capability assessments have been conducted for septic tank effluent disposal and secondary roads, as inappropriate siting of these land uses may lead to significant engineering difficulties and environmental problems..  It is thought that current technologies can overcome most land and soil constraints in the construction of earthen dams and building foundations, therefore they have not been included in the capability assessment.

The landform and soils within certain land components can vary substantially in the Shire.  This variation within a component is more likely to occur with large size allotments.  It is recognised that in areas greater than 5 ha, detailed site inspection can highlight areas with a higher or lower capability to support a given land use.

For example, septic tanks as a form of effluent disposal may be restricted by slow permeability on a small allotment (less than 2 ha), however on a larger allotment better drained soils may be found that are more capable of supporting septic tanks.  Larger allotments also allow for greater flexibility in management and design, while an allotment of 0.4 ha will place absolute limits on options for development.

In assessing the overall capability for rural residential development, the capability of septic tanks effluent disposal and secondary roads  has been combined to determine the overall capability class.

For the purpose of this study, low density residential  development has been defined as allotment sizes between 0.4 - 2.0 ha, while rural living has been defined as allotment sizes between 2.0 - 40 ha.

3    LAND SYSTEM DESCRIPTIONS

3.1 Active floodplains - Murray & Campaspe Rivers

General Description

| Land System: 4.1Ffc3, 4.1Ffc4, 4.1FLfc4 |
| --- |
| Parent material | Quaternary alluvial sediments |
| Climate | 300 - 500 mm (mean annual rainfall) |
| Land component | 1 | 2 | 3 | 4 |
| Soil association & dominant soil types | Kanyapella (Kanyapella clay loam, Kanyapella clay) | Wallenjoe (Wallenjoe Clay) |  | Campaspe (Campaspe Suite Type1, Type 2, Type 3) |
| Landform element | Higher active floodplain | Swamp, Oxbow lake, Site drainage depression | Murray lower active floodplain | Campaspe lower active floodplain |
| Slope range | 0 - 1 % | 0 - 1 % | 0 - 1 % | 0 - 1 % |
| General soil description | Strongly structured, heavy textured cracking grey clays | Low lying, heavy textured cracking grey clays. | Low lying heavy textured clays and variable soils. | Low lying high texture contrast soils and heavy textured clays. |
| Factual Key | Dy3.12 | Ug5.2 | Ug5.2, Uf | Dd2.43, Uf |
| Australian Soil Classification | Grey Sodosol (3) | Grey Vertosol (2) | Grey Vertosol (3) Grey Sodosol (2) | (2) |
| Site Drainage | Poorly drained | Very poorly drained | Very poorly drained | Poorly drained |
| Estimated permeability (subsoil) | Moderately permeable | Slowly permeable | Very slowly permeable | Moderately permeable |
| Rock outcrop | Nil | Nil | Nil | Nil |
| Depth to hardrock | > 200 cm | > 200 cm | > 200 cm | > 200 cm |
| Susceptibility to land degradation | Sheet and rill: Low Wind erosion: Low Gully erosion: Low | Sheet and rill: Low Wind erosion: Low Gully erosion: Low | Sheet and rill: Low Wind erosion: Low Gully erosion: Low | Sheet and rill: Low Wind erosion: Low Gully erosion: Low |
| Broad Vegetation Type | Northern Riverine Grassy Woodlands Complex, Swamp Scrub Complex |
| Current land use | Dryland grazing, irrigated horticulture | Dryland grazing, irrigated horticulture | Dryland grazing, irrigated horticulture | Dryland grazing, irrigated horticulture |

3.1 Active floodplains - Murray & Campaspe Rivers (continued)

Detailed Soil Description

| Land component | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Representative soil type | A1 0 - 10 cm Brownish grey (2.5Y 5/1) clay loam or light clay, moderate subangular blocky structure, slight buckshot gravel, gradual transition to: B1 10 - 45 cm Yellowish grey(2.5Y 5/2) light or medium clay, moderate angular blocky structure, slight ferruginous concretions, gradual transition to: B21 45 - 85 cm Weakly mottled yellow brown and grey medium clay, slight soft calcium carbonate and concretions, gradual transition to: B23 85 - 120+ cm Mottled yellow brown and grey light clay | A1 0 - 10 cm Grey (N 4/0) heavy clay, moderate angular blocky structure, gradual transition to: B1 10 - 60 cm Steel grey (N 5/0) heavy clay, moderate angular blocky structure, gradual transition to: B2 60 - 120+ cm Heavy clay with calcium carbonate | A1 0 - 5 cm Very dark greyish brown (10YR 3/2) loam, strong subangular blocky structure, pH 7.0, abrupt transition to : B11 5 - 15 cm Light grey (10YR 7/2) silty clay, weak subangular blocky structure, few mottles, pH 7.0, diffuse transition to: B12 15 - 30 cm Light grey (10YR 7/2) light medium clay, moderate subangular blocky structure, common mottles, pH 7.0, diffuse transition to: B21 30 - 70+ cm Yellowish brown (10YR 5/4) medium clay, strong subangular blocky structure, few mottles, pH7.0 | A1 0-15 cm Grey brown (7.5YR4/2) loam A2 15-25 cm loam abrupt transition to: B21 25-40cm Dark greysih brown (7.5YR 3/2) medium clay, gradual transition to: B22 40-75cm Greyish-brown medium clay, gradual transition to: B23 75-120+cm Yellowish and greyish brown medium clay, diffusely mottled. |
| Source of detailed soils information | Skene, J.K.M. (1963) Kanyapella clay profile 29 | Skene, J.K.M. & Harford, L.B. (1964) Wallenjoe clay profile 24 | Field sampling | Skene, J.K.M. & Harford, L.B. (1964) Campaspe suite 1 profile 18 |

3.1 Active floodplains - Murray & Campaspe Rivers (continued)

Standard Planning Responses

| Land System 4.2Flf3, 4.2Flf4 |
| --- |
| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| Rice | 1 | iii | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Estimated subsoil permeability | Must comply with the Planning Scheme Refer to Assessment of Land Suitability for Rice Growing Guidelines Seek advice from the Industry Development Officer within DNRE |
|  | 3 | i | Nil | As above |
|  | 4 | iii | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
| Irrigated cropping | 1 | ii | Site drainage Depth of topsoil | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE |
|  | 2 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 3 | iii | Site drainage | As above |
|  | 4 | ii | Site drainage | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE |
| Irrigated perennial pasture | 1 | ii | Site drainage | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE |
|  | 2 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 3 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 4 | ii | Site drainage | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE |

3.1 Active floodplains - Murray & Campaspe Rivers (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Irrigated perennial horticulture | 1 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 4 | iii | Site drainage | As above |
| Irrigated tomatoes | 1 | ii | Susceptibility to surface crusting | Must comply with the Planning Scheme Refer to TomCHECK, Guidelines to Successful processing tomato production Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 2 | ii | Susceptibility to surface crusting | As above |
|  | 3 | ii | Susceptibility to surface crusting | As above |
|  | 4 | i | Nil | As above |
| Irrigated farm forestry | 1 | ii | Site drainage | Must comply with the Planning Scheme Refer to the Irrigation and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 2 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 3 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 4 | ii | Site drainage | Must comply with the Planning Scheme Refer to the Irrigation and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |

3.1 Active floodplains - Murray & Campaspe Rivers (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Dryland olives | 1 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 4 | iii | Site Drainage | As above |
| Dryland viticulture | 1 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 4 | iii | Site drainage | As above |
| Broadacre Effluent disposal (feedlots) | 1 | iv | Flooding risk | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | iv | Estimated subsoil permeability Flooding risk | As above |
|  | 3 | v | Estimated subsoil permeability Flooding risk | As above |
|  | 4 | v | Flooding risk | As above |
| Effluent disposal (septic tank) | 1 | iv | Flooding risk | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | iv | Estimated subsoil permeability Flooding risk | As above |
|  | 3 | v | Estimated subsoil permeability Flooding risk | As above |
|  | 4 | v | Flooding risk | As above |
| Secondary roads | 1 | iv | Site drainage | Must comply with the Planning Scheme |
|  | 2 | v | Flood risk | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome |
|  | 3 | v | Flooding risk | As above |
|  | 4 | v | Flooding risk | As above |

3.2 Corop wetland complex

General Description

| Land System: 4.2Flf3, 4.2Flf4 |
| --- |
| Parent material | Quaternary alluvial sediments |
| Climate | 300-500 mm (mean annual rainfall) |
| Land component | 1 | 2 | 3 | 4 |
| Soil association & dominant soil types | Carag (Carag Clay) Wallenjoe ( Wallenjoe clay) Moora-Wallenjoe (Wallenjoe Clay, Moora clay loam, Yuga clay) | Corop (Corop clay) | Unclassified variable soils | Koga (Koga Clay) Cornella (Cornella clay) Karook (Karook loam, Arkoo loam, Moora clay loam) |
| Landform element | Swamp / Site drainage depression | Minor alluvial plain | Lunette | Low alluvial plain |
| Slope range | 0 - 1 % | 0 - 1 % | 0 - 10 % | 0 - 1 % |
| General soil description | Heavy textured grey or black cracking clay soils | Heavy textured grey cracking clay soils | Strongly structured heavy textured brown clay soils | High texture contrast soils with mottled yellow clay subsoils and strongly structured, heavy textured grey cracking clays |
| Factual Key | Ug5.2, Ug5.1 | Ug5.2 | Uf, Dr, Dy | Db1.33, Dy3.13, Dy3.23, Ug5.2 |
| Australian Soil Classification | Grey Vertosol (2), Brown Vertosol (2) | Grey Vertosol (2) | Brown Deromosol (3) | Brown Vertosol (2), Grey Vertosol (2), Grey Sodosol (2) Brown Sodosol (2) |
| Site Drainage | Very poorly drained | Very poorly drained | Well drained | Poorly drained |
| Estimated permeability (subsoil) | Slowly permeable | Slowly permeable | Moderately permeable | Slowly permeable |
| Rock outcrop | Nil | Nil | Nil | Nil |
| Depth to hardrock | > 200 cm | > 200 cm | > 200 cm | > 200 cm |
| Susceptibility to land degradation | Sheet and rill: Low Wind erosion: Low Gully erosion: Low-med | Sheet and rill: Low Wind erosion: Low Gully erosion: Medium | Sheet and rill: Low Wind erosion: Low Gully erosion: Medium | Sheet and rill: Low Wind erosion: Low Gully erosion: Medium |
| Broad Vegetation Type | Northern Plains Grassy Woodland Complex, Swamp Scrub Complex, Mallee Heath Complex |
| Current land use | Dryland grazing and cropping | Dryland grazing and cropping | Dryland grazing and cropping | Dryland grazing and cropping |

3.2 Corop wetland complex (continued)

Detailed Soil Description

| Land component | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Representative soil type | A1 0 - 10 cm Grey (N 4/0) heavy clay, moderate angular blocky structure, gradual transition to: B1 10 - 60 cm Steel grey (N 5/0) heavy clay, moderate angular blocky structure, gradual transition to: B2 60 - 120+ cm Heavy clay with calcium carbonate | A1 0 - 10 cm Grey (10YR 5/1) medium clay, weak angular blocky structure, sharp transition to: B1 10 - 45 cm Grey (5Y 4/1) heavy clay, moderate subangular blocky structure, gradual transition to: B21 45 - 100 cm Yellowish grey (5Y 5/2) heavy clay, moderate subangular blocky structure, slight calcium carbonate and gypsum, gradual transition to: B22 100 - 180 + cm Mottled yellowish grey heavy clay, slight calcium carbonate | A1 0 - 15 cm Reddish brown (5YR 5/3) medium heavy clay, strong subangular blocky structure, pH 6.0, gradual transition to: B21 15 - 35 cm Reddish brown (10YR 4/4) medium clay, strong subangular blocky structure, pH 8.5, gradual transition to: B22 35 - 60 cm Strong brown (7.5YR 5/6) light medium clay, weak subangular blocky structure, pH 9.0, gradual transition to: B23 60 - 80+ cm Reddish yellow (10YR 6/6) light medium clay, weak subangular blocky structure, pH 10.0 | A1 0 - 10 cm Mottled grey brown (7.5YR 4/4) clay loam A2 10 - 15 cm Sporadically bleached, sharp transition to: B1 15 - 50 cm Brown (7.5YR 4/3) to yellowish grey-brown (10YR 4/3) heavy clay, moderate angular blocky structure, gradual transition to: B21 50 - 75 cm Yellowish brown (10YR 5/4) heavy clay, moderate subangular blocky structure, slight calcium carbonate, gradual transition to: B22 75 - 120 cm Yellowish brown medium clay, slight calcium carbonate and gypsum B23 120+ cm Mottled brownish yellow-grey and brown medium clay, slight calcium carbonate |
| Source of detailed soils information | Skene, J.K.M. & Harford, L.B. (1964) Wallenjoe clay profile 24 | Skene, J.K.M. (1963) Corop clay profile 14 | Field sampling | Skene, J.K.M. & Harford, L.B. (1964) Koga clay loam profile 27 |

3.2 Corop wetland complex (continued)

Standard Planning Responses

| Land System 4.2Flf3, 4.2Flf4 |
| --- |
| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| Rice | 1 | ii | Estimated subsoil permeability | Must comply with the Planning Scheme Refer to Assessment of Land Suitability for Rice Growing Guidelines Seek advice from the Industry Development Officer within DNRE |
|  | 2 | ii | Estimated subsoil permeability | As above |
|  | 3 | iii | Slope Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 4 | ii | Estimated subsoil permeability | Must comply with the Planning Scheme Refer to Assessment of Land Suitability for Rice Growing Guidelines Seek advice from the Industry Development Officer within DNRE |
| Irrigated cropping | 1 | iii | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Estimated subsoil permeability | As above |
|  | 3 | iii | Slope | As above |
|  | 4 | ii | Site drainage Susceptibility to surface crusting | Must comply with the Planning Scheme. Refer to the Irrigation and Planning Practice. Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
| Irrigated perennial pasture | 1 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage | As above |
|  | 3 | iii | Slope | As above |
|  | 4 | ii | Site drainage Available water capacity | Must comply with the Planning Scheme. Refer to the Irrigation and Planning Practice. Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE |
| Irrigated perennial horticulture | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |

3.2 Corop wetland complex (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Irrigated perennial horticulture | 3 | i | Nil | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE |
|  | 4 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
| Irrigated tomatoes | 1 | ii | Susceptibility to surface crusting | Must comply with the Planning Scheme Refer to TomCHECK, Guidelines to Successful processing tomato production Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 2 | ii | Susceptibility to surface crusting Available water capacity | As above |
|  | 3 | i | Nil | As above |
|  | 4 | ii | Susceptibility to surface crusting Available water capacity | As above |
| Irrigated farm forestry | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | iii | Slope | Must comply with the Planning Scheme Refer to the Irrigation and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE |
|  | 4 | iii | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
| Dryland olives | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | i | Nil | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE |
|  | 4 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |

3.2 Corop wetland complex (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Dryland viticulture | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | i | Nil | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE |
|  | 4 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
| Broadacre Effluent disposal (feedlots) | 1 | v | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | v | Estimated subsoil permeability | As above |
|  | 3 | ii | Nil | Must comply with the Planning Scheme Must comply with the Guidelines for the conduct of intensive animal industries Must comply with the Victorian code for Cattle Feedlots or; Must comply with the Code of practice for piggeries or; Must comply with the Code of accepted farming practice for the welfare of domestic fowl Manage to overcome physical limitations (Refer to Appendix A) |
|  | 4 | v | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
| Effluent disposal (septic tank) | 1 | v | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | v | Estimated subsoil permeability | As above |
|  | 3 | ii | Nil | Must comply with the planning scheme Must comply with the Code of Practice - Septic Tanks |
|  | 4 | v | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |

3.2 Corop wetland complex (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-v) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Secondary roads | 1 | iv | Site drainage Flooding risk | Must comply with the Planning Scheme |
|  | 2 | iv | Site drainage | As above |
|  | 3 | ii | Nil | As above |
|  | 4 | iv | Site drainage | As above |

3.3 Prior streams alluvial plain

General Description

| Land System : 4.2Pf4.2 |
| --- |
| Parent material | Quaternary alluvium |
| Climate | 400 - 500 mm (mean annual rainfall) |
| Land component | 1 | 2 | 3 | 4 | 5 |
| Soil association & dominant soil types | Carag (Carag clay) Congupna (Congupna clay) | Coomboona (Congupna clay , Congupna clay loam) | Goulburn (Goulburn loam, Goulburn clay loam) Coomboona (Goulburn loam, Goulburn clay loam) | Wanalta (Wanalta loam, Wana loam) Lemnos (Lemnos loam) Wanurp (Wanurp sandy loam) | Naneela (Naneela fine sandy loam) Timmering (Timmering loam) Shepparton (Shepparton fine sandy loam) |
| Landform element | Site drainage depression | Low alluvial plain | Mid alluvial plain | Higher alluvial plain | Prior stream beds & levees |
| Slope range | 0 - 1 % | 0 - 1 % | 0 - 1 % | 0 - 1 % | 0 - 3 % |
| General soil description | Heavy textured grey cracking clay soils | Heavy textured grey cracking clay soils, or high texture contrast soils with yellow mottled clay subsoils | High texture contrast soils with clay loams topsoils and mottled yellow clay subsoils | High texture contrast soils with brown loamy topsoils, bleached A2 horizons and mottled red clay subsoils | High texture contrast soils with brown loamy topsoils, occassional bleached A2 horizons, and red clay subsoils |
| Factual Key | Ug5.2 | Ug, Dy3.23 | Dy3.13 | Dr3.33 Dr3.23, Dr3.43 | Dr2.13, Dr2.33, Dr3.33 |
| Australian Soil Classification | Brown Vertosol (2) | Brown Vertosol (2), Grey Sodosol (2) | Brown Sodosol (2) | Red Sodosol (2) | Red Sodosol (2) |
| Site Drainage | Very poorly drained | Poorly drained | Imperfectly drained | Imperfectly drained | Moderately well drained |
| Estimated permeability (subsoil) | Very slowly permeable | Very slowly permeable | Slowly permeable | Moderately permeable | Moderately permeable |
| Rock outcrop | Nil | Nil | Nil | Nil | Nil |
| Depth to hardrock | > 200 cm | > 200 cm | > 200 cm | > 200 cm | > 200 cm |
| Susceptibility to land degradation | Sheet and rill: Low Wind erosion: Low Gully erosion: Low | Sheet and rill: Medium Wind erosion: Low Gully erosion: Medium | Sheet and rill: Low Wind erosion: Medium Gully erosion: Low | Sheet and rill: Low Wind erosion: Medium Gully erosion: Low | Sheet and rill: Low Wind erosion: Medium Gully erosion: Low |
| Broad Vegetation Type | Northern Plains Grassy Woodland Complex, Northern Riverine Grassy Woodland Complex |
| Current land use | Grazing | Grazing, irrigated pasture | Grazing, irrigated pasture | Dryland cropping and grazing, irrigated pasture, dairying, stonefruits, tomatoes | Dryland cropping and grazing , irrigated pasture, dairying, stonefruits, irrigated horticulture |

3.3 Prior streams alluvial plain (continued)

Detailed Soil Description

| Land component | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
| Representative soil type | A1 0 - 10 cm Dark grey brown 10YR 3/3) cracking clay, moderate subangular blocky structure, sharp transition to: B1 10 - 50 cm Yellow grey (2.5Y 5/3) heavy clay, weak angular blocky structure, gradual transition to: B21 50 - 90 cm Yellow grey (2.5Y 5/3) heavy clay, weak angular blocky structure, slight soft calcium carbonate and gypsum, gradual transition to: B22 90 - 190+ cm Brownish or mottled grey medium clay, slight calcium carbonate | A1 0 - 10 cm Grey (2.5Y 4/1 to 10YR 4/1) clay loam, weak to moderate angular blocky structure, buckshot gravels, sharp transition to: B1 10 - 50 cm Brownish grey (2.5Y 4/2) heavy clay, moderate angular blocky structure, gradual transition to: B2 50+ cm Brownish yellow grey (2.5Y 4/4) medium clay, apedal, slight calcium carbonate | A1 0 - 10 cm Grey brown (10TR 4/2) loam, weak angular blocky structure, slight buckshot gravel, sharp transition to: B1 10 - 45 cm Yellowish brown (7.5YR 5/6) medium clay, weak to moderate prismatic structure, gradual transition to: B21 45 - 80 cm Yellowish brown (10YR 5/6) heavy clay, weak subangular blocky structure, slight calcium carbonate, gradual transition to: B22 80 - 120+ cm Yellowish grey or mottled light yellowish grey (2.5Y 5/2) medium or heavy clay, slight calcium carbonate | A1 0 - 10 cm Brown (5YR 5/4) to greyish brown (7.5YR 5/4) loam, A2 10 - 15 cm Loam , sporadically bleached at boundary of B1, sharp transition to: B1 15 - 50 cm Red-brown (5YR 3/4) heavy clay, moderate prismatic to weak blocky structure, gradual transition to: B21 50 - 70 cm Brown medium clay, soft calcium carbonate, gradual transition to: B22 70 - 120 cm Mottled greyish brown and yellowish grey brown light clay B23 120+ cm Moderately mottled grey and grey brown medium clay | A1 0 - 15 cm Brown (7.5YR 4/4) loam A2 15 - 25 cm Loam sporadically bleached, sharp transition to: B1 25 - 50 cm Red-brown (2.5YR 3/6) medium clay, moderate subangular blocky structure, gradual transition to: B21 50 - 95 cm Brown or yellowish brown light clay, strong subangular blocky structure, slight calcium carbonate, gradual transition to: B22 95 - 120+ cm Mottled yellowish grey-brown light clay, slight calcium carbonate |
| Source of detailed soils information | Skene, J.K.M. & Harford L.B. (1964) Carag clay profile 16 | Skene, J.K.M. & Poutsma, T.J. (1962) Congupna clay loam profile 47 | Skene, J.K.M. & Poutsma, T.J. (1962) Goulburn clay loam profile 16 | Skene, J.K.M. & Harford, L.B. (1964) Wanalta loam profile 5 | Skene, J.K.M. & Harford, L.B. (1964) Timmering loam profile 35 |

3.3 Prior streams alluvial plain (continued)

Standard Planning Responses

| Land System |
| --- |
| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| Rice | 1 | i | Nil | Must comply with the Planning Scheme Refer to Assessment of Land Suitability for Rice Growing Guidelines Seek advice from the Industry Development Officer within DNRE |
|  | 2 | i | Nil | As above |
|  | 3 | ii | Estimated subsoil permeability | As above |
|  | 4 | iii | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 5 | iii | Estimated subsoil permeability | As above |
| Irrigated cropping | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Estimated subsoil permeability | As above |
|  | 3 | ii | Depth of topsoil Available water capacity | As above |
|  | 4 | i | Nil | As above |
|  | 5 | i | Nil | As above |
| Irrigated perennial pasture | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Estimated subsoil permeability | As above |
|  | 3 | ii | Available water capacity | Must comply with the Planning Scheme. Refer to the Irrigation and Planning Practice. Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 4 | ii | Depth of topsoil Estimated subsoil permeability | As above |
|  | 5 | i | Nil | As above |

3.3 Prior streams alluvial plain (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Irrigated perennial horticulture | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | ii | Site driainage Depth of topsoil Estimated subsoil permeability | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 4 | ii | Site drainage Estimated subsoil permeability | As above |
|  | 5 | i | Nil | As above |
| Irrigated tomatoes | 1 | i | Nil | Must comply with the Planning Scheme Refer to TomCHECK, Guidelines to Successful processing tomato production Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 2 | ii | Susceptibility to surface crusting Available water capacity | As above |
|  | 3 | ii | Available water capacity | As above |
|  | 4 | i | Nil | As above |
|  | 5 | i | Nil | As above |
| Irrigated farm forestry | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Estimated subsoil permeability | As above |
|  | 3 | ii | Estimated subsoil permeability | Must comply with the Planning Scheme Refer to the Irrigation and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 4 | ii | Estimated subsoil permeability | As above |
|  | 5 | i | Nil | As above |

3.3 Prior streams alluvial plain (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Dryland olives | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | ii | Site drainage Depth of topsoil available water capacity Estimated subsoil permeability | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 4 | ii | Site drainage Depth of topsoil Estimated subsoil permeability | As above |
|  | 5 | i | Nil | As above |
| Dryland viticulture | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | ii | Site drainage Depth of topsoil available water capacity Estimated subsoil permeability | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 4 | ii | Site drainage Depth of topsoil Estimated subsoil permeability | As above |
|  | 5 | i | Nil | As above |

3.3 Prior streams alluvial plain (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-v) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Broadacre Effluent disposal (feedlots) | 1 | v | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | v | Estimated subsoil permeability | As above |
|  | 3 | iv | Estimated subsoil permeability | Must comply with the Planning Scheme Must comply with the Guidelines for the conduct of intensive animal industries Must comply with the Victorian code for Cattle Feedlots or; Must comply with the Code of practice for piggeries or; Must comply with the Code of accepted farming practice for the welfare of domestic fowl Manage to overcome physical limitations (Refer to Appendix A) |
|  | 4 | iv | Estimated subsoil permeability | As above |
|  | 5 | ii | Nil | As above |
| Effluent disposal (septic tank) | 1 | v | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | v | Estimated subsoil permeability | As above |
|  | 3 | iv | Estimated subsoil permeability | Must comply with the planning scheme Must comply with the Code of Practice - Septic Tanks |
|  | 4 | iv | Estimated subsoil permeability | As above |
|  | 5 | ii | Nil | As above |
| Secondary roads | 1 | iv | Site drainage Flooding risk | Must comply with the Planning Scheme |
|  | 2 | iv | Site drainage | As above |
|  | 3 | iv | Site drainage | As above |
|  | 4 | iii | Site drainage | As above |
|  | 5 | iii | Site drainage | As above |

3.4 Treeless alluvial plain

General Description

| Land System: 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 |
| --- |
| Parent material | Quaternary alluvial sediments |
| Climate | 300 - 500 mm (mean annual rainfall) |
| Land component | 1 | 2 | 3 | 4 | 5 |
| Soil association & dominant soil types | Carag (Carag clay) Wallenjoe (Wallenjoe clay) | Restdown (Restdown clay) Rochester (Rochester clay) | Yuga - Wallenjoe (Yuga clay, Wallenjoe clay) | Koga (Koga clay loam) | Koyuga (Koyuga clay loam) |
| Landform element | Swamp / Site drainage depressions | Low alluvial /gilgai plains | Lower alluvial plain | Mid alluvial plain | Higher alluvial plain |
| Slope range | 0 - 1 % | 0 - 1 % | 0 - 1 % | 0 - 1 % | 0 - 1 % |
| General soil description | Heavy textured grey cracking clay soils | Heavy textured black cracking clay soils and gilgai formations | Heavy textured black cracking clay soils | High texture contrast soils with clay loam topsoils and mottled brown clay subsoils | High texture contrast soils with clay loam topsoils, bleached A2 horizons and either mottled or whole colored red clay subsoils |
| Factual Key | Ug5.2 | Ug5.1 | Ug5.1 | Db1.33 | Dr2.33, Dr3.43, Dr2.13, Dr3.13 |
| Australian Soil Classification | Grey Vertosol (2) | Black Vertosol (2) | Black Vertosol (2) | Brown Sodosol (2) | Red Sodosol (2) |
| Site Drainage | Very poorly drained | Very poorly drained | Very poorly drained | Imperfectly drained | Imperfectly drained |
| Estimated permeability (subsoil) | Very slowly permeable | Very slowly permeable | Very slowly permeable | Moderately permeable | Moderately permeable |
| Rock outcrop | Nil | Nil | Nil | Nil | Nil |
| Depth to hardrock | > 200 cm | > 200 cm | > 200 cm | > 200 cm | > 200 cm |
| Susceptibility to land degradation | Sheet and rill: Low Wind erosion: Low Gully erosion: Medium | Sheet and rill: Low Wind erosion: Low Gully erosion: Low | Sheet and rill: Medium Wind erosion: Low Gully erosion: Medium | Sheet and rill: Low Wind erosion: Low Gully erosion: Medium | Sheet and rill: Low Wind erosion: Low Gully erosion: Low-med |
| Broad Vegetation Type | Northern Plains Grassy Woodland Complex, Northern Plains Grasslands |
| Current land use | Dryland Grazing | Dryland grazing | Dryland grazing | Dryland cropping and grazing, irrigated pastures | Dryland cropping and grazing, irrigated pasture, dairying |

3.4 Treeless alluvial plain (continued)

Detailed Soil Description

| Land component | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
| Representative soil type | A1 0 - 10 cm Grey (N 4/0) heavy clay, moderate angular blocky structure, gradual transition to: B1 10 - 60 cm Steel grey (N 5/0) heavy clay, moderate angular blocky structure, gradual transition to: B2 60 - 120+ cm Heavy clay with calcium carbonate | A 0 - 10 cm Dark grey (10YR 3/1) cracking medium clay, moderate subangular blocky structure, sharp transition to: B1 10 - 50 cm Dark brownish grey (10YR 3/2) heavy clay, moderate angular blocky structure, gradual transition to: B2 50 - 120+ cm Brownish grey heavy clay with calcium carbonate | A1 0 - 10 cm Brownish grey to grey (2.5Y 4/2) light clay, diffusely mottled, sharp transition to: B1 10 - 40 cm Dark brownish grey (10YR 3/2) heavy clay, moderate angular blocky structure, gradual transition to: B21 40 - 55 cm Brownish yellow grey heavy clay, weak angular blocky structure, slight calcium carbonate, gradual transition to: B22 55 - 120+ cm Yellow grey heavy clay, slight calcium carbonate and gypsum | A1 0 - 10 cm Mottled grey brown (7.5YR 4/4) clay loam A2 10 - 15 cm Sporadically bleached, sharp transition to: B1 15 - 50 cm Brown (7.5YR 4/3) to yellowish grey-brown (10YR 4/3) heavy clay, moderate angular blocky structure, gradual transition to: B21 50 - 75 cm Yellowish brown (10YR 5/4) heavy clay, moderate subangular blocky structure, slight calcium carbonate, gradual transition to: B22 75 - 120 cm Yellowish brown medium clay, slight calcium carbonate and gypsum B23 120+ cm Mottled brownish yellow-grey and brown medium clay, slight calcium carbonate | A1 0 - 10 cm Brown (7.5YR 5/4) clay loam, weak angular blocky structure A2 10 - 15 cm Sporadically bleached, apedal, sharp transition to: B1 15 - 50 cm Dark reddish brown (2.5YR 3/4) heavy clay, moderate angular blocky structure, gradual transition to: B21 50 - 75 cm Yellowish brown heavy clay, slight calcium carbonate, gradual transition to: B22 75 - 120 cm Diffusely mottled yellowish brown medium clay , slight calcium carbonate and gypsum B23 120+ cm Moderately mottled brownish yellow-grey and brown medium clay, slight calcium carbonate |
| Source of detailed soils information | Skene, J.K.M. (1963) Wallenjoe clay profile no.24 | Skene, J.K.M. & Harford, L.B. (1964) Rochester clay profile 10 | Skene, J.K.M. & Harford, L.B. (1964) Yuga clay profile 7 | Skene, J.K.M. & Harford, L.B. (1964) Koga clay loam profile 27 | Skene, J.K.M. & Harford, L.B. (1964) Koyuga clay loam profile 4 |

3.4 Treeless alluvial plain (continued)

Standard Planning Responses

| Land System |
| --- |
| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| Rice | 1 | i | Nil | Must comply with the Planning Scheme Refer to Assessment of Land Suitability for Rice Growing Guidelines Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 2 | i | Nil | As above |
|  | 3 | ii | Estimated subsoil permeability | As above |
|  | 4 | iii | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 5 | iii | Estimated subsoil permeability | As above |
| Irrigated cropping | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 4 | ii | Available water capacity Susceptibility to surface crusting | Must comply with the Planning Scheme Refer to Irrigation and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Ground water overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 5 | ii | Susceptibility to surface crusting | As above |
| Irrigated perennial pasture | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 4 | ii | Available water capacity | Must comply with the Planning Scheme Refer to Irrigation and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Ground water overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 5 | i | Nil | As above |

3.4 Treeless alluvial plain (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Irrigated perennial horticulture | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 4 | ii | Site drainage Estimated subsoil permeability | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 5 | ii | Site drainage Estimated subsoil permeability | As above |
| Irrigated tomatoes | 1 | ii | Susceptibility to surface crusting | Must comply with the Planning Scheme Refer to TomCHECK, Guidelines to Successful processing tomato production Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 2 | ii | Susceptibility to surface crusting | As above |
|  | 3 | ii | Available water capacity Susceptibility to surface crusting | As above |
|  | 4 | ii | Available water capacity Susceptibility to surface crusting | As above |
|  | 5 | ii | Susceptibility to surface crusting | As above |
| Irriagted farm forestry | 1 | iii | Site drainage Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 3 | iii | Site drainage Estimated subsoil permeability | As above |
|  | 4 | ii | Estimated subsoil permeability | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 5 | ii | Estimated subsoil permeability | As above |

3.4 Treeless alluvial plain (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Dryland olives | 1 | iii | Estimated subsoil permeability Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Estimated subsoil permeability Site drainage | As above |
|  | 3 | iii | Estimated subsoil permeability Site drainage | As above |
|  | 4 | ii | Site drainage Available water capacity Estimated subsoil permeability | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 5 | ii | Estimated subsoil permeability Site drainage | As above |
| Dryland viticulture | 1 | iii | Estimated subsoil permeability Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Estimated subsoil permeability Site drainage | As above |
|  | 3 | iii | Estimated subsoil permeability Site drainage | As above |
|  | 4 | ii | Site drainage Available water capacity Estimated subsoil permeability | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 5 | ii | Estimated subsoil permeability Site drainage | As above |

3.4 Treeless alluvial plain (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-v) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Broadacre Effluent disposal (feedlots) | 1 | v | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | v | Estimated subsoil permeability | As above |
|  | 3 | v | Estimated subsoil permeability | As above |
|  | 4 | v | Estimated subsoil permeability | As above |
|  | 5 | iv | Estimated subsoil permeability | Must comply with the Planning Scheme Must comply with the Guidelines for the conduct of intensive animal industries Must comply with the Victorian code for Cattle Feedlots or; Must comply with the Code of practice for piggeries or; Must comply with the Code of accepted farming practice for the welfare of domestic fowl Manage to overcome physical limitations (Refer to Appendix A) |
| Effluent disposal (septic tank) | 1 | v | Estimated subsoil permeability | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | v | Estimated subsoil permeability | As above |
|  | 3 | v | Estimated subsoil permeability | As above |
|  | 4 | v | Estimated subsoil permeability | As above |
|  | 5 | iv | Estimated subsoil permeability | Must comply with the planning scheme Must comply with the Code of Practice - Septic Tanks |
| Secondary roads | 1 | iv | Site drainage Flooding risk | Must comply with the Planning Scheme |
|  | 2 | iv | Site drainage | As above |
|  | 3 | iv | Site drainage | As above |
|  | 4 | iv | Site drainage | As above |
|  | 5 | iv | Site drainage | As above |

3.5 Knowsley low undulating sedimentary hills

General Description

| Land System: 2.1Gs4-7 |
| --- |
| Parent material | Permian glacial sediments (tillite, conglomerate, sandstone) |
| Climate | 500 - 550 mm (mean annual rainfall) |
| Land component | 1 | 2 | 3 |
| Soil association | N/A | N/A | N/A |
| Landform element | Gentle crest | Gentle slope | Site drainage depression |
| Slope range | 1 - 4 % | 1 - 8 % | 0 - 2 % |
| General soil description | Strong texture contrast soil with mottled yellow clay subsoils and a conspicuously bleached A2 horizon, often with buckshot and quartz gravels present | Strong texture contrast soil with mottled yellow clay subsoils and a conspicuously bleached A2 horizon, often with buckshot and quartz gravels present | Strong texture contrast soil with mottled yellow clay subsoils and a conspicuously bleached A2 horizon |
| Factual Key | Dy3.41, Dr2.41, Dr3.43 | Dy3.41, Dr2.41, Dr3.43 | Dy3.41, Dy3.42 |
| Australian Soil Classification | Yellow Sodosol (3) Red sodosol (3) | Yellow Sodosol (3) Red sodosol (3) | Yellow Sodosol (2) |
| Site Drainage | Well drained | Well drained | Poorly drained |
| Estimated permeability (subsoil) | Moderately permeable | Moderately permeable | Moderately permeable |
| Rock outcrop | 0 - 10 % | 0 - 5 % | Nil |
| Depth to hardrock | 50 - 150 cm | > 100 cm | > 200 cm |
| Susceptibility to land degradation | Sheet and rill: Medium Wind erosion: Medium Gully erosion: Medium - Low | Sheet and rill: Medium Wind erosion: Medium Gully erosion: Medium - Low | Sheet and rill: Low Wind erosion: Medium Gully erosion: Low - High |
| Broad Vegetation Type | Northern Plains Grassy Woodland Complex, Box/Ironbark Forest + Woodland Complex |
| Current land use | Grazing, cereal cropping | Grazing, cereal cropping | Grazing |

3.5 Knowsley low undulating sedimentary hills (continued)

Detailed Soil Description

| Land component | 1 | 2 | 3 |
| --- | --- | --- | --- |
| Representative soil type | A1 0 - 10 cm Dark brown (10YR 3/3) loam, weak subangular blocky structure, few gravel fragments, abrupt transition to: A2 10 - 20 cm Brown (10YR 4/3) fine sandy loam, massive, abundant gravel fragments, abrupt transition to: B21 20 - 30 cm Brown (10YR 4/3) heavy clay, moderate angular blocky structure, few gravel fragments B22 30 - 120+ cm Reddish brown (5YR5/4) heavy clay, strong angular blocky structure, few gravel fragments | A1 0 - 10 cm Dark reddish brown (5YR 3/3) fine sandy loam, weak subangular blocky structure, few stone fragments, abrupt transition to: A2 10 - 15 cm Dark reddish brown (5YR 3/3) fine sandy loam, apedal, abundant stone fragments, clear transition to: B1 15 - 45 cm Dark reddish brown (5YR 6/3) heavy clay, weak angular blocky structure, abrupt transition to: B2 45 - 90cm reddish yellow (7.5YR 7/8) medium clay, strong angular blocky structure, few stone fragments, abrupt transition to: BC 90 - 150+ cm Reddish brown (2.5YR 5/4) medium clay, strong angular blocky structure, many stone fragments | Alluvial wash 0 - 5 cm Dark brown (7.5YR 3/3) silty loam, apedal, pH 5.5, abrupt transition to: A1 5 - 15 cm Dark brown (10YR 3/3) silty loam, apedal, pH 6.5, gradual transition to: A21 15 - 30 cm Yellowish brown (10YR 5/4) sandy loam fine sandy, apedal, pH 6.5, abrupt transition to: A22 30 - 45 cm White (10YR 7/3) loamy sand, apedal, pH 6.5, clear transition to: B2 45 -75 cm Light brownish grey (10YR 6/2) sandy clay loam, apedal, pH 5.5, abrupt transition to: C 75 - 85+ cm Weathered sedimentary rock |
| Source of detailed soils information | Lorimer, M.S, & N.R. Shoknecht (1987) Knowsley Land System (site 723) | Lorimer, M.S, & N.R. Shoknecht (1987) Knowsley Land System (site 722) | Lorimer, M.S, & N.R. Shoknecht (1987) Knowsley Land System (site 1124) |

3.5 Knowsley low undulating sedimentary hills (continued)

Standard Planning Responses

| Land System 2.1Gs4.7 |
| --- |
| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| Rice | 1 | iii | Slope Estimated subsoil permeability Depth of sodic clay | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope Estimated subsoil permeability Depth of sodic clay | As above |
|  | 3 | iii | Slope Estimated subsoil permeability | As above |
| Irrigated cropping | 1 | iii | Slope Depth to hard rock Proportion of stones and boulders | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | iii | Slope | As above |
| Irrigated perennial pasture | 1 | iii | Slope | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | ii | Slope Site drainage | Must comply with the Planning Scheme. Refer to the Irrigation and Planning Practice. Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
| Irrigated perennial horticulture | 1 | iii | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Susceptibility to gully erosion Susceptibility to sheet/rill erosion | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |

3.5 Knowsley low undulating sedimentary hills (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Irrigated tomatoes | 1 | iii | Depth to hard rock Proportion of stones and boulders | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Available water capacity Susceptibility to sheet/rill erosion Susceptibility to gully erosion Proportion of stones and boulders | Must comply with the Planning Scheme Refer to TomCHECK, Guidelines to Successful processing tomato production Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | ii | Available water capacity | As above |
| Irrigated farm forestry | 1 | iii | Slope Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | iii | Slope | As above |
| Dryland olives | 1 | iii | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Available water capacity | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
| Dryland viticulture | 1 | iii | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Depth to hard rock Available water capacity | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |

3.5 Knowsley low undulating sedimentary hills (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Broadacre Effluent disposal (feedlots) | 1 | iv | Depth to hard rock | Must comply with the Planning Scheme Must comply with the Guidelines for the conduct of intensive animal industries Must comply with the Victorian code for Cattle Feedlots or; Must comply with the Code of practice for piggeries or; Must comply with the Code of accepted farming practice for the welfare of domestic fowl Manage to overcome physical limitations (Refer to Appendix A) |
|  | 2 | ii | Nil | As above |
|  | 3 | iv | Estimated subsoil permeability | As above |
| Effluent disposal (septic tank) | 1 | iv | Depth to hard rock | Must comply with the planning scheme Must comply with the Code of Practice - Septic Tanks |
|  | 2 | ii | Nil | As above |
|  | 3 | iv | Estimated subsoil permeability | As above |
| Secondary roads | 1 | iii | Susceptibility to gully erosion Susceptibility to sheet/rill erosion | Must comply with the Planning Scheme |
|  | 2 | iii | Susceptibility to gully erosion Susceptibility to sheet/rill erosion | As above |
|  | 3 | iv | Site drainage | As above |

3.6 Rushworth low undulating sedimentary hills

General Description

| Land System: 1.1Gs4-1, 1.1Gs4-2, 1.1Gs5-1 |
| --- |
| Parent material | Rushworth low undulating sedimentary hills (mudstone, sandstone) |
| Climate | 400-600 mm (mean annual rainfall) |
| Land component | 1 | 2 | 3 |
| Soil association & dominant soil types | Erwen (Erwen loam shallow phase) | Erwen (Erwen loam, Wenora loam) | Erwen (Wenora loam) |
| Landform element | Gentle crest | Gentle slopes | Site drainage depressions |
| Slope range | 1 - 8 % | 1 - 5 % | 0 - 2 % |
| General soil description | Strong texture contrast soils with brown loam topsoils and red clay subsoils | Strong texture contrast soils with brown loam topsoils, occasional bleached A2 horizons and red clay subsoils | Strong texture contrast soils with loam or clay loam topsoils, bleached A2 horizons and yellow clay subsoils |
| Factual Key | Gn3.13, Dr2.13 | Dr2.13, Dr2.43, Dy3.12, Dy3.42 | Dy3.43 |
| Australian Soil Classification | Red Sodosol (2) | Red Sodosol (2) | Yellow Sodosol (3) |
| Site Drainage | Well drained | Well drained | Poorly drained |
| Estimated permeability (subsoil) | Moderately permeable | Moderately permeable | Slowly permeable |
| Rock outcrop | 0 - 3 % | Nil | Nil |
| Depth to hardrock | 0 - 60 cm | 60 - 150 cm | > 100 cm |
| Susceptibility to land degradation | Sheet and rill: Medium Wind erosion: Low Gully erosion: Low | Sheet and rill: Medium Wind erosion: Low Gully erosion: Medium | Sheet and rill: Low Wind erosion: Medium-Low Gully erosion: Medium |
| Broad Vegetation Type | Box/Ironbark Forest + Woodland Complex |
| Current land use | Grazing | Grazing | Grazing |

3.6 Rushworth low undulating sedimentary hills (continued)

Detailed Soil Description

| Land component | 1 | 2 | 3 |
| --- | --- | --- | --- |
| Representative soil type | A1 0 - 10 cm Greyish brown loam with buckshot gravel B21 10 - 45 cm Red brown heavy clay B22 45 - 60 cm Mottled red clay C 60+ cm Weathered sedimentary rock | A1 0 - 10 cm Greyish brown (5YR 3/2) loam weakly bleached in lower part with buckshot and sedimentary gravels, sharp transition to: B1 10 - 45 cm Red brown (2.5YR 3/6) heavy clay, gradual transition to: B2 45 - 70 cm Reddish brown (5YR 4/6) heavy clay, light calcium carbonate, gradual transition to: B23 70 - 120 cm Mottled red to brownish grey heavy clay, light calcium carbonate, gradual transition to: C 120+ cm Weathered sedimentary rock | A1 0 - 10 cm Dark brownish grey loam or clay loam, gradual transition to: A2 10 - 15 cm Bleached grey-brown loam or clay loam, slight to moderate buckshot and sedimentary gravels, sharp transition to: B1 15 - 45 cm Yellowish brown heavy clay, gradual transition to: B21 45 - 110 cm Mottled grey , yellow, brown clay, few sedimentary fragments, soft calcium carbonate, gradual transition to: B22 110 - 210 cm Mottled grey and brown silty clay, many sedimentary fragments C 210+ cm Weathered sedimentary rock |
| Source of detailed soils information | Skene, J.K.M. & Poutsma, T.J. (1962) Erwen Loam shallow phase profile 31 | Skene, J.K.M. & Poutsma, T.J. (1962) Erwen loam profile 30 | Skene, J.K.M. & Poutsma, T.J. (1962) Wenora loam profile 54 |

3.6 Rushworth low undulating sedimentary hills (continued)

Standard Planning Responses

| Land System 1.1Gs4-1, 1.1Gs4-2, 1.1Gs5-1 |
| --- |
| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| Rice | 1 | iii | Slope Estimated subsoil permeability Depth of sodic clay | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope Estimated subsoil permeability Depth of sodic clay | As above |
|  | 3 | iii | Slope | As above |
| Irrigated cropping | 1 | iii | Slope Depth to hard rock Proportion of stones and boulders | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | iii | Slope | As above |
| Irrigated perennial pasture | 1 | iii | Slope | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | ii | Slope Site drainage | Must comply with the Planning Scheme. Refer to the Irrigation and Planning Practice. Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
| Irrigated perennial horticulture | 1 | iii | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Susceptibility to gully erosion Susceptibility to sheet/rill erosion Depth to hard rock | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |

3.6 Rushworth low undulating sedimentary hills (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Irrigated tomatoes | 1 | iii | Depth to hard rock Proportion of stones and boulders | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Susceptibility to gully erosion Susceptibility to sheet/rill erosion Depth to hard rock Proportion of stones and boulders Available water capacity | Must comply with the Planning Scheme Refer to TomCHECK, Guidelines to Successful processing tomato production Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | ii | Susceptibility to gully erosion Available water capacity | As above |
| Irrigated farm forestry | 1 | iii | Slope Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | iii | Slope | As above |
| Dryland olives | 1 | iii | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Depth to hard rock Available water capacity | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
| Dryland viticulture | 1 | iii | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Depth to hard rock Available water capacity | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |

3.6 Rushworth low undulating sedimentary hills (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-v) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Broadacre Effluent disposal (feedlots) | 1 | v | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | iii | Depth to hard rock | Must comply with the Planning Scheme Must comply with the Guidelines for the conduct of intensive animal industries Must comply with the Victorian code for Cattle Feedlots or; Must comply with the Code of practice for piggeries or; Must comply with the Code of accepted farming practice for the welfare of domestic fowl Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iv | Estimated subsoil permeability | As above |
| Effluent disposal (septic tank) | 1 | v | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | iii | Depth to hard rock | Must comply with the planning scheme Must comply with the Code of Practice - Septic Tanks |
|  | 3 | iv | Estimated subsoil permeability | As above |
| Secondary roads | 1 | iii | Susceptibility to sheet/rill erosion | Must comply with the Planning Scheme |
|  | 2 | iii | Susceptibility to sheet/rill erosion Susceptibility to gully erosion | As above |
|  | 3 | iv | Site drainage | As above |

3.7 Myola East low undulating sedimentary hills

General Description

| Land Systems : 2.1Gs4-5, 2.1Gs4-4, 2.1Gs5.5 |
| --- |
| Parent material | Myola East low undulating sedimentary hills (sandstone, mudstone, silicified shale) |
| Climate | 400 - 520 mm (mean annual rainfall) |
| Land component | 1 | 2 | 3 | 4 |
| Soil association | N/A | N/A | N/A | N/A |
| Landform element | Steeper crest and slopes | Gentle slope | Broad Site drainage depression | Gentle crest |
| Slope range | 3 - 20 % | 1 - 4 % | 0 - 3 % | 1 - 4 % |
| General soil description | Strong texture contrast soil with red clay subsoils, a pale or conspicuously bleached A2 horizon, and ironstone gravel is common in the surface horizons | Strong texture contrast soil with red clay subsoils, a pale or conspicuously bleached A2 horizon, and ironstone gravel is common in the surface horizons | Strong texture contrast soil with mottled yellow clay subsoils and a conspicuously bleached A2 horizon | Strong texture contrast soil with red clay subsoils, a pale or conspicuously bleached A2 horizon, and ironstone gravel is common in the surface horizons |
| Factual Key | Gn3.71, Gn3.13, Dr2.13, Dr2.41 | Dr2.13, Dr2.41, Dr2.22, Dr2.32, Dr3.41 | Dy3.42, Dy3.43, Dr2.42 | Dr2.42, Dr2.43, Dr2.41, Dr2.22, Dr3.32 |
| Australian Soil Classification | Red Dermosol (2), Red Sodosol (2) | Red Sodosol (2), Red Kurosol (2) | Yellow Sodosol (2) | Red Sodosol (2), Red Kurosol (2) |
| Site Drainage | Rapidly drained | Well drained | Poorly drained | Well drained |
| Estimated permeability (subsoil) | Highly permeable | Moderately permeable | Moderately permeable | Moderately permeable |
| Rock outcrop | 0 - 20 % | 0 - 5 % | Nil | 0 - 5 % |
| Depth to hardrock | 40 - 70 cm | 60 - 120 cm | 100 - 200 cm | 20 - 60 cm |
| Susceptibility to land degradation | Sheet and rill: High Wind erosion: Low Gully erosion: Medium | Sheet and rill: Low Wind erosion: Medium Gully erosion: Medium | Sheet and rill: Medium Wind erosion: Low Gully erosion: Medium | Sheet and rill: Low Wind erosion: Medium Gully erosion: Low |
| Broad Vegetation Type | Northern Plains Grassy Woodland Complex, Box/Ironbark Forest + Woodland Complex |
| Current land use | Grazing | Grazing | Grazing | Grazing |

3.7 Myola East low undulating sedimentary hills (continued)

Detailed Soil Description

| Land component | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Representative soil type | A1 0 - 10 cm Reddish brown (5YR 5/4) clay loam, weak subangular blocky structure, many gravel and stone fragments, pH 4.5, gradual transition to: B2 10 - 50 cm Reddish brown (5YR 5/4) silty clay, moderate subangular blocky structure, many gravel and stone fragments pH 6.0 BC 50 cm + Weathered shale and clay material | A1 0 - 10 cm Dark brown (7.5YR 4/4) fine sandy loam, pH6.0, clear transition to: B21 10 - 50 cm Red (2.5YR 4/6) light medium clay, sub angular blocky structure, pH 8.5, abrupt transition to: B22 50 - 90 cm Yellowish red (5YR 5/8) light medium clay, moderate subangular blocky structure, pH 9.0, gradual transition to: BC 90+ cm medium clay | Alluvial wash 0 - 10 cm Yellowish red (5YR 4/6) clay loam, moderate sub angular blocky structure, few gravel fragments, pH 6.0, clear transition to: A1 10 - 20 cm Dark reddish brown (5YR 3/4) fine sandy clay loam, weak sub angular blocky, common gravel fragments, pH 6.5, clear transition to: A2 20 - 30 cm Pink (7.5YR 8/4) sandy clay loam, massive, abundant gravel fragments, pH 6.5, clear transition to: B1 30 - 45 cm Strong brown (7.5YR 5/6) sandy clay, massive, many gravel fragments, pH 7.0, gradual transition to: B2 45 - 60 cm Strong brown (7.5YR 5/6) medium clay, moderate sub angular blocky structure, many gravel fragments, pH 7.0 abrupt transition to: C 60+ cm Weathered sedimentary rock | A11 0 - 5 cm Dusky red (2.5YR 3/2) loam, weak subangular blocky structure, few gravel and stone fragments, pH 6.0, clear transition to; A12 5 - 10 cm Dark reddish brown (5YR 3/2) loam, weak subangular blocky structure, many gravel and stone fragments, pH 5.5, clear transition to: A2 10 - 20 cm Yellowish red (5YR 5/6) clay loam, moderate subangular blocky structure, abundant gravel and stone fragments, pH 5.0, clear transition to: B2 20+ cm Reddish yellow (5YR 6/6) silty clay, moderate subangular blocky structure, many gravel and stone fragments, pH4.5 |
| Source of detailed soils information | Lorimer, M.S, & N.R. Shoknecht (1987) Myola East Land System (site 1018) | Lorimer, M.S, & N.R. Shoknecht (1987) Myola East Land System (site 1021) | Lorimer, M.S, & N.R. Shoknecht (1987) Myola East Land System (site 1020) | Lorimer, M.S, & N.R. Shoknecht (1987) Myola East Land System (site 1019) |

3.7 Myola East low undulating sedimentary hills (continued)

Standard Planning Responses

| Land System 2.1Gs4.5, 2.1Gs4.4, 2.1Gs5.5 |
| --- |
| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| Rice | 1 | iii | Slope Estimated subsoil permeability Depth of sodic clay | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope Estimated subsoil permeability Depth of sodic clay | As above |
|  | 3 | iii | Slope Estimated subsoil permeability | As above |
|  | 4 | iii | Slope Estimated subsoil permeability Depth of sodic clay | As above |
| Irrigated cropping | 1 | iii | Slope Site drainage Depth to hard rock Proportion of stones and boulders | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | iii | Slope | As above |
|  | 4 | iii | Slope Depth to hard rock Proportion of stones and boulders | As above |
| Irrigated perennial pasture | 1 | iii | Slope | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Slope | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | ii | Slope Available water capacity Estimated subsoil permeability | As above |
|  | 4 | iii | Slope | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |

3.7 Myola East low undulating sedimentary hills (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Irrigated perennial horticulture | 1 | iii | Site drainage Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Susceptibility to gully erosion Depth of topsoil Depth to hard rock | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 4 | iii | Depth to hard rock | As above |
| Irrigated tomatoes | 1 | iii | Depth to hard rock Proportion of stones and boulders | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Susceptibility to gully erosion Depth to hard rock Proportion of stones and boulders Available water capacity | Must comply with the Planning Scheme Refer to TomCHECK, Guidelines to Successful processing tomato production Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | ii | Susceptibility to gully erosion Susceptibility to sheet/rill erosion Available water capacity | As above |
|  | 4 | iii | Depth to hard rock Proportion of stones and boulders | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
| Irrigated farm forestry | 1 | iii | Slope Site drainage Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | Must comply with the Planning Scheme Refer to the Irrigation and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |

3.7 Myola East low undulating sedimentary hills (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Irrigated farm forestry | 3 | iii | Slope Site drainage | As above |
|  | 4 | iii | Slope Depth to hard rock | As above |
| Dryland olives | 1 | iii | Site drainage Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Depth to hard rock Available water capacity Depth of topsoil | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 4 | iii | Depth to hard rock | As above |
| Dryland viticulture | 1 | iii | Site drainage Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Depth to hard rock Available water capacity Depth of topsoil | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 4 | iii | Depth to hard rock | As above |
| Broadacre Effluent disposal (feedlots) | 1 | iv | Depth to hard rock | Must comply with the Planning Scheme Must comply with the Guidelines for the conduct of intensive animal industries Must comply with the Victorian code for Cattle Feedlots or; Must comply with the Code of practice for piggeries or; Must comply with the Code of accepted farming practice for the welfare of domestic fowl Manage to overcome physical limitations (Refer to Appendix A) |
|  | 2 | iii | Depth to hard rock | As above |
|  | 3 | iv | Estimated subsoil permeability | As above |
|  | 4 | iii | Depth to hard rock | As above |

3.7 Myola East low undulating sedimentary hills (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-v) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Effluent disposal (septic tank) | 1 | iv | Depth to hard rock | Must comply with the planning scheme Must comply with the Code of Practice - Septic Tanks |
|  | 2 | ii | Depth to hard rock | As above |
|  | 3 | iv | Estimated subsoil permeability | As above |
|  | 4 | iii | Depth to hard rock | As above |
| Secondary roads | 1 | iv | Slope Susceptibility to sheet/rill erosion | Must comply with the Planning Scheme |
|  | 2 | iii | Susceptibility to gully erosion | As above |
|  | 3 | iv | Site drainage | As above |
|  | 4 | ii | Nil | As above |

3.8 Mount Camel rolling low volcanic hills

General Description

| Land System: 2.1Gv4, 2.1Gf4 |
| --- |
| Parent material | Cambrian volcanics (greenstones and cherts) |
| Climate | 450 - 550 mm (mean annual rainfall) |
| Land component | 1 | 2 | 3 |
| Soil association and dominant soil types | Colbinabbin (Colbinabbin clay loam, Colbinabbin clay) | Colbinabbin (Colbinabbin clay loam, Colbinabbin clay) | Binabbin (Binabbin clay, Cornella clay) |
| Landform element | Crest and steep rocky slopes | Moderate to gentle colluvial slopes | Very gentle colluvial slopes and alluvial plain |
| Slope range | 5 - 40 % | 5 - 20 % | 0 - 5 % |
| General soil description | Moderately structured soils lacking strong texture contrast with red clay loam topsoils and red clay subsoils | Moderately structured soils lacking strong texture contrast with red clay loam topsoils and red clay subsoils | Moderately structured brown cracking clay soils |
| Factual Key | Gn4.12, Gn3.12, Dr2.13 | Gn3.12, Dr2.13, Uf | Ug5.3 |
| Australian Soil Classification | Red Dermosol (2) | Red Dermosol (2) | Brown Vertosol (2) |
| Site drainage | Rapidly drained | Well drained | Poorly drained |
| Estimated permeability (subsoil) | Highly permeable | Moderately permeable | Slowly permeable |
| Rock outcrop | 0 - 20 % | Nil | Nil |
| Depth to hardrock | 30 - 100 cm | > 100 cm | > 200 cm |
| Susceptibility to land degradation | Sheet and rill: High Wind erosion: Low Gully erosion: Medium - Low | Sheet and rill: Medium Wind erosion: Low Gully erosion: Medium - High | Sheet and rill: Medium Wind erosion: Low Gully erosion: Medium - High |
| Broad Vegetation Type | Northern Plains Grassy Woodland Complex |
| Current land use | Grazing, minor cropping | Grazing, minor cropping | Grazing, cereal cropping |

3.8 Mount Camel rolling low volcanic hills (continued)

Detailed Soil Description

| Land component | 1 | 2 | 3 |
| --- | --- | --- | --- |
| Representative soil type | A1 0 - 10 cm Dark red (2.5YR 3/6) fine sandy clay loam, moderate blocky structure, pH 5.6 B21 10 - 20 cm Dark red (2.5YR 3/6) light medium clay, moderate blocky structure, few quartz and greenstone fragments, pH 6.0 B22 20 - 35 cm Dark red (2.5YR 3/6) light clay, moderate blocky structure, pH 6.6 B23 35 - 60 cm Red (2.5YR 4/8) sandy clay loam C 60 - 100 cm Weathered greenstone rock | A1 0 - 10 cm Dark red (2.5YR 3/6) fine sandy clay loam, moderate blocky structure, pH 5.6 B21 10 - 20 cm Dark red (2.5YR 3/6) light medium clay, moderate blocky structure, few quartz and greenstone fragments, pH 6.0 B22 20 - 35 cm Dark red (2.5YR 3/6) light clay, moderate blocky structure, pH 6.6 B23 35 - 60 cm Red (2.5YR 4/8) sandy clay loam C 60 - 100 cm Weathered greenstone rock | A 0 - 10 cm Dark grey brown (7.5YR 3/3) cracking clay with slight calcium carbonate B21 10 - 40 cm Dark greyish brown (7.5YR 3/4) heavy clay with slight calcium carbonate B22 40 - 75 cm Dark brown (2.5YR 3/4) heavy clay, with slight calcium carbonate and gypsum B23 75 - 180 cm Brown (2.5YR 4/5) heavy clay with light calcium carbonate |
| Source of detailed soils information | Mt Camel Landcare Group - Soil Pit Field Day Notes, Soil Pit No. LP99 | Mt Camel Landcare Group - Soil Pit Field Day Notes, Soil Pit No. LP99 | Skene, J.K.M. & Harford, L.B. (1964) Binnabbin clay profile 34 |

3.8 Mount Camel rolling low volcanic hills (continued)

Standard Planning Responses

| Land System 2.1Gv4, 2.1Gf4 |
| --- |
| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| Rice | 1 | iii | Slope Estimated subsoil permeability Depth of sodic clay | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope Estimated subsoil permeability Depth of sodic clay | As above |
|  | 3 | iii | Slope | As above |
| Irrigated cropping | 1 | iii | Slope | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | ii | Slope Site Drainage Depth to hard rock Proportion of stones and boulders | Must comply with the Planning Scheme. Refer to the Irrigation and Planning Practice. Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
| Irrigated perennial pasture | 1 | iii | Slope Site Drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | ii | Slope Site Drainage | Must comply with the Planning Scheme. Refer to the Irrigation and Planning Practice. Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
| Irrigated perennial horticulture | 1 | iii | Slope Site Drainage Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Susceptibility to gully erosion Susceptibility to sheet/rill erosion Depth of topsoil | Must comply with the Planning Scheme Refer to the Irrigated and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site Drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |

3.8 Mount Camel rolling low volcanic hills (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-iii) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Irrigated tomatoes | 1 | iii | Slope Depth to hard rock Proportion of stones and boulders | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Susceptibility to gully erosion Susceptibility to sheet/rill erosion | Must comply with the Planning Scheme Refer to TomCHECK, Guidelines to Successful processing tomato production Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | ii | Susceptibility to gully erosion Susceptibility to sheet/rill erosion | As above |
| Irrigated farm forestry | 1 | iii | Slope Site Drainage Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iii | Slope | As above |
|  | 3 | ii | Slope Site Drainage | Must comply with the Planning Scheme Refer to the Irrigation and Site drainage Practice Refer to Salinity Management Plan Campaspe West Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
| Dryland olives | 1 | iii | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Depth to hard rock Available water capacity | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site Drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |

3.8 Mount Camel rolling low volcanic hills (continued)

Standard Planning Responses (continued)

| Land Use Activity | Land Component | Class (i-v) | Major Physical Limitations | Planning Response |
| --- | --- | --- | --- | --- |
| Dryland viticulture | 1 | iii | Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | ii | Depth to hard rock Available water capacity | Must comply with the Planning Scheme Refer to Campaspe Catchment Salinity Management Plan Refer to Groundwater overlay Seek advice from the Industry Development Officer within DNRE Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iii | Site Drainage | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
| Broadacre Effluent disposal (feedlots) | 1 | v | Slope Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | iii | Slope | Must comply with the Planning Scheme Must comply with the Guidelines for the conduct of intensive animal industries Must comply with the Victorian code for Cattle Feedlots or; Must comply with the Code of practice for piggeries or; Must comply with the Code of accepted farming practice for the welfare of domestic fowl Manage to overcome physical limitations (Refer to Appendix A) |
|  | 3 | iv | Estimated subsoil permeability | As above |
| Effluent disposal (septic tank) | 1 | v | Slope Depth to hard rock | Development should not occur without a detailed site assessment to determine whether the major engineering or environmental limitations can be economically overcome An alternative form of effluent disposal should be considered |
|  | 2 | iii | Slope | Must comply with the planning scheme Must comply with the Code of Practice - Septic Tanks |
|  | 3 | iv | Estimated subsoil permeability | As above |
| Secondary roads | 1 | v | Slope | Development should not occur without a detailed site assessment to determine whether the major production or environmental limitations can be economically overcome |
|  | 2 | iv | Slope | Must comply with the Planning Scheme |
|  | 3 | iv | Site drainage | As above |

5.    ACKNOWLEDGEMENTS

The authors would sincerely like to thank those staff from the Centre for Land Protection Research and Institute for Sustainable Irrigated Agriculture who contributed to the preparation of this report.

In addition, the authors would also like to thank the planning staff at the Shire of Campapse, particularly Jan Boynton and David Merret for their assistance during the study.

Gathering of soils information would not be possible without the support of the landholders in the district, who provided access to their properties for the collection of detailed soil and landform information.

6.    REFERENCES

Elliot, G.L. and Leys, J.F. 1991 Soil erodibility. Ch. 12. In Soils: their properties and management. Eds. P.E.V. Charman and B.W. Murphy.  Sydney University Press; Soil Conservation Service, NSW.

Environment Protection Authority, Department of Water Resources and Health Department. 1990 Septic tanks code of practice.

Isbell, R.F. 1996 The Australian Soil Classification. CSIRO Publishing, Victoria.

Lorimer, M.S. 1985 Estimating the susceptibility of soil to wind erosion in Victoria. J. Aust. Inst. Ag. Sci. 51: 122-126.

McDonald, R.C., Isbell, R.F., Speight, J.G., Walker, J. and Hopkins, M.S. 1990 Australian soil and land survey - field handbook. Inkata Press.

Northcote, K.N. 1979 A factual key for the recognition of Australian soils.  Rellim Technical Publications Pty. Ltd., South Australia.

Salter, P.J. and Williams J.B.1969 The influence of texture on the moisture characteristics of soil. V. Relationships between particle size composition and moisture contents at the upper and lower limits of available water. J. Soil Sci. 20: 126-31.

Sargent, I.J, Newell, J.W. & Walbran, W.I. 1978 Soils and land use in the Torumbarry Irrigation District, Victoria.  Research Project Series No.49, Department of Agriculture, Victoria.

Skene, J.K.M 1963 Soils and land use in the Deakin Irrigation Area, Victoria. Technical Bulletin No16. Department of Agriculture, Victoria.

Skene, J.K.M 1971 Soils and land use in the Mid Loddon Valley, Victoria. Technical Bulletin No22. Department of Agriculture, Victoria.

Skene, J.K.M & Harford, L.B. 1964 Soils and land use in the Rochester and Echuca Districts, Victoria. Technical Bulletin No17. Department of Agriculture, Victoria.

Skene, J.K.M & Poutsma, T.J 1962 Soils and land use in part of the Goulburn Valley, Victoria. Technical Bulletin No14. Department of Agriculture, Victoria.

APPENDIX A.    GUIDELINES  AND REFERRAL DOCUMENTS

This is not a comprehensive reference list.  Other references may be used and added to this list.

Agriculture Victoria. Getting started.

Anon. 1994 Code of accepted farming practice for the welfare of domestic fowl. Agnote 7, Agriculture Victoria.

Australian Government Publishing Service, Canberra 1987. Guidelines for use of reclaimed water in Australia.

Anon, 1996 TomCheck, Guidelines to successful processing tomato production. Australian Processing Tomatoe Research Council Inc.

Booth, N. and Davies, G. 1996 An Introduction to Olive Growing in Southern Australia. Primary Industries South Australia.

Campaspe West Sub-Regional Working Group 1989 Salinity Managment Plan Campaspe West (Draft).

Campaspe Community Working Group 1992 Campaspe Catchment Salinity Management Plan (Draft).

Coombe, B.G. and Dry P.R. (Eds.) 1995 Viticulture Volume 1 Resources  Winetitles  Adelaide.

Coombe, B.G. and Dry, P.R. (Eds.) 1995 Viticulture Volume 2 Practices Winetitles  Adelaide.

Cornish, J. and Lawler, D. 1995 Design criteria for flood irrigation land layout. Agnote 232, Institute of Sustainable Irrigated Agriculture, Cobram.

Cornish, J.B., Murphy, J.P. and Fowler, C.A. (Eds.) 1990. Irrigation For Profit. Irrigation Association of Australia.

Department of Agriculture, Victoria. Guidelines for the conduct of intensive animal industries.

Depratment of Agriculture Energy and Minerals Victoria  1995 Victorian Code for Cattle Feedlots.

Eden, R.E. 1992 Code of Practice Piggeries. Department of Agriculture, Victoria.

Environment Protection Authority Code of Practice - Septic Tanks.

Ferguson, L., Sibbett, G.S. and Martin, G.C. (Eds.) 1994  Olive Production Manual.  University of California, Division of Agriculture and Natural Resources, Oakland, CA. Publication 3353.

Goodwin, I. 1995 Minisprinkler and microspray irrigation for orchards. Agnote 296, Institute of Sustainable Irrigated Agriculture, Tatura.

Goulburn-Murray Water 1997 Assessment of land suitability for rice growing, Guidelines-1997/98.

James, E. 1995 Testing and interpretation of salinity and pH. Agnote 244, Institute for Horticultural Development, Knoxfield.

Jerie, P. 1994 Choosing an orchard irrigation system. Agnote 192, Institute of Sustainable Irrigated Agriculture, Tatura.

Lolicato, S. 1997 Irrigated Lucerne. Institute of Sustainable Irrigated Agriculture, Tatura.

Lolicato, S. 1997 Maizecheck Recommendations. Institute of Sustainable Irrigated Agriculture, Tatura.

Mehanni, A.H. and Repsys, A.P. 1986 Perennial pasture production after irrigation with saline groundwater in the Goulburn Valley, Victoria. Aust. J. Exp. Agric., 26, 319-24.

Mulcahy, S. and Schroen, J. (Eds.) 1993 Target 10 Irrigation and Drainage Reference Manual. Department of Agriculture, Victoria.

Pritchard, K. 1995 Irrigated summer fodder crops 1: crops for Northern Victoria. Agnote 226, Kyabram Dairy Centre, Institute of Sustainable Irrigated Agriculture.

Rogers, M.E., Noble, C.L., and West, D.W. 1994 Salinity and the growth of forage species. Agnote 284, Institute of Sustainable Irrigated Agriculture, Tatura.

Rural Water Commission of Victoria 1988 Irrigation and Drainage Practice.

Schneider, H. 1995 Soils for fruitgrowing in the Goulburn Valley-Cobram area. Agnote 239, Institute of Sustainable Irrigated Agriculture, Cobram.

Smith, C. 1994 Perennial pastures for irrigated dairy farms in Northern Victoria. Agnote, 194, Kerang.

Vance, W. 1996 Productivity, Socio-Economic and Natural Resource Impact of Changing Catchment Enterprises. Part 2. Development of Industry Options. Department of Natural Resources and Environment.

Varley, A. and McCaffery, D. 1997 Soycheck 1997/98. NSW Agriculture.

Varley, A. and Lacy, J. 1997 Irrigated Wheat Check Recommendations. NSW Agriculture.

Wheeler, J. 1995 Flood irrigation of dairy shed wastewater. Agnote 426, Kyabram Dairy Centre, Institute of Sustainable Irrigated Agriculture.

APPENDIX B.    RESPONSES TO OVERCOME IDENTIFIED LIMITATIONS

B.1   Agricultural land suitability

| Category | Result | Management response |
| --- | --- | --- |
| Slope | Steep slopes may impact upon machinery access to crops or paddocks, particularly under wet conditions. Steep slopes are more susceptible to sheet and rill erosion and are not appropriate for furrow or check bank irrigation. | Fence out paddocks with steep slopes, maintain groundcover, manage for light grazing or forestry purposes. |
| Site drainage | Poor site drainage in clay soils result in waterlogging and ponded surface water. Plant growth is inhibited under these conditions. Alternatively, rapid site drainage in sandy soils may result in insufficient water available for plant growth. | Avoid cropping and horticulture in areas with very poor site drainage. Establish surface/ubsurface drainage where appropriate. Regulate irrigation regime to suit soil type and pasture species, or return to dryland farming practices. |
| Susceptibility to sheet/rill, gully and wind erosion | Loss of topsoil through erosion reduces the soils water and nutrient holding capacity. Plant growth is therefore restricted. Soil erosion will also result in off-site siltation of streams and waterways. | Maintain vegetative ground cover. Establish wind protection barriers. |
| Susceptibility to surface crusting | Soil surface forms a water resistant crust which leads to increased runoff and reduced seedling establishment. | Maintain vegetative groundcover . Apply gypsum if the topsoil is sodic. Increase organic matter content to impoprove topsoil structure. |
| Topsoil depth (cm) | Reduced water and nutrient holding capacity. Reduced volume of soil that can be exploited by plants. For perennial horticulture, shallow topsoils provide inadequate material for mounding. | Increase amount of organic matter by incorporating surface mulch such as green manure crops, stubble or manure. Avoid deep ripping where shallow topsoils are present. |
| Depth to hard rock (m) | Shallow soil depth restricts the rooting depth of plants and thereby limits the amount of water and nutrients available for plant growth. | Fence out paddocks with shallow soils, generally manage for light grazing or forestry purposes. |
| Proportion of stones and boulders (%) | High proportions of stones and boulders increase the maintenance required for farm machinery and reduce the water and nutrients available for plant growth. | Avoid cropping stony rises and rocky plains. |
| Depth to seasonal watertable (m) | Waterlogging in the root zone of plants occurs, as may transportation of soluble salts into the rootzone . Both lead to inhibited plant growth or death of the plant under severe situations. | Plant deep rooted plant species. Establish surface/subsurface drainage where appropriate. Regulate irrigation regime to suit soil type and pasture species, or return to dryland farming practices. |
| Amount of water available to plants | Under dry conditions , insufficient soil-water storage capacity may limit plant growth or lead to plant death. | Increase organic matter by growing green manure crops. Increase the rooting depth of plants by reducing the restrictive layer (ie. deep rip with gypsum if sodic subsoil is restricting root penetration). |
| Electrical conductivity | Electrical conductivity measures the soluble salts stored with the soil, where high soluble salt levels are present in the rootzone, growth is restricted or plant death may occur. | Fence off saline discharge areas and avoid cropping or disturbance of soils. Maintain and improve vegetative cover and reduce grazing pressure in discharge areas. |
| Estimated subsoil permeability | Very poor permeability results in restricted water and air movement in the soil, usually in the clayey subsoil. Therefore, waterlogging is a common problem leading to poor root growth and plant death in severe situations. | Plant deep rooted plant species. Establish surface/subsurface drainage where appropriate. Regulate irrigation regime to suit soil type and pasture species, or return to dryland farming practices. |

B.2  Low density residential and rural living capability

| Category | Result | Management response |
| --- | --- | --- |
| Slope | As the slope increases, so does the difficulty and cost in establishing roads and other infrastructure required to support both urban and rural development. | Where slope is excessive, existing engineering limits will restrict roading, effluent disposal , construction of farm dams and building foundations. Careful planning is required to ensure development is located in appropriate locations. |
| Site drainage | Poor site drainage can lead to failure in the foundations of roads and buildings, and will restrict the effectiveness of septic tanks. | Avoid development in areas of poor drainage. Establish flat bottomed and broad drains up slope to reduce runoff, improve drains down slope where poor site drainage occurs. Consider alternative forms of effluent disposal. Where poor permeability is restrictive but not prohibitive, modify trench length , depth and width ,and utilise evapotranspiration from vegetation to increase the effectiveness of standard septic tanks. |
| Flooding risk | Floods may cause severe damage to roads, bridges buildings and other infrastructure. | Avoid development in areas where there is a significant flood risk. |
| Susceptibility to sheet/rill, gully and wind erosion | Loss of groundcover and increased run-off, particularly on steep slopes, leads to soil erosion. This can result in eroded table drains, blocked cut-off drains, and undercutting of roads and bridges. In addition, runoff contributes to off-site siltation and eutrophication of streams and waterways. | Maintain vegetative ground cover. Identify erosion prone land types, utilise sealed roads with appropriate drainage. Prohibit secondary or gravel roads. |
| Depth to seasonal watertable | The Septic Tank Code of Practice (Environment Protection Authority 1996) requires greater than 0.75 m of unsaturated soil for the proper functioning of effluent disposal trenches. Ideally, the groundwater table should be much lower than one metre, thereby reducing the risk of a rising groundwater table influencing the effectiveness of the absorption trenches. The risk of salinity problems also increase when a water table rises to within 1.0-1.5 m of the soil surface. | Avoid development on areas with shallow watertables. Consider alternative forms of effluent disposal. |
| Depth to hard rock or impermeable layer | The depth to hard rock provides a measure of the effectiveness of the soil profile in filtering the nutrient and bacterial content from the effluent. The Septic Tank Code of Practice (Environment Protection Authority et. al. 1990) requires a depth of at least one metre. In addition, the presence of hard rock may require removal for the purpose of constructing roading, building and dams etc. | Where shallow soils are present, consider alternative forms of effluent disposal , and carefully site roading, buildings and dams etc. |
| Estimated subsoil permeability | Poor subsoil permeability can result in failure of septic tanks and ineffective broadacre effluent disposal, particularly in high rainfall areas. Alternatively, very high permeability may result in rapid leaching of nutrients into groundwater systems or local streams. | Avoid standard septic tanks where very poor/high permeability is present. Seek an alternative form of effluent disposal. Where poor permeability is restrictive but not prohibitive, modify trench length , depth and width ,and utilise evapotranspiration from vegetation to increase the effectiveness of standard septic tanks. |

APPENDIX C.    SPECIFIC NOTES TO ACCOMPANY LAND CAPABILITY/SUITABILITY ASSESSMENT TABLES

C.1   Total amount of water available to plants

Available Water Capacity (AWC) is a measure of the amount of useable water in the soil for plant growth. It is determined from the difference between the amount of water retained by the soil after drainage (field capacity) and the moisture content of a soil at wilting (permanent wilting point). There is a reasonable correlation between soil texture and AWC (Salter and Williams 1969).

Available water capacity of soils

| Range (mm/m) | Average value for calculations (mm/m) | Sands | Sandy loams | Loams | Clay loams | Clays |
| --- | --- | --- | --- | --- | --- | --- |
| 76 - 100 | 90 | KS |  |  |  |  |
| 101 - 125 | 110 | LKS | KSL |  |  |  |
| 126 - 150 | 130 | S |  |  |  | SC, C |
| 151 - 175 | 160 | CS, LS | SL | L | SCL |  |
| 176 - 200 | 190 | FS | FSL | CL, ZL | ZCL | ZC |
| 201 - 225 | 210 | LFS |  |  |  |  |

The total amount of water available to plants can be calculated by adding the amount of available water in each horizon down to a maximum depth of two metres or the rooting depth, e.g. if the subsoil is very sodic the total amount of water available to plants is calculated to the sodic horizon.

Note that gravel content of the soil horizons should be taken into account.

| Soil horizon | Texture | Depth of horizon (m) | AWC of horizon (mm/m) | Available water in horizon (mm) |
| --- | --- | --- | --- | --- |
| A | SL | 0.15 | 160 | 24 |
| B2 | SC | 1.25 | 130 | 143 |

For example, the total amount of water in the worked example above = 167 (Class 2)

C.2   Electrical conductivity

The following correlation between the electrical conductivity of soil samples taken from the 0 - 50 cm layer of the soil profile and soil salinity has been established.

It illustrates the relationship between rating class, soil salinity, EC and site characteristics such as plant growth.

The effects of soil salting on plant growth

| Class | Severity of salting | E.C. dS/m * | Site characteristics |
| --- | --- | --- | --- |
| 1 | Nil/very low | < 0.3 | Plant growth unaffected |
| 2 | Low | 0.30 - 0.53 | Growth of salt-sensitive plants, eg cereals and clover is restricted |
| 3 | Moderate | 0.53 - 1.26 | Patchy pasture growth; salt-sensitive plants are replaced with species that are more salt-tolerant |
| 4 | High | 1.26 - 2.5 | Small areas of bare ground; surviving plant species have high salt tolerance |
| 5 | Very high/severe | > 2.5 | Large areas of bare ground; highly salt-tolerant plants; trees may be dead or dying |

* NB:  1000 µS/cm = 1 dS/m

C.3   Flooding risk

Building regulations prohibit building on flood-prone land, therefore land with some risk of flooding must be identified.  Flooding is unlikely to cause a septic tank to fail, however the risk of polluting the floodwaters with phosphorus, nitrogen and bacterial organisms increases with the number of effluent disposal fields involved.  The dilution factor will be dependent on the quantity of floodwater.

Dams are built to intercept and store run-off water.  It is not possible in these tables to distinguish between seasonal run-off and seasonal flooding; the latter poses a threat to the stability of the dam, and the risk of flooding will depend on the intensity and duration of rainfall, the run-off characteristics of the catchment and the land use within the catchment. Flooding risk is rated below.

Flooding risk

| Risk | Class | Limitation | Condition of flood |
| --- | --- | --- | --- |
| Nil | 1 | No limitation | No flooding |
| Low | 2 | Minor | Minor inundation No debris Flood return period: 1 in 100 years |
| Moderate | 3 | Significant | Broad, slow moving No debris Flood return period: 1 in 100 years |
| High | 4 | Major | Broad, slow moving Little debris Flood return period: 1 in 20 years |
| Severe | 5 | Prohibitive | Deep channel, fast flowing Debris carrying Flood return period: annual |

C.4   Estimated permeability of a soil profile

Permeability is controlled by the least permeable layer of a soil profile and its ability to transmit water.  Permeability is independent of climate and surface drainage.  The rate at which water moves down through the soil profile is an indicator of the tendency of a soil to saturate. It is an important feature if plant growth is to be maintained in areas where rainfall is spasmodic or unreliable.

Permeability provides a measure of the rate at which a saturated soil profile will conduct water to depth.  Permeability measurements may over-estimate the value for the disposal of effluent because the soil macropores are transmitting water, whereas the real situation must take into account the clogging effect of effluent on the bottom of effluent disposal trenches, thereby reducing the rate of water movement into the soil.

The measurement of permeability often produces quite variable results.  Therefore, the setting of class limits is difficult and by necessity must be very broad.  Estimates of permeability can be made for both dry and irrigated lands.

Permeability is influenced by key physical and chemical properties of the soil. By identifying the presence or absence of these properties, an estimate of soil permeability can be determined.

Estimated subsoil permeability

| Parameter | Category | Score |
| --- | --- | --- |
| Principle Profile Form | Uc Gc, Gn, Um Uf, Ug, D | 1 2 3 |
| Subsoil texture (field texture) | (< 20 % clay) sands, loamy sands, sandy loams (25 - 35 % clay) loams, sandy clay loams, clay loams, silty loams, sandy clays, light clays (> 40 % clay) light-medium clay, medium clays, heavy clays | 1 2 3 |
| Subsoil sodicity (ESP)/structure | < 6 (strong to moderate blocky structure/single grain) 6 - 15 > 15 (weak structure, large peds) | 1 2 3 |
| Linear shrinkage (%)/presence of cracking soils | 0 - 12 (no cracking) 13 - 22 > 22 (cracks at least 5mm wide) | 1 2 3 |

| Total score | Estimated permeability | Estimated absorption rate (mm/day) | Time taken for saturated soil to drain to field capacity |
| --- | --- | --- | --- |
| 11 - 12 | Very slowly permeable | < 10 | Months |
| 9 - 10 | Slowly permeable | 10 - 100 | Weeks |
| 7 - 8 | Moderately permeable | 100 - 500 | Days |
| 5 - 6 | Highly permeable | 500 - 1500 | Hours |
| 4 | Very highly permeable | > 1500 | Rarely saturated |

C.5   Susceptibility to gully erosion

No single factor can adequately represent the susceptibility of an area to the gully erosion process. A number of factors are involved and each should be scored independently and then the sum of the scores can be related back to a 5 - class rating.

Susceptibility to gully erosion

| Criteria | Description | Score |
| --- | --- | --- |
| Slope | < 1 % 1 - 3 % 4 - 10 % 11 - 32 % > 32 % | 1 2 3 4 5 |
| Subsoil ESP | < 6 6 - 15 > 15 | 1 4 5 |
| Subsoil structure | Apedal , massive Weak fine < 2 mm mod 2 - 10 mm coarse > 10 mm Moderate fine < 2 mm mod 2 - 10 mm coarse > 10 mm Strong fine < 2 mm mod 2 - 10 mm coarse > 10 mm Apedal single grained | 1 3 2 1 4 3 2 5 3 1 5 |
| Rating for susceptibility to gully erosion: | Class Low Medium High | Total score 3 - 8 9 - 12 13 - 15 |

C.6   Susceptibility to slope failure

The instability of slopes in a catchment area of a dam poses a threat to the storage capacity of that dam.  Additional costs are also involved if the dam requires regular desludging.  This assessment considers that land slips are the result of factors such as soil depth, slope, soil texture, volume of water held in the soil, permeability of the solum and the underlying parent material.  Since the quantity of water in a profile is itself a function of soil texture, depth and permeability, the table below is presented as a first attempt to assess the susceptibility of land to slope failure by relating the total amount of water in the soil profile to the slope.

Susceptibility to slope failure

| Slope | Total amount of water in the soil profile |
| --- | --- |
|  | Low (< 70 mm H20) | Moderate (70 - 170 mm H20) | High (> 170 mm H20) |
| Gentle < 10 % | Very low | Very low | Low |
| Moderate 10 - 32 % | Low | Moderate | High |
| Steep > 32 % | Moderate | High | Very high |

C.7   Susceptibility of soil to sheet and rill erosion by water

The following table has been adapted from Elliott and Leys (1991).  The erodibility index for a range of soil properties closely relates to the susceptibility of soils to erosion by water, and in the tables below, the same soil properties have been used (texture, structure grade, topsoil depth and dispersibility (Emerson aggregate test)) and then related to slope to determine a rating for susceptibility.  The final rating for susceptibility to sheet/rill erosion is read from the second table, once the erodibility of the topsoil and the slope of the area have been assessed.

Erodibility of topsoils

| Soil parameters | Soil Dispersibility |
| --- | --- |
| Texture group (A1) | Structure grade (A1) | Horizon depth (A1 + A2) | Very Low - Low ESP <6 | Medium - High ESP 6 -15 | Very High ESP >15 |
| Sand | apedal | < 0.2 m 0.2 - 0.4 m > 0.4 m | M L L |  |  |
| Sandy loam | apedal weakly pedal | < 0.2 m 0.2 - 0.4 m > 0.4 m < 0.2 m 0.2 - 0.4 m > 0.4 m | M L L H M M | H M E V |  |
| Loam | apedal weakly pedal peds evident | < 0.2 m 0.2 - 0.4 m > 0.4 m < 0.2 m 0.2 - 0.4 m > 0.4 m < 0.2 m 0.2 - 0.4 m > 0.4 m | M L L H M M H H H | H M E V E |  |
| Clay loam | apedal weakly pedal peds evident | < 0.2 m 0.2 - 0.4 m > 0.4 m < 0.2 m 0.2 - 0.4 m > 0.4 m < 0.2 m 0.2 - 0.4 m > 0.4 m | M L L H M M H H M | H M E V E E |  |
| Light clay | weakly pedal peds evident highly pedal | < 0.2 m 0.2 - 0.4 m > 0.4 m < 0.2 m 0.2 - 0.4 m > 0.4 m < 0.2 m 0.2 - 0.4 m > 0.4 m | H M M M M M H M M | E V V V H H E V V | E E E E E E |
| Medium to heavy clay | weakly pedal peds evident highly pedal | < 0.2 m 0.2 - 0.4 m > 0.4 m < 0.2 m 0.2 - 0.4 m > 0.4 m < 0.2 m 0.2 - 0.4 m > 0.4 m | M M M H M M H M M | H H H E V V E V V | E V V E E E E E E |

L - Low         M - Moderate         H - High         V - Very high         E - Extreme

Susceptibility of soil to sheet and rill erosion*

| Slope | Topsoil erodibility (from Table C.10) |
| --- | --- |
|  | Low | Moderate | High | Very high | Extreme |
| < 1 % | Low | Low | Low | Medium | Medium |
| 1 - 3 % | Low | Low | Medium | Medium | Medium |
| 4 - 10 % | Low | Medium | Medium | Medium | High |
| 11 - 32 % | Medium | Medium | Medium | High | High |
| > 32 % | Medium | Medium | High | High | High |

* Note:	Topsoil erodibility is determined from the texture, structure, depth and dispersibility of the topsoil (Table C.7). The susceptibility of the topsoil to sheet and rill erosion relates to the combined effect of slope and topsoil erodibility (Table C.8).

C.8   Susceptibility of soil to erosion by wind

The susceptibility of land to wind erosion is a function of soil erodibility, the probability of erosive winds when the soil is dry and the exposure of the land component to wind (Lorimer 1985).  Soil erodibility is a very important factor to consider in land capability rating tables.

Soil erodibility

| Soil type | Rating |
| --- | --- |
| 1 | Surface soil has a strong blocky structure (aggregates > 0.8 mm), or is apedal and cohesive or has a dense layer of stones, rock or gravel | Low |
|  | Surface soil has strong fine structure (aggregates < 0.8 mm) | Medium |
|  | Surface soil has a weak-moderate structure or is apedal and loose | Go to 2 |
| 2 | Surface soils with organic matter > 20 % | Medium |
|  | Surface soils with organic matter 7 - 20 % | Medium |
|  | Surface soils with organic matter < 7 % | Go to 3 |
| 3 | Surface soils with the following textures: |
|  | Fine-medium sands | High |
|  | Loamy sands | High |
|  | Sandy loams, silty loams | Medium |
|  | Loams, coarse sands | Medium |
|  | Clay loams | Low |
|  | Clays | Low |

C.9   Susceptibility to surface crusting

A surface crust typically forms when raindrops impact on unstable soil surfaces.

In order to compensate for limited information, such as dispersion results and Exchangeable Sodium Percentage (ESP), the table has been produced to estimate the potential susceptibility of a soil to surface crusting.

Estimating susceptibility to surface crusting

| Criteria | Description | Score |
| --- | --- | --- |
| ESP (topsoil) | > 6 | 3 |
|  | < 6 | 1 |
| Topsoil texture | Silty clay loam | 3 |
|  | Silty clay | 3 |
|  | Fine sandy clay loam | 3 |
|  | Clay | 3 |
|  | Clay loam | 2 |
|  | Coarse sandy clay loam | 2 |
|  | Sandy loam | 2 |
|  | Silty loam | 2 |
|  | Loam | 1 |
|  | Organic clay loam | 1 |
| Topsoil structure | Apedal | 3 |
|  | Weak | 3 |
|  | Moderate | 2 |
|  | Strong | 1 |
|  | Self-mulching | 1 |
| Class Low Moderate High |  | Score 3 - 5 6 - 7 8 - 9 |

APPENDIX D.     PHYSICAL AND CHEMICAL  LABORATORY RESULTS

| Site/Laboratory Number | Horizon | Horizon Depth cm | Particle Size Distribution | pH H2O | EC dS/m | Total Soluble Salts % | Organic Carbon % | Total Nitrogen % | Skene K mg/kg | Olsen P mg/kg | Exchangeable Al+++ mg/kg | Exchangeable Bases | Total of Extractable Bases | Exchangeable H+ meq/100g |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Gravel > 2mm % | Coarse sand % | Fine Sand % | Silt % | Clay % |  |  |  |  |  |  |  |  | Ca ++ meq/100g | Mg++ meq/100g | K+ meq/100g | Na+ meq/100g |  |  |
| Field sample, Murray River floodplain |
| Land System: 4.1Ffc3, 4.1Ffc4, 4.1Flfc4. Land component: 3 |
| 970275 | A1 | 0-5 | 0 | 14 | 35 | 34 | 16 | 5.8 | 0.22 | 0.07 | 10 | 0.87 | 570 | 12 | < 10 | 15 | 7.3 | 1.5 | 1.2 | 25.0 | 21.0 |
| 970276 | B21 | 5-16 | 0 | 2 | 24 | 49 | 25 | 6.4 | 0.13 | 0.04 | 0.54 | < 0.05 | 260 | 2 | < 10 | 3.1 | 3.6 | 0.71 | 0.95 | 8.4 | 3.6 |
| 970277 | B23 | 30-70 | 0 | 2 | 21 | 36 | 41 | 6.5 | 0.12 | 0.04 | 0.30 | < 0.05 | 250 | 2 | < 10 | 3.1 | 7 | 0.79 | 1.3 | 12.0 | 4.5 |
| Mount Camel Landcare Group, Soil Pit Field Day. |
| Land System: 2.1Gv4, 2.1Gf4. Land components: 1, 2 |
| LP99 | A1 | 0-7 |  | 6 | 34 | 25 | 30 | 5.6 | < 0.05 |  | 3.0 | 0.34 |  |  |  | 12 | 5.0 | 0.2 | 0.4 | 17.6 |  |
| LP99 | B21 | 7-20 |  | 7 | 32 | 21 | 38 | 6.0 | < 0.05 |  |  |  |  |  |  | 19 | 7.3 | 0.2 | 0.2 | 26.7 |  |
| LP99 | B22 | 20-35 |  | 9 | 31 | 20 | 33 | 6.6 | < 0.05 |  |  |  |  |  |  | 36 | 16 | 0.2 | 0.2 | 52.4 |  |
| LP99 | B23 | 35-60 |  |  |  |  |  | 6.9 | < 0.05 |  |  |  |  |  |  | 39 | 19 | 0.1 | 0.3 | 58.4 |  |
| LP99 | C | 60-100 |  |  |  |  |  | 7.9 | < 0.05 |  |  |  |  |  |  | 32 | 18 | 0.1 | 0.4 | 50.5 |  |
| Skene & Poutsma (1962). Soils and Land Use in part of the Goulburn Valley, Victoria. Technical Bulletin, 14 |
| Congupna clay loam: Profile 47. Land System: 4.2Pf4-2. Land component: 2 |
| 19077 |  | 0-8 | - | 12 | 40 | 16 | 29 | 6.6 | 0.061 | 0.02 | 1.42 | 0.10 |  |  |  | 5.3 | 5.6 | 0.8 | 0.9 | 12.6 |  |
| 19078 |  | 8-33 | - | 7 | 23 | 12 | 57 | 7.4 | 0.182 | 0.06 | 0.61 | 0.07 |  |  |  | 10.5 | 11.2 | 1.3 | 3.5 | 26.5 |  |
| 19079 |  | 33-56 | - | 6 | 21 | 12 | 59 | 8.3 | 0.576 | 0.19 |  |  |  |  |  |  |  |  |  |  |  |
| 19081 |  | 56-84 | - | 6 | 24 | 15 | 53 | 8.7 | 0.878 | 0.29 |  |  |  |  |  | 8.9 | 12.2 | 1.1 | 5.7 | 27.9 |  |
| 19080 |  | 94-152 | - | 9 | 36 | 14 | 40 | 8.6 | 0.697 | 0.23 |  |  |  |  |  |  |  |  |  |  |  |
| Erwen Loam: Profile 30. Land System: 1.1Gs4-1, 1.1Gs4-2, 1.1Gs5-1. Land component: 2 |
| 27019 |  | 0-10 | - | 13 | 39 | 20 | 24 | 6.7 | 0.061 | 0 | 1.52 | 0.11 |  |  |  | 5.5 | 3.8 | 1 | 0.9 | 11.2 |  |
| 27020 |  | 10-43 | - | 6 | 18 | 9 | 66 | 8.1 | 0.182 | 0.1 | 0.53 | 0.08 |  |  |  | 4.7 | 12.8 | 1.8 | 3.9 | 23.2 |  |
| 27021 |  | 43-58 | - | 5 | 18 | 10 | 66 | 8.7 | 0.636 | 0.2 |  |  |  |  |  |  |  |  |  |  |  |
| 27022 |  | 58-94 | 13 | 4 | 18 | 12 | 57 | 9.0 | 0.878 | 0.3 |  |  |  |  |  | 5.9 | 15.2 | 1.9 | 6 | 29 |  |
| 27023 |  | 94-119 | 30 | 5 | 22 | 12 | 51 | 9.1 | 0.878 | 0.3 |  |  |  |  |  |  |  |  |  |  |  |
| Erwen Loam, shallow phase: Profile 31. Land System: 1.1Gs4-1, 1.1Gs4-2, 1.1Gs5-1. Land component: 1 |  |
| 27025 |  | 0-8 | 51 | 10 | 52 | 17 | 20 | 6.2 | 0.061 | 0 |  |  |  |  |  |  |  |  |  |  |  |
| 27026 |  | 8-13 | 14 | 11 | 50 | 16 | 23 | 6.5 | 0.030 | 0 |  |  |  |  |  |  |  |  |  |  |  |
| 27027 |  | 13-33 |  | 6 | 26 | 11 | 55 | 7.2 | 0.061 | 0 |  |  |  |  |  |  |  |  |  |  |  |
| 27028 |  | 33-58 |  | 3 | 18 | 19 | 48 | 8.6 | 0.182 | 0.1 |  |  |  |  |  |  |  |  |  |  |  |
| Goulburn clay loam: Profile 16. Land System: 4.2Pf4-2. Land component: 3 |  |
| 11323 |  | 0-15 | - | 10 | 39 | 24 | 26 | 6.9 | 0.061 | 0 | 1.08 | 0.08 |  |  |  | 6.1 | 3.5 | 1.1 | 0.5 | 11.2 |  |
| 11324 |  | 15-51 | - | 8 | 29 | 18 | 45 | 8.1 | 0.121 | 0 |  |  |  |  |  | 7.2 | 7.9 | 1.1 | 2.3 | 18.5 |  |
| 11325 |  | 51-61 | - | 6 | 28 | 18 | 46 | 8.7 | 0.212 | 0.1 |  |  |  |  |  |  |  |  |  |  |  |
| 11326 |  | 61-84 | - | 8 | 33 | 20 | 40 | 8.9 | 0.394 | 0.1 |  |  |  |  |  |  |  |  |  |  |  |
| 11327 |  | 84-104 | - | 9 | 33 | 22 | 35 | 9.0 | 0.545 | 0.2 |  |  |  |  |  | 4.9 | 7.2 | 1.2 | 3.9 | 17.2 |  |
| 11328 |  | 104-127 | - | 6 | 31 | 19 | 43 | 8.7 | 0.636 | 0.2 |  |  |  |  |  |  |  |  |  |  |  |
| Wenora Loam: Profile 54. Land Systems: 1.1Gs4-1, 1.1Gs4-2, 1.1Gs5-1. Land component: 3 |  |
| 27964 |  | 0-8 | 28 | 4 | 38 | 28 | 28 | 5.8 | 0.091 | 0 |  |  |  |  |  |  |  |  |  |  |  |
| 27965 |  | 8-13 | 67 | 5 | 42 | 29 | 22 | 6.4 | 0.091 | 0 |  |  |  |  |  |  |  |  |  |  |  |
| 27966 |  | 13-28 | 10 | 2 | 26 | 16 | 56 | 7.8 | 0.242 | 0.1 |  |  |  |  |  |  |  |  |  |  |  |
| 27967 |  | 28-51 | 10 | 1 | 19 | 13 | 65 | 8.4 | 0.515 | 0.2 |  |  |  |  |  |  |  |  |  |  |  |
| 27968 |  | 51-81 | 5 | 1 | 22 | 20 | 56 | 8.8 | 0.818 | 0.3 |  |  |  |  |  |  |  |  |  |  |  |
| 27969 |  | 81-130 | - |  | 9 | 21 | 69 | 7.8 | 1.24 | 0.4 |  |  |  |  |  |  |  |  |  |  |  |
| 27970 |  | 130-213 | 16 | 1 | 14 | 42 | 42 | 5.4 | 0.606 | 0.2 |  |  |  |  |  |  |  |  |  |  |  |
| Skene (1963). Soils and Land Use in the Deakin Irrigation Area, Victoria. Technical Bulletin, 16 |
| Corop Clay: Profile 14. Land System: 4.2Flf3, 4.2Flf4. Land component: 2 |
| 9717 |  | 0-8 | - | 3 | 27 | 14 | 54 | 6.5 | 0.125 | 0 | 1.4 | 0.15 |  |  |  |  |  |  |  |  |  |
| 9718 |  | 8-46 | - | 1 | 12 | 10 | 77 | 8.1 | 0.500 | 0.2 |  |  |  |  |  | 9.4 | 19.8 | 1.6 | 6.2 | 37 |  |
| 9719 |  | 46-61 | - | 1 | 10 | 8 | 77 | 8.0 |  | * |  |  |  |  |  |  |  |  |  |  |  |
| 9720 |  | 61-117 | 1 | 1 | 8 | 10 | 77 | 8.0 |  | * |  |  |  |  |  |  |  |  |  |  |  |
| 9721 |  | 117-183 | - | 1 | 7 | 13 | 77 | 8.0 | 2.53 | 0.8 |  |  |  |  |  |  |  |  |  |  |  |
| Kanyapella Clay: Profile 29. Land System: 4.1Ffc3, 4.1Ffc4, 4.1Flfc4. Land component: 1 |
| 8718 |  | 0-10 | - | 6 | 32 | 30 | 29 | 6.3 | 0.093 | 0 | 2.5 | 0.2 |  |  |  |  |  |  |  |  |  |
| 8719 |  | 10-30 | - | 3 | 25 | 28 | 42 | 7.6 | 0.125 | 0 |  |  |  |  |  |  |  |  |  |  |  |
| 8720 |  | 30-43 | - | 2 | 16 | 28 | 52 | 8.9 | 0.563 | 0.2 |  |  |  |  |  |  |  |  |  |  |  |
| 8721 |  | 43-86 | - | 1 | 14 | 28 | 57 | 8.7 | 1.00 | 0.3 |  |  |  |  |  |  |  |  |  |  |  |
| 8723 |  | 86-127 | - | 2 | 12 | 27 | 57 | 8.2 | 1.13 | 0.4 |  |  |  |  |  |  |  |  |  |  |  |
| 8724 |  | 127-183 | - | 2 | 16 | 29 | 52 | 8.1 | 1.06 | 0.3 |  |  |  |  |  |  |  |  |  |  |  |
| Skene & Harford (1963). Soils and Land Use in the Deakin Irrigation Area, Victoria. Technical Bulletin, 16 |
| Binabbin Clay: Profile 34. Land System: 2.1Gv4, 2.1Gf4. Land component: 3 |
| 13055 |  | 0-5 | - | 6 | 25 | 10 | 54 | 7.6 | 0.156 | 0.1 | 2.11 | 0.19 |  |  |  |  |  |  |  |  |  |
| 13056 |  | 5-23 | - | 6 | 23 | 11 | 58 | 7.9 | 0.156 | 0.1 | 1.17 | 0.14 |  |  |  | 32.4 | 8.4 | 1.3 | 0.7 | 42.8 | 2.5 |
| 13057 |  | 23-43 | - | 5 | 23 | 10 | 59 | 8.2 | 0.219 | 0.1 |  |  |  |  |  | 27.8 | 12.4 | 1 | 2.4 | 43.6 | - |
| 13058 |  | 43-71 | - | 5 | 21 | 9 | 56 | 8.7 | 0.344 | 0.1 |  |  |  |  |  |  |  |  |  |  |  |
| 13059 |  | 71-94 | - | 5 | 20 | 10 | 55 | 8.9 | 0.531 | 0.2 |  |  |  |  |  | 14.8 | 16.7 | 1.1 | 8.1 | 40.7 | - |
| 13061 |  | 122-160 | - | 3 | 20 | 11 | 58 | 8.5 | 1.69 | 0.5 |  |  |  |  |  |  |  |  |  |  |  |
| 13063 |  | 183-234 | - | 3 | 19 | 10 | 65 | 8.2 | 1.94 | 0.6 |  |  |  |  |  |  |  |  |  |  |  |
| Carag Clay: Profile 16. Land System: 4.2Pf4-2. Land component: 1 |
| 20722 |  | 0-8 | - | 2 | 23 | 13 | 58 | 6.2 | 0.188 | 0.1 | 2.48 | 0.22 |  |  |  |  |  |  |  |  |  |
| 20723 |  | 8-28 | - | 1 | 13 | 8 | 75 | 7.5 | 0.250 | 0.1 | 0.79 | 0.10 |  |  |  |  |  |  |  |  |  |
| 20724 |  | 28-66 | - | 1 | 17 | 13 | 67 | 8.7 | 0.594 | 0.2 |  |  |  |  |  |  |  |  |  |  |  |
| 20725 |  | 66-89 | - | 2 | 22 | 13 | 61 | 9.0 | 1.00 | 0.3 |  |  |  |  |  |  |  |  |  |  |  |
| 20726 |  | 89-137 | - | 2 | 27 | 13 | 55 | 9.2 | 0.969 | 0.3 |  |  |  |  |  |  |  |  |  |  |  |
| Koga Clay Loam: Profile 27. Land System: 4.2Pf3-1, 4.2Pf4-1, 4.2Pf4-5. Land component: 4 |
| 20662 |  | 0-8 | - | 6 | 41 | 18 | 33 | 7.1 | 0.063 | 0 | 1.03 | 0.1 |  |  |  | 2.7 | 5.2 | 1.1 | 1.4 | 10.4 | 6.7 |
| 20663 |  | 8-38 | - | 3 | 20 | 12 | 64 | 8.2 | 0.281 | 0.1 | 0.62 | 0.09 |  |  |  | 8.3 | 12.6 | 1.0 | 5.0 | 26.9 | - |
| 20664 |  | 38-64 | - | 3 | 20 | 15 | 59 | 8.7 | 1.47 | 0.5 |  |  |  |  |  |  |  |  |  |  |  |
| 20665 |  | 64-107 | - | 3 | 20 | 16 | 59 | 8.2 |  |  |  |  |  |  |  | 4.9 | 13.9 | 1.1 | 9.1 | 29.0 | - |
| 20666 |  | 107-137 | - | 2 | 19 | 18 | 59 | 9.0 | 1.47 | 0.5 |  |  |  |  |  |  |  |  |  |  |  |
| 20667 |  | 152-193 | - | 5 | 25 | 20 | 49 | 8.7 | 1.16 | 0.4 |  |  |  |  |  |  |  |  |  |  |  |
| Koyuga Clay Loam: Profile 4. Land System: 4.2Pf3-1, 4.2Pf4-1, 4.2Pf4-5. Land component:5 |
| 23353 |  | 0-10 | - | 2 | 50 | 23 | 23 | 6.5 | 0.031 | 0.01 | 0.82 | 0.09 |  |  |  | 2.3 | 2.8 | 0.80 | 0.50 | 6.4 | 5.5 |
| 23354 |  | 10-33 | - | 1 | 24 | 14 | 60 | 7.0 | 0.250 | 0.08 | 0.86 | 0.11 |  |  |  | 5.8 | 10.1 | 1.00 | 3.50 | 20.4 | 7.7 |
| 23355 |  | 33-58 | - | 1 | 26 | 16 | 54 | 8.1 | 1.06 | 0.34 |  |  |  |  |  |  |  |  |  |  |  |
| 23356 |  | 58-76 | - | 1 | 28 | 17 | 46 | 8.0 |  | * |  |  |  |  |  |  |  |  |  |  |  |
| 23357 |  | 76-97 | - | 1 | 32 | 20 | 45 | 8.6 | 1.25 | 0.40 |  |  |  |  |  |  |  |  |  |  |  |
| 23358 |  | 97-122 | - | 3 | 34 | 23 | 38 | 8.5 | 1.00 | 0.32 |  |  |  |  |  |  |  |  |  |  |  |
| 23359 |  | 122-145 | - | 2 | 21 | 18 | 57 | 8.5 | 1.25 | 0.40 |  |  |  |  |  |  |  |  |  |  |  |
| 23361 |  | 168-213 | - | 2 | 21 | 25 | 49 | 8.8 | 1.16 | 0.37 |  |  |  |  |  |  |  |  |  |  |  |
| Rochester Clay 'Gilgai Shelf': Profile 10. Land System: 4.2Pf3-1, 4.2Pf4-1, 4.2Pf4-5. Land component: 2 |
| 20684 |  | 0-15 | - | 5 | 27 | 18 | 48 | 7.3 | 0.063 | 0.02 | 1.49 | 0.15 |  |  |  | 15.7 | 6.2 | 0.4 | 1.6 | 23.9 | 5.6 |
| 20685 |  | 15-25 | - | 6 | 25 | 18 | 50 | 8.0 | 0.094 | 0.03 | 0.61 | 0.07 |  |  |  |  |  |  |  |  |  |
| 20686 |  | 25-53 | - | 6 | 24 | 17 | 50 | 8.7 | 0.156 | 0.05 |  |  |  |  |  | 15.2 | 7.2 | 0.7 | 0.8 | 23.9 | - |
| Timmering Loam: Profile 35. Land System: 4.2Pf4-2. Land component: 5 |
| 17853 |  | 0-13 | - | 3 | 53 | 23 | 17 | 6.5 | 0.094 | 0.03 | 2.42 | 0.21 |  |  |  | 6.5 | 2.9 | 0.5 | 0.4 | 10.3 | 6.8 |
| 17854 |  | 13-18 | - | 3 | 52 | 25 | 19 | 7.1 | 0.063 | 0.02 |  |  |  |  |  |  |  |  |  |  |  |
| 17855 |  | 18-46 | - | 2 | 35 | 18 | 45 | 7.3 | 0.250 | 0.08 |  |  |  |  |  | 4.3 | 8.4 | 0.5 | 2.6 | 15.8 | 5.2 |
| 17856 |  | 46-76 | 4 | 1 | 41 | 12 | 44 | 9.3 | 0.531 | 0.17 |  |  |  |  |  | 4.1 | 12.9 | 0.9 | 4.0 | 21.9 | - |
| 17857 |  | 76-91 | - | 1 | 44 | 9 | 43 | 9.4 | 0.407 | 0.13 |  |  |  |  |  |  |  |  |  |  |  |
| 17858 |  | 91-107 | - | 5 | 39 | 11 | 43 | 9.3 | 0.282 | 0.09 |  |  |  |  |  |  |  |  |  |  |  |
| Wallenjoe Clay: Profile 24. Land System: 4.1Ffc3, 4.1Ffc4, 4.1Flfc4. Land component: 2 |
| 17891 |  | 0-15 | - | 1 | 8 | 22 | 66 | 6.6 | 0.125 | 0.04 | 1.18 | 0.13 |  |  |  |  |  |  |  |  |  |
| 17892 |  | 15-56 | - | 2 | 10 | 26 | 60 | 7.0 | 0.156 | 0.05 |  |  |  |  |  |  |  |  |  |  |  |
| 17893 |  | 56-81 | - | 2 | 10 | 24 | 62 | 7.0 | 0.469 | 0.15 |  |  |  |  |  |  |  |  |  |  |  |
| 17894 |  | 81-122 | - | 1 | 11 | 23 | 64 | 7.9 | 0.656 | 0.21 |  |  |  |  |  |  |  |  |  |  |  |
| Wanalta Loam: Profile 5. Land System: 4.2Pf4-2. Land component: 4 |
| 23347 |  | 0-13 | - | 1 | 52 | 25 | 21 | 5.9 | 0.031 | 0.01 | 1.14 | 0.11 |  |  |  | 4.6 | 2.1 | 0.5 | 0.2 | 7.4 | 5.8 |
| 23348 |  | 13-48 | - | - | 25 | 18 | 55 | 8.0 | 0.125 | 0.04 | 0.68 | 0.09 |  |  |  | 11.4 | 10.3 | 1.0 | 1.3 | 24.0 | 3.0 |
| 23349 |  | 48-71 | - | - | 31 | 23 | 42 | 8.8 | 0.406 | 0.13 |  |  |  |  |  |  |  |  |  |  |  |
| 23350 |  | 71-102 | - | - | 31 | 28 | 38 | 8.1 | 0.938 | 0.30 |  |  |  |  |  | 7.2 | 10.4 | 0.7 | 3.2 | 21.5 |  |
| 23351 |  | 114-137 | - | 1 | 21 | 29 | 46 | 7.6 | 2.19 | 0.70 |  |  |  |  |  |  |  |  |  |  |  |
| 23352 |  | 137-198 | - | 1 | 27 | 24 | 46 | 7.1 | 1.97 | 0.63 |  |  |  |  |  |  |  |  |  |  |  |
| Yuga Clay: Profile 7. Land System: 4.2Pf3-1, 4.2Pf4-1, 4.2Pf4-5. Land component: 3 |
| 20705 |  | 0-8 | - | 5 | 39 | 18 | 35 | 6.6 | 0.094 | 0.03 | 1.10 | 0.08 |  |  |  | 3.3 | 6.2 | 0.9 | 1.8 | 12.2 | 8.4 |
| 20706 |  | 8-36 | - | 1 | 14 | 10 | 72 | 8.3 | 0.344 | 0.11 | 0.65 | 0.09 |  |  |  | 8.2 | 15.3 | 1.3 | 6.8 | 31.6 | - |
| 20707 |  | 36-64 | - | 1 | 14 | 11 | 71 | 8.7 | 1.19 | 0.38 |  |  |  |  |  |  |  |  |  |  |  |
| 20708 |  | 64-104 | - | 1 | 19 | 15 | 60 | 8.5 |  | * |  |  |  |  |  | 2.3 | 14.9 | 1.2 | 9.3 | 27.7 | - |
| 20709 |  | 104-157 | - | 1 | 21 | 16 | 56 | 8.2 |  | * |  |  |  |  |  |  |  |  |  |  |  |
| 20710 |  | 157-198 | - | 2 | 25 | 15 | 57 | 8.5 | 1.91 | 0.61 |  |  |  |  |  |  |  |  |  |  |  |
| Lorimer & Schoknecht (1987). A Study of the Land in the Campaspe River Catchment |
| Myola East Land System. Land System: 2.1Gs4-5, 2.1Gs4-4, 2.1Gs5-5. Land component: 1 |
| 1018 | A | 0-10 | 30 | 19 | 32 | 20 | 25 | 4.6 | 0.250 |  | 2.3 | 0.15 | 320 | 28 |  | 0.9 | 1.7 | 0.60 | 0.40 | 3.6 |  |
| 1018 | B | 13-20 | 41 | 16 | 22 | 24 | 36 | 4.7 | 0.210 |  | 0.93 | 0.08 | 400 | 8 |  | 0.3 | 2.5 | 0.50 | 0.40 | 3.7 |  |
| 1018 | B | 20-30 | 12 | 9 | 18 | 28 | 42 | 4.9 | 0.210 |  | 0.58 | 0.08 | 360 | 10 |  | 0.2 | 3.7 | 0.60 | 0.50 | 5.0 |  |
| 1018 | B | 30-53 | 17 |  |  |  |  | 5.9 | 0.260 |  |  |  |  |  |  |  |  |  |  |  |  |
| Myola East Land System. Land System: 2.1Gs4-5, 2.1Gs4-4, 2.1Gs5-5. Land component: 4 |
| 1019 | A11 | 0-6 | 15 | 17 | 37 | 19 | 16 | 5.5 | 0.220 |  | 8.3 | 0.25 | 720 | 150 |  | 10.4 | 3.5 | 1.0 | 0.3 | 15.2 |  |
| 1019 | A12 | 6-10 | 77 | 12 | 45 | 20 | 17 | 5.3 | 0.370 |  | 3.5 | 0.11 | 340 | 55 |  |  |  |  |  |  |  |
| 1019 | A2 | 12-18 | 52 | 12 | 42 | 21 | 21 | 5.0 | 0.550 |  | 1.7 | 0.12 | 460 | 25 |  | 2.3 | 2.7 | 0.4 | 0.6 | 6.0 |  |
| 1019 | B | 20-30 | 8 | 10 | 33 | 22 | 33 | 4.4 | 0.650 |  | 0.77 | 0.06 | 420 | 10 |  | 0.7 | 3.2 | 0.4 | 0.5 | 4.8 |  |
| Myola East Land System. Land System: 2.1Gs4-5, 2.1Gs4-4, 2.1Gs5-5. Land component: 3 |
| 1020 | Aw | 0-7 | 3 | 7 | 36 | 23 | 29 | 6 | 0.100 |  | 2.3 | 0.14 | 640 | 17 |  | 6.9 | 5.6 | 1.2 | 0.2 | 13.9 |  |
| 1020 | A1 | 7-10 | 5 | 10 | 37 | 25 | 27 | 6.2 | 0.038 |  | 1.1 | 0.10 | 520 | 13 |  | 6.2 | 4.9 | 0.9 | 0.3 | 12.3 |  |
| 1020 | A1 | 10-17 | 30 |  |  |  |  | 6.5 | 0.031 |  | 0.58 | 0.05 | 440 | 18 |  |  |  |  |  |  |  |
| 1020 | A2 | 17-20 | 21 |  |  |  |  | 7.3 | 0.025 |  | 0.17 | 0.03 | 360 | 35 |  |  |  |  |  |  |  |
| 1020 | A2 | 20-29 | 23 | 21 | 30 | 14 | 32 | 7.1 | 0.045 |  | 0.20 | 0.02 | 400 | 17 |  | 4.1 | 6.2 | 0.6 | 1.0 | 11.9 |  |
| 1020 | B1 | 30-46 | 19 | 26 | 28 | 10 | 33 | 7.0 | 0.120 |  |  |  |  |  |  | 3.7 | 6.9 | 0.6 | 1.9 | 13.1 |  |
| 1020 | B2 | 46-59 | 20 | 13 | 20 | 8 | 57 | 7.6 | 0.620 |  |  |  |  |  |  | 6.1 | 14.4 | 0.9 | 4.4 | 25.8 |  |
| 1020 | C | 60-90 | 40 | 35 | 13 | 6 | 45 | 8.7 | 0.590 |  |  |  |  |  |  | 4.9 | 13.3 | 0.7 | 5.2 | 24.1 |  |
| Myola East Land System. Land System: 2.1Gs4-5, 2.1Gs4-4, 2.1Gs5-5. Land component: 2 |
| 1021 | A | 0-10 | 5 | 25 | 55 | 5 | 12 | 5.7 | 0.055 |  | 1.2 | 0.09 | 560 | 18 |  | 1.7 | 1.9 | 0.7 | 0.1 | 4.4 |  |
| 1021 | B21 | 10-20 | 4 | 15 | 37 | 4 | 40 | 6.8 | 0.080 |  | 0.70 | 0.06 | 620 | 28 |  | 2.1 | 6.7 | 1.1 | 0.9 | 10.8 |  |
| 1021 | B21 | 20-30 | 1 |  |  |  |  | 7.5 | 0.190 |  | 0.44 | 0.05 | 640 | 27 |  |  |  |  |  |  |  |
| 1021 | B21 | 30-50 | 3 |  |  |  |  | 8.7 | 0.650 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1021 | B22 | 50-60 | 3 | 9 | 24 | 4 | 56 | 9.1 | 1.100 |  |  |  |  |  |  | 2.9 | 12.2 | 1.3 | 4.7 | 21.1 |  |
| 1021 | B22 | 60-90 | 1 |  |  |  |  | 9.1 | 1.200 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1021 | BC | 90-120 | 5 | 8 | 24 | 5 | 58 | 9.0 | 1.400 |  |  |  |  |  |  | 2.1 | 11.3 | 0.8 | 5.3 | 19.5 |  |
| Knowsley Land System. Land System: 2.1Gs4-7. Land component: 2 |
| 722 | A1 | 0-7 | 13 | 13 | 52 | 12 | 17 | 5.5 | 0.068 |  | 3.3 | 0.24 | 240 | 14 |  | 3.9 | 1.3 | 0.70 | 0.07 | 6.0 |  |
| 722 | A2 | 7-10 | 57 |  |  |  |  | 5.4 | 0.029 |  | 1.1 | 0.09 | 100 | 7 |  |  |  |  |  |  |  |
| 722 | A2 | 10-15 | 53 | 19 | 54 | 12 | 19 | 5.7 | 0.028 |  | 0.51 | 0.04 | 90 | 6 |  | 1.7 | 0.88 | 0.29 | 0.08 | 3.0 |  |
| 722 | B1 | 15-20 | 23 |  |  |  |  | 6.6 | 0.077 |  | 0.51 | 0.06 | 240 | 3 |  |  |  |  |  |  |  |
| 722 | B1 | 20-30 | 20 | 3 | 12 | 6 | 76 | 7.2 | 0.110 |  | 0.51 | 0.06 | 380 | 3 |  | 8.7 | 5.9 | 1.6 | 0.80 | 17.0 |  |
| 722 | B2 | 50-60 | 21 | 3 | 14 | 9 | 71 | 7.9 | 0.280 |  |  |  |  |  |  | 7.8 | 8.0 | 1.4 | 1.6 | 18.8 |  |
| 722 | B-C | 80-90 | 25 | 6 | 25 | 22 | 45 | 8.5 | 0.390 |  |  |  |  |  |  | 3.9 | 6.0 | 0.60 | 1.3 | 11.8 |  |
| 722 | B-C | 110-120 | 38 |  |  |  |  | 8.4 | 0.480 |  |  |  |  |  |  |  |  |  |  |  |  |
| 722 | B-C | 140-150 | 42 |  |  |  |  | 8.3 | 0.530 |  |  |  |  |  |  |  |  |  |  |  |  |
| Knowsley Land System. Land System: 2.1Gs4-7. Land component: 1 |
| 723 | A1 | 0-7 | 8 | 16 | 59 | 13 | 9 | 5.4 | 0.028 |  | 1.5 | 0.11 | 140 | 15 |  | 2.0 | 0.77 | 0.42 | 0.08 | 3.3 |  |
| 723 | A2 | 7-10 | 29 |  |  |  |  | 5.3 | 0.024 |  | 0.75 | 0.05 | 80 | 3 |  |  |  |  |  |  |  |
| 723 | A2 | 10-17 | 31 | 19 | 60 | 15 | 5 | 5.8 | 0.017 |  | 0.62 | 0.04 | 80 | 3 |  | 1.3 | 0.55 | 0.20 | 0.13 | 2.2 |  |
| 723 | B | 17-20 | 34 |  |  |  |  | 6.1 | 0.089 |  | 0.42 | 0.04 | 160 | 3 |  |  |  |  |  |  |  |
| 723 | B | 20-30 | 26 | 10 | 31 | 9 | 49 | 6.1 | 0.100 |  | 0.33 | 0.04 | 200 | 4 |  | 4.7 | 9.3 | 0.91 | 1.9 | 16.8 |  |
| 723 | B | 50-60 | 22 |  |  |  |  | 7.3 | 0.330 |  |  |  |  |  |  |  |  |  |  |  |  |
| 723 | B | 80-90 | 21 | 9 | 40 | 12 | 37 | 8.0 | 0.500 |  |  |  |  |  |  | 3.0 | 9.9 | 0.61 | 3.6 | 17.1 |  |
| 723 | B | 110-120 | 22 |  |  |  |  | 7.6 | 0.560 |  |  |  |  |  |  |  |  |  |  |  |  |
| 723 | B-C | 140-150 | 13 |  |  |  |  | 5.1 | 0.780 |  |  |  |  |  |  |  |  |  |  |  |  |
| 723 | B-C | 170-180 | 15 |  |  |  |  | 4.6 | 0.780 |  |  |  |  |  |  |  |  |  |  |  |  |
| Knowsley Land System. Land System: 2.1Gs4-7. Land component: 3 |
| 1124 | Aw | 0-4 | <1 | 10 | 39 | 29 | 18 | 5.4 | 0.075 |  | 2.2 | 0.20 | 215 | 3.0 |  | 4.3 | 3.9 | 0.8 | 0.3 | 9.3 |  |
| 1124 | A1 | 4-10 | 1 | 8 | 37 | 31 | 21 | 5.7 | 0.091 |  | 1.5 | 0.13 | 164 | 1.6 |  | 4.8 | 3.7 | 0.7 | 0.4 | 9.6 |  |
| 1124 | A1 | 10-15 | 1 |  |  |  |  | 5.7 | 0.120 |  | 1.0 | 0.09 | 141 | 1.1 |  |  |  |  |  |  |  |
| 1124 | A21 | 15-20 | 3 |  |  |  |  | 5.9 | 0.090 |  | 0.70 | 0.06 | 128 | 0.9 |  |  |  |  |  |  |  |
| 1124 | A12 | 20-30 | 9 | 18 | 44 | 25 | 11 | 6.4 | 0.022 |  | 0.30 | 0.03 | 81 | 0.6 |  | 5.1 | 1.4 | 0.2 | 0.2 | 6.9 |  |
| 1124 | A22 | 30-46 | 7 | 21 | 50 | 21 | 8 | 6.6 | 0.016 |  |  |  |  |  |  | 0.7 | 0.9 | 0.3 | 0.1 | 2.0 |  |
| 1124 | B21 | 46-60 | 5 | 22 | 41 | 6 | 29 | 6.2 | 0.057 |  |  |  |  |  |  | 1.5 | 5.3 | 0.2 | 0.1 | 7.1 |  |
| 1124 | B21 | 60-76 | 5 |  |  |  |  | 5.9 | 0.100 |  |  |  |  |  |  |  |  |  |  |  |  |
| 1124 | C | 90-106 | 10 | 15 | 28 | 19 | 36 | 6.0 | 0.400 |  |  |  |  |  |  | 1.0 | 10 | <0.1 | 4.2 | 15.3 |  |

APPENDIX E.    LAND CAPABILITY/SUITABILITY CLASS TABLES

Land suitability assessment for irrigated rice production

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope (%) | - | - | - | - | - | - | 3 | - | - | - | - | - | - |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 3 | 2 | 1 | 3 | 2 | 2 | 3 | 2 | 1 | 1 | 2 | 3 | 3 |
| Depth of sodic, heavy - medium clay in the top 3.6 m | - | - | - | - | - | - | - | - | - | - | - | - | - |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | - | - | - | - | - | 3 | 3 | 3 | 3 | 3 | 3 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 2 |
| Depth of sodic, heavy - medium clay in the top 3.6 m | - | - | - | - | - | 3 | 3 | - | 3 | 3 | - |

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 3 | 3 | 3 | 3 | 3 | 3 | 3 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 3 | 3 | 3 | 3 | 3 | 3 | 2 |
| Depth of sodic, heavy - medium clay in the top 3.6 m | 3 | 3 | - | 3 | 3 | 3 | - |

Land suitability assessment for irrigated cropping

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope (%) | - | - | - | - | - | - | 3 | - | - | - | - | - | - |
| Site drainage | 2 | 3 | 3 | 2 | 3 | 3 | 1 | 2 | 3 | 2 | 1 | 1 | 1 |
| Depth of topsoil (cm) | 2 | 2 | 2 | 1 | 2 | 2 | 1 | 1 | 2 | 2 | 2 | 1 | 1 |
| Depth to hard rock | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Proportion of stones and boulders | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Total amount of water available to plants (mm) | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 2 | 1 | 2 | 2 | 1 | 1 |
| Susceptibility to surface crusting | 2 | 2 | 2 | 1 | 2 | 2 | 1 | 2 | 1 | 2 | 1 | 1 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 1 | 3 | 1 | 1 | 1 | 1 | 1 | 3 | 3 | 1 | 1 | 1 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | - | - | - | - | - | 3 | 3 | 3 | 3 | 3 | 3 |
| Site drainage | 3 | 3 | 3 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 2 |
| Depth of topsoil (cm) | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 |
| Depth to hard rock | 1 | 1 | 1 | 1 | 1 | 3 | 2 | 1 | 3 | 2 | 1 |
| Proportion of stones and boulders | 1 | 1 | 1 | 1 | 1 | 3 | 2 | 1 | 3 | 2 | 1 |
| Total amount of water available to plants (mm) | 1 | 1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 |
| Susceptibility to surface crusting | 2 | 2 | 2 | 2 | 2 | 1 | 2 | 2 | 1 | 2 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 3 | 3 | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |

Land suitability assessment for irrigated cropping (continued)

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 3 | 3 | 3 | 3 | 3 | 3 | 3 |
| Site drainage | 3 | 1 | 2 | 1 | 3 | 1 | 2 |
| Depth of topsoil (cm) | 2 | 2 | 1 | 1 | 2 | 2 | 2 |
| Depth to hard rock | 3 | 2 | 1 | 3 | 3 | 1 | 1 |
| Proportion of stones and boulders | 3 | 2 | 1 | 3 | 3 | 1 | 1 |
| Total amount of water available to plants (mm) | 2 | 2 | 2 | 2 | 2 | 2 | 1 |
| Susceptibility to surface crusting | 2 | 2 | 1 | 1 | 2 | 2 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 1 | 1 | 1 | 1 | 1 | 2 |

Land suitability assessment for irrigated perennial pasture (dairying)

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope (%) | - | - | - | - | - | - | 3 | - | - | - | - | - | - |
| Site drainage | 2 | 3 | 3 | 2 | 3 | 3 | 1 | 2 | 3 | 2 | 1 | 1 | 1 |
| Depth of topsoil (cm) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Total amount of water (mm) available to plants | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 2 | 1 | 2 | 2 | 1 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 1 | 3 | 1 | 1 | 1 | 1 | 1 | 3 | 3 | 1 | 1 | 1 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | - | - | - | - | - | 3 | 3 | 2 | 3 | 3 | 2 |
| Site drainage | 3 | 3 | 3 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 2 |
| Depth of topsoil (cm) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 |
| Total amount of water available to plants (mm) | 1 | 1 | 2 | 2 | 1 | 2 | 1 | 1 | 2 | 1 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 3 | 3 | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 3 | 2 | 2 | 3 | 3 | 3 | 2 |
| Site drainage | 3 | 1 | 2 | 1 | 3 | 1 | 2 |
| Depth of topsoil (cm) | 2 | 1 | 1 | 2 | 2 | 1 | 1 |
| Total amount of water available to plants (mm) | 2 | 2 | 2 | 2 | 2 | 2 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 1 | 1 | 1 | 1 | 1 | 1 |

Land suitability assessment for irrigated perennial horticulture

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Site drainage | 3 | 3 | 3 | 3 | 3 | 3 | 1 | 3 | 3 | 3 | 2 | 2 | 1 |
| Susceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Susceptibility to sheet/rill erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Depth of topsoil (cm) | 2 | 2 | 2 | 1 | 2 | 2 | 1 | 1 | 2 | 2 | 2 | 1 | 1 |
| Depth to hard rock (m) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 2 | 3 | 3 | 1 | 3 | 3 | 1 | 3 | 3 | 3 | 2 | 2 | 1 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Site drainage | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 3 | 1 | 1 | 3 |
| Susceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 2 | 2 |
| Susceptibility to sheet/rill erosion | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 1 | 2 | 2 | 1 |
| Depth of topsoil (cm) | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 |
| Depth to hard rock (m) | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 3 | 2 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 2 | 1 | 1 | 2 |

Land suitability assessment for irrigated perennial horticulture (continued)

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 3 | 1 | 1 |
| Site drainage | 3 | 1 | 3 | 1 | 3 | 1 | 3 |
| Suceptibility to gully erosion | 2 | 2 | 2 | 1 | 2 | 2 | 2 |
| Suceptibility to sheet/rill erosion | 2 | 1 | 2 | 1 | 2 | 2 | 2 |
| Depth of topsoil (cm) | 2 | 2 | 1 | 1 | 2 | 2 | 2 |
| Depth to hard rock (m) | 3 | 2 | 1 | 3 | 3 | 1 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 1 | 1 | 1 | 1 | 1 | 2 |

Land suitability assessment for irrigated tomato production

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Suceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Suceptibility to sheet/rill erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Depth of topsoil (cm) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Depth to hard rock (m) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Proportion of stones and boulders (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Susceptibility to surface crusting | 2 | 2 | 2 | 1 | 2 | 2 | 1 | 2 | 1 | 2 | 1 | 1 | 1 |
| Total amount of water available to plants (mm) | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 2 | 1 | 2 | 2 | 1 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Susceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 2 | 2 |
| Susceptibility to sheet/rill erosion | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 1 | 2 | 2 | 1 |
| Depth of topsoil (cm) | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 2 | 1 | 1 |
| Depth to hard rock (m) | 1 | 1 | 1 | 1 | 1 | 3 | 1 | 1 | 3 | 2 | 1 |
| Proportion of stones and boulders (%) | 1 | 1 | 1 | 1 | 1 | 3 | 2 | 1 | 3 | 2 | 1 |
| Susceptibility to surface crusting | 2 | 2 | 2 | 2 | 2 | 1 | 2 | 2 | 1 | 2 | 1 |
| Total amount of water available to plants (mm) | 1 | 1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |

Land suitability assessment for irrigated tomato production (continued)

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 3 | 1 | 1 |
| Susceptibility to gully erosion | 2 | 2 | 2 | 1 | 2 | 2 | 2 |
| Susceptibility to sheet/rill erosion | 2 | 1 | 2 | 1 | 2 | 2 | 2 |
| Depth of topsoil (cm) | 2 | 1 | 1 | 2 | 2 | 1 | 1 |
| Depth to hard rock (m) | 3 | 2 | 1 | 3 | 3 | 1 | 1 |
| Proportion of stones and boulders (%) | 3 | 2 | 1 | 3 | 3 | 1 | 1 |
| Susceptibility to surface crusting | 2 | 2 | 1 | 1 | 2 | 2 | 1 |
| Total amount of water available to plants (mm) | 2 | 2 | 2 | 2 | 2 | 2 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 |

Land suitability assessment for irrigated farm forestry

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope | - | - | - | - | - | - | 3 | - | - | - | - | - | - |
| Site drainage | 2 | 3 | 3 | 2 | 3 | 3 | 1 | 2 | 3 | 2 | 1 | 1 | 1 |
| Depth of topsoil (cm) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Depth to hardrock | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 2 | 3 | 1 | 3 | 3 | 1 | 3 | 3 | 3 | 2 | 2 | 1 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | - | - | - | - | - | 3 | 3 | 3 | 3 | 3 | 3 |
| Site drainage | 3 | 3 | 3 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 2 |
| Depth of topsoil (cm) | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 2 | 1 | 1 |
| Depth to hardrock | 1 | 1 | 1 | 1 | 1 | 3 | 1 | 1 | 3 | 2 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 2 | 1 | 1 | 2 |

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 3 | 3 | 3 | 3 | 3 | 3 | 3 |
| Site drainage | 3 | 1 | 3 | 1 | 3 | 1 | 3 |
| Depth of topsoil (cm) | 2 | 1 | 1 | 2 | 2 | 1 | 1 |
| Depth to hardrock | 3 | 2 | 1 | 3 | 3 | 1 | 1 |
| EC (dS/mECe) | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 1 | 1 | 1 | 1 | 1 | 2 |

Land suitability assessment for dryland olive production

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Site drainage | 3 | 3 | 3 | 3 | 3 | 3 | 1 | 3 | 3 | 3 | 2 | 2 | 1 |
| Susceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Susceptibility to sheet/rill erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Depth of topsoil (cm) | 2 | 2 | 2 | 1 | 2 | 2 | 1 | 1 | 2 | 2 | 2 | 1 | 1 |
| Depth to hard rock (cm) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Total amount of water available to plants (mm) | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 2 | 1 | 2 | 2 | 1 | 1 |
| Soil salinity (dS/m) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 1 |
| Estimated subsoil permeability | 2 | 3 | 3 | 1 | 3 | 3 | 1 | 3 | 3 | 3 | 2 | 2 | 1 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Site drainage | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 3 | 1 | 1 | 3 |
| Susceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Susceptibility to sheet/rill erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Depth of topsoil (cm) | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 |
| Depth to hard rock (cm) | 1 | 1 | 1 | 1 | 1 | 3 | 1 | 1 | 3 | 2 | 1 |
| Total amount of water available to plants (mm) | 1 | 1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 |
| Soil salinity (dS/m)) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 2 | 1 | 1 | 2 |

Land suitability assessment for dryland olive production (continued)

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 3 | 1 | 1 |
| Site Drainage | 3 | 1 | 3 | 1 | 3 | 1 | 3 |
| Susceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Susceptibility to sheet/rill erosion | 2 | 1 | 1 | 1 | 2 | 1 | 1 |
| Depth of topsoil (cm) | 2 | 2 | 1 | 1 | 2 | 2 | 2 |
| Depth to hard rock (cm) | 3 | 2 | 1 | 3 | 3 | 1 | 1 |
| Total amounts of water available to plants (mm) | 2 | 2 | 2 | 2 | 2 | 2 | 1 |
| Soil salinity (dS/m)) | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 1 | 1 | 1 | 1 | 1 | 2 |

Land suitability assessment for dryland viticulture

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Site drainage | 3 | 3 | 3 | 3 | 3 | 3 | 1 | 3 | 3 | 3 | 2 | 2 | 1 |
| Susceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Susceptibility to sheet/rill erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Depth of topsoil (cm) | 2 | 2 | 2 | 1 | 2 | 2 | 1 | 1 | 2 | 2 | 2 | 1 | 1 |
| Depth to hard rock (cm) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Total amount of water available to plants (mm) | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 2 | 1 | 2 | 2 | 1 | 1 |
| Soil salinity (dS/m) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 1 |
| Estimated subsoil permeability | 2 | 3 | 3 | 1 | 3 | 3 | 1 | 3 | 3 | 3 | 2 | 2 | 1 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Site drainage | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 3 | 1 | 1 | 3 |
| Susceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Susceptibility to sheet/rill erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Depth of topsoil (cm) | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 |
| Depth to hard rock (cm) | 1 | 1 | 1 | 1 | 1 | 3 | 1 | 1 | 3 | 2 | 1 |
| Total amount of water available to plants (mm) | 1 | 1 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 |
| Soil salinity (dS/m) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 2 | 1 | 1 | 2 |

Land suitability assessment for dryland viticulture (continued)

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 3 | 1 | 1 |
| Site drainage | 3 | 1 | 3 | 1 | 3 | 1 | 3 |
| Susceptibility to gully erosion | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Susceptibility to sheet/rill erosion | 2 | 1 | 1 | 1 | 2 | 1 | 1 |
| Depth of topsoil (cm) | 2 | 2 | 1 | 1 | 2 | 2 | 2 |
| Depth to hard rock (cm) | 3 | 2 | 1 | 3 | 3 | 1 | 1 |
| Total amount of water available to plants (mm) | 2 | 2 | 2 | 2 | 2 | 2 | 1 |
| Soil salinity (dS/m) | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 1 | 1 | 1 | 1 | 1 | 1 | 2 |

Land capability assessment for broadacre effluent disposal (ground absorption) for feedlots

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Flooding risk | 4 | 4 | 5 | 5 | 4 | 3 | 1 | 3 | 4 | 3 | 2 | 2 | 2 |
| Depth to hard rock or impermeable layer (m) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 2 | 4 | 5 | 2 | 4 | 4 | 2 | 4 | 5 | 5 | 4 | 2 | 2 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 2 | 2 | 1 |
| Flooding risk | 4 | 3 | 3 | 2 | 2 | 1 | 1 | 2 | 1 | 1 | 2 |
| Depth to hard rock or impermeable layer (m) | 1 | 1 | 1 | 1 | 1 | 4 | 2 | 1 | 5 | 3 | 1 |
| Estimated subsoil permeability | 5 | 5 | 5 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 |

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 3 | 2 | 2 | 2 | 5 | 3 | 2 |
| Flooding risk | 1 | 1 | 2 | 1 | 1 | 1 | 1 |
| Depth to hard rock or impermeable layer (m) | 4 | 3 | 2 | 3 | 5 | 2 | 1 |
| Estimated subsoil permeability | 1 | 2 | 4 | 2 | 1 | 2 | 4 |

Land capability assessment (ground absorption) for septic tanks

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Flooding risk | 4 | 4 | 5 | 5 | 4 | 3 | 1 | 2 | 4 | 3 | 2 | 2 | 2 |
| Depth to hard rock or impermeable layer (m) | 1 | 1 | 1 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Estimated subsoil permeability | 2 | 4 | 5 | 2 | 4 | 4 | 2 | 4 | 5 | 5 | 4 | 2 | 2 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 2 | 2 | 1 |
| Flooding risk | 4 | 3 | 3 | 2 | 2 | 1 | 1 | 2 | 1 | 1 | 2 |
| Depth to hard rock or impermeable layer (m) | 1 | 1 | 1 | 1 | 1 | 4 | 2 | 1 | 5 | 3 | 1 |
| Estimated subsoil permeability | 5 | 5 | 5 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 |

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 3 | 2 | 2 | 2 | 5 | 3 | 1 |
| Flooding risk | 1 | 1 | 2 | 1 | 1 | 1 | 1 |
| Depth to hard rock or impermeable layer (m) | 4 | 3 | 2 | 3 | 5 | 2 | 1 |
| Estimated subsoil permeability | 1 | 2 | 4 | 2 | 1 | 2 | 4 |

Land capability assessment for secondary (gravel) roads

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Drainage | 4 | 4 | 4 | 4 | 4 | 4 | 2 | 4 | 4 | 4 | 4 | 3 | 3 |
| Susceptibility to sheet / rill erosion | 2 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
| Susceptibility to gully erosion | 2 | 2 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
| Susceptibility to slope failure | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Flood risk | 4 | 5 | 5 | 5 | 4 | 3 | 1 | 3 | 4 | 3 | 2 | 2 | 2 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Slope (%) | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 1 | 2 | 2 | 1 |
| Drainage | 4 | 4 | 4 | 4 | 4 | 2 | 2 | 4 | 2 | 2 | 4 |
| Susceptibility to sheet / rill erosion | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 2 | 3 | 3 | 2 |
| Susceptibility to gully erosion | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 2 | 2 | 3 | 3 |
| Susceptibility to slope failure | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Flood risk | 4 | 3 | 3 | 2 | 2 | 1 | 1 | 2 | 1 | 1 | 2 |

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Slope (%) | 4 | 2 | 2 | 2 | 5 | 4 | 2 |
| Drainage | 1 | 2 | 4 | 2 | 1 | 2 | 4 |
| Susceptibility to sheet / rill erosion | 4 | 2 | 3 | 2 | 4 | 3 | 3 |
| Susceptibility to gully erosion | 3 | 3 | 3 | 2 | 3 | 3 | 3 |
| Susceptibility to slope failure | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| Flood risk | 1 | 1 | 2 | 1 | 1 | 1 | 1 |

Land capability assessment for low density residential development

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Secondary roads | 4 | 5 | 5 |  | 4 | 4 | 2 | 4 | 4 | 4 | 4 | 3 | 3 |
| Effluent disposal | 5 | 5 | 5 |  | 5 | 5 | 2 | 5 | 5 | 5 | 4 | 4 | 2 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Secondary roads | 4 | 4 | 4 | 4 | 4 | 3 | 3 | 4 | 3 | 3 | 4 |
| Effluent disposal | 5 | 5 | 5 | 5 | 4 | 4 | 2 | 4 | 5 | 3 | 4 |

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Secondary roads | 4 | 3 | 4 | 2 | 5 | 4 | 4 |
| Effluent disposal | 4 | 3 | 4 | 3 | 5 | 3 | 4 |

Land capability assessment for rural living development

| Land System | 4.1Ffc3, 4.1Ffc4 4.1Flfc4 Active floodplains Murray & Campaspe Rivers | 4.2Flf3, 4.2Flf4 Corop wetland complex | 4.2Pf4.2 Prior streams alluvial plain |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 5 |
| Secondary roads | 4 | 5 | 5 |  | 4 | 4 | 2 | 4 | 4 | 4 | 4 | 3 | 3 |
| Effluent disposal | 5 | 5 | 5 |  | 4 | 4 | 2 | 4 | 4 | 4 | 3 | 3 | 2 |

| Land System | 4.2Pf3.1, 4.2Pf4.1, 4.2Pf4.5 Treeless alluvial plain | 2.1Gs4.7 Knowsley low undulating sedimentary hills | 1.1Gs4.1, 1.1Gs4.2 1.1Gs51-21 Rushworth low undulating sedimentary hills |
| --- | --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 5 | 1 | 2 | 3 | 1 | 2 | 3 |
| Secondary roads | 4 | 4 | 4 | 4 | 4 | 3 | 3 | 4 | 3 | 3 | 4 |
| Effluent disposal | 4 | 4 | 4 | 4 | 3 | 3 | 2 | 3 | 4 | 2 | 3 |

| Land System | 2.1Gs4.5, 2.1Gs4.4 2.1Gs5.5 Myola East low undulating sedimentary hills | 2.1Gv4, 2.1Gf4 Mt Camel rolling low volcanic hills |
| --- | --- | --- |
| Map components | 1 | 2 | 3 | 4 | 1 | 2 | 3 |
| Secondary roads | 4 | 3 | 4 | 2 | 5 | 4 | 4 |
| Effluent disposal | 3 | 2 | 3 | 2 | 5 | 3 | 3 |

GLOSSARY

Angular blocky structure:  A cube-shaped ped bounded by six faces (sides)

Apedal:  Describes a soil in which none of the soil material occurs as peds in the moist state.  Such a soil is without apparent structure and is typically massive or single-grained.

Available water for plant growth:  The amount of water in the soil that can be held between field capacity and the moisture content at which plant growth ceases.

Australian Soil Classification (Isbell 1996):  A soil classification recently developed by Ray Isbell.  The classification scheme operates using a hierarchical system and is based on Australian soils data that is significant with regard to land management.

Bleached horizon:  Horizons that are paler than adjacent horizons and are best seen when the soil is dry.  A bleach is generally associated with the A2 horizon, although it is not restricted to it.  It generally occurs over a much less permeable subsoil, pan or hard rock.  A conspicuously bleached horizon is one in which 80% or more of the horizon is bleached, whereas a sporadic bleach occurs irregularly throughout the horizon or as blotches at the interface of the A and B horizons (Northcote, 1979).  This horizon is the most leached part of the soil.  Organic matter, clay, iron, aluminium and nutrient elements have been removed leaving an accumulation of silica, which gives the horizon its whitish colour.  Field observations have established that bleached horizons are often saturated with water and their occurrence is usually an indication of periodic waterlogging.  This can indicate sodic subsoils where this is a strong texture contrast between A and B horizons.

Blocky structure:  See Angular blocky structure

CEC (cation exchange capacity):  The measure of the capacity of a soil to hold the major cations: calcium, magnesium, sodium and potassium (including hydrogen, aluminium and manganese in acid soils).  It is a measure of the potential nutrient reserve in the soil and is therefore an indicator of inherent soil fertility.  An imbalance in the ratio of cations can result in soil structural problems.  High levels of individual cations (e.g. aluminium and manganese) can also be toxic to plants.

Colour  Soil colour is assessed in the moist condition using a Munsell Colour Chart (Munsell Colour Company, 1975) to assess the dominant colour.  Secondary colours, bleaches and mottles are also recorded.  Colour provides a useful indication of a number of profile attributes.  Dark surface soils, for instance indicates a high level of organic matter.  In subsurface horizons (i.e. A2), bleached colours indicate low levels of plant nutrients and that seasonal or periodic waterlogging occurs.  In subsoils, the colour sequence from red to brown and yellow to grey colours, indicate a sequence from well aerated and well drained soils to poorly aerated and poorly drained soils.

Columnar structure:  Soil particles are arrange around a vertical axis with flat faced peds.  The tops of the columns have clearly defined domes.  Columnar structure is often associated with subsoil sodicity.

Compaction:  The process whereby soil density is increased as a result of tillage, stock trampling and/or vehicular trafficking.  Compaction can lead to lower soil permeability, poorer soil aeration resulting in increased erosion hazard and poorer plant productivity.  Deep ripping and conservation tillage can alleviate the condition.

Drainage:  Drainage is a term used to summarise local soil wetness conditions.  It is affected by internal attributes which include soil structure, texture, porosity, hydraulic conductivity, water holding capacity, and external attributes such as evapotranspiration, gradient and length of slope and position in the landscape.  Categories are as follows:

Very poorly drained: Free water remains at or near the surface for most of the year.  Soils are usually strongly gleyed.  Typically a level or depressed site and/or a clayey subsoil.

Poorly drained: All soil horizons remain wet for several months each year.  Soils are usually gleyed, strongly mottled and/or have orange or rusty linings of root channels.

Imperfectly drained: Some soil horizons remain wet for periods of several weeks.  Subsoils are often mottled and may have orange or rusty linings of root channels.

Moderately well-drained: Some soils may remain wet for a week after water addition.  Soils are often whole coloured, but may be mottled at depth and of medium to clayey texture.

Well-drained: No horizon remains wet for more than a few hours after water addition.  Soils are usually of medium texture and not mottled.

Rapidly drained: No horizon remains wet except shortly after water addition.  Soils are usually of coarse texture, or shallow, or both, and are not mottled.

Duplex profile form:  A primary profile form of the Northcote Factual Key (1979) classification.  It describes a soil where there is a sharp contrast in the texture between the A and B horizons (often sandy or loamy surface horizons with a sharp to clear boundary to clay subsoils).

EC (electrical conductivity):  A measure of the conduction of electricity through water.  The value can reflect the amount of soluble salts in an extract and therefore provide an indication of soil salinity.  Saline soils are defined as those with an EC of grater than 1.5 dS/m for a 1:5 soil water extract.

| Value range (dS/m) | Interpretation |
| --- | --- |
| < 0.30 | Very low |
| 0.30 - 0.53 | Low |
| 0.53 - 1.26 | Moderate |
| 1.26 - 2.50 | High |
| > 2.50 | Very high |

ECe (electrical conductivity of the saturation extract):  Using the EC of a 1:5 soil/water suspension and converting to an approximate ECe value by multiplying by appropriate factors for different soils textures.

ESP (exchangeable sodium percentage):  Is a calculation as the proportion of the cation exchange capacity occupied by the sodium ions and is expressed as a percentage.  Sodic soils are categorised as soils with an ESP of 6-14% and strongly sodic soils have an ESP of greater than 15% (see Sodicity).

Factual Key (Northcote 1979):  A soil classification system used in Australia that groups soils into recognisable profile forms.  These are based on visible morphological properties and simple chemical properties and simple chemical properties of a soil and are labelled used an alphanumeric code.

Gully erosion:  Erosion of soil or soft rock material by running water that forms channels larger and deeper than rills (i.e 300 mm).

Gypsum:	 A naturally occurring soft crystalline material that is a hydrated form of calcium sulphate.  Deposits occur naturally in inland Australia.  Gypsum contains approximately 23% calcium and 18% sulphur.  It is used to improve soil structure and reduce crusting in hard setting clay soils.

Hardsetting:  The condition of a dry surface that is compact and hard with no apparent pedal development.

Horizons:  A layer within the soil profile having morphological characteristics (e.g. colour, texture, and structure) differing from the layer above and or/below it.

A horizon: consists of one or more surface mineral horizons and can be subdivided into:

A1 horizon:	this is the mineral horizon at or near the surface, usually with some accumulation of organic matter making the colour darker than the underlying horizon.  This horizon is usually high in biological activity.  The A1 horizon can be further subdivided into the A11 horizon: more organic matter, darker colour with relatively high amounts of biological activity; A12 horizon varies in colour usually lighter, but not pale enough to be and A2 horizon.  A13 and A14 horizons are further options if necessary.

A2 horizon: this is the mineral horizon having either less organic matter; and/or less clay than the surrounding horizons.  It can be differentiated from the A1 and the B horizon by its paler colour.

A3 horizon: this is a transitional horizon between the A and B horizon that is dominated by A horizon properties.

B horizon: consists of one or more mineral soil layers characterised by one or more of the following: a concentration of silicate clays, iron, aluminium, and/or organic matter; a structure and/or consistence unlike the A horizon or any horizon below; stronger colours than the above or below horizon.  The B horizon is subdivided into:

B1 horizon: the transition between the A and B horizons where the underlying B2 horizon properties dominate (as opposed to the A horizon properties).

B2 horizon: the dominant feature is one of the following maximum horizon of clay or pedological development within the profile i.e. different structure; consistence and/or stronger colours than the A horizon or any horizon below.  The B2 horizon can further be divided into B21, B22 and B23 horizons.

B3 horizon: a transition between the B and C horizon where the B2 horizon characteristic dominate.

C horizon:  The layer below the B horizons, that consists of consolidated or unconsolidated parent material and is not significantly affected by soil forming processes.  It is easily recognised by its lack of soil characteristic development and visible geologic structure.

Impeding layer:  Physical barriers (hardpans, rock etc.) or chemical barriers (high salinity or pH layers) that restrict rooting depth and therefore the volume of soil that plants can exploit for nutrients and moisture.

Internal drainage:  Is an indication of waterlogging potential.

Land capability assessment:  A systematic and rational method of determining the relative ability of different areas of land to sustain a specific land use under a nominated level of management without being degraded or causing any long term off-site degradation.

Land units or components:  An area of land, distinct from adjacent units or components because of specific slope, soil, or geomorphological characteristics, e.g. crest, gentle slope, drainage depression.

Land system:  An area of land, distinct from surrounding terrain, that has a specific climatic range, parent material and modal slope.  Made up of a recurring sequence of land elements or components, e.g. sedimentary rolling hills.

Lime:  A naturally occurring calcareous material used to raise the pH of an acidic soil and/or supply calcium for plant growth.  It is effective for treating acid soils.

Land capability assessment:  A systematic and rational method of determining the relative ability of different areas of land to sustain a specific land use under a nominated level of management without being degraded or causing any long term off-site degradation.

Land units or components:  An area of land, distinct from adjacent units or components because of specific slope, soil, or geomorphological characteristics, eg. crest, lower slope.

Land pattern/system:  An area of land, distinct from surrounding terrain, that has a specific climatic range, parent material and modal slope.  Made up of a recurring sequence of land elements or components, eg. sedimentary rolling hills.

Lunettes:  Crescent shaped aeolian deposits of fine sediment located on the eastern sides (or the lee sides) of lake beds or swamps in semi-arid areas of southern Australia.

Mottling:  The presence of more than one soil colour in a horizon.  The soil may differ in colour either within peds or aggregates, or between them.  Mottling occurs as blotches or streaks of subdominant colour throughout the main (ie. matrix) colour.  it does not refer to stains or coloured deposits on ped faces.  Mottling is often an indication  of poor profile drainage but may also be caused by the weathering of the parent material.

Nutrient status:  Sum of exchangeable base cations (Ca, Mg, K)

| Value range (meq/100g) | Interpretation |
| --- | --- |
| < 4 | Very low |
| 4 - 8 | Low |
| 9 - 18 | Moderate |
| 19 - 30 | High |
| > 30 | Very high |

Organic matter:  All constituents of the soil arising from living matter ie. plant and microfauna detritus, fresh or decomposed.  The following values for organic matter have been used in this report:

| Value range (%) | Interpretation |
| --- | --- |
| < 1 | Very low |
| 1 - 2 | Low |
| 2 - 3 | Moderate |
| > 3 | High |
| (* indicates estimated value) (organic matter % = organic C% x 1.72) |

Parent material/rock:  The geological material from which a soil profile develops.  It may be bed-rock or unconsolidated materials including alluvium, colluvium, aeolian deposits or other sediments.

Peds:  The natural unit of soil structure formed by the soil’s tendency to fracture along plains of weakness.

Permeability:  The characteristic of a soil, soil horizon or soil material which governs the rate at which water moves through it.  It is a composite expression of soil properties and depends largely on soil texture, soil structure, the presence of compacted or dense soil horizons and the size and distribution of pores in the soil.  In this study, the permeability has been measured as Ksat (saturated hydraulic conductivity).  Where estimates have been made, based on the properties of the soil profile, this is clearly indicated.

| Value range (mm/day) | Interpretation |
| --- | --- |
| < 10 | Very slow |
| 10 - 100 | Slow |
| 100 - 500 | Moderate |
| 500 - 1500 | Rapid |
| 1500 - 3000 | Very rapid |
| > 3000 | Excessive |

pH (Soil):  A measure of soil acidity and soil alkalinity on a scale of 0 (extremely acidic) to 14 (extremely alkaline), with a pH of 7 being neutral.  It gives an indication of the availability of plant nutrients and relates to the growth requirements of particular crops.  Acid soils are usually deficient in necessary nutrients e.g. calcium and magnesium.

Plant available water capacity (PAWC):  The amount of soil water that can be extracted by the plant.  It is defined as the difference in soil moisture content between the field capacity and the wilting point.  It is expressed as millimetres of plant-available water within the root zone.

Prismatic structure:  Soil particles are arranged around a vertical axis and bound by relatively flat faces.  The top of the prisms are also relatively flat.  Prismatic structure is often associated with subsoil sodicity.

Profile:  The vertical section of the soil from the soil surface down through the horizons including the parent material.

Rill erosion:  Erosion by small channels less than 300 mm deep which can be completely smoothed by normal cultivation.

Recharge:  Movement of surface water down into the underlying groundwaters.

Rock outcrop:  Any exposed area of rock that is inferred to be continuous with the underlying parent material.

Salinity:  A measure of the total soluble salts in a soil.  A saline soil is one with an accumulation of free salts at the soil surface and/or within the profile affecting plant growth and/or land use.  It is generally attributed to changes in land use or natural changes in drainage or climate that affects the movement of water through the landscape.  Salinity levels of soil or water can be tested using Electrical Conductivity (see EC).

Self-mulching:  A structural condition of soils, notably found in the surface soils of Vertosols, where there is a high degree of pedality and the peds naturally fall apart as the soil dries to form a loos surface mulch.

Sheet erosion/sheet wash:  The relatively uniform removal of soil from an area without the development of conspicuous channels.

Slope:  Landform element that is neither a crest or a depression and that has an inclination greater than 1%.  Slope can be broken up into the following categories:

| Value range (%) | Interpretation |
| --- | --- |
| < 1% | Level |
| 1 - 3% | Very gentle slope |
| 4 - 10% | Gentle slope |
| 11 - 20% | Moderate slope |
| 21 - 32% | Moderately steep slope |
| > 32% | Steep slope |

Sodicity:  Is a measure of exchangeable sodium in relation to other exchangeable cations.  It is expressed as the Exchangeable Sodium Percentage (see ESP).  A sodic soil contains sufficient exchangeable sodium to interfere with the growth of plants, including crops.  A soil with an ESP greater than 6 is generally regarded as being a sodic soil in Australia (Northcote and Skene, 1972).  ESP levels are further classified in the Australian Soil Classification (Isbell, 1996).

Sodosol:  A soil order of the Australian Soil Classification (Isbell, 1996).  These soils have a clear or abrupt textural change between A horizons and sodic B horizons.

Soil colour:  Determined by comparison with a standard Munsell soil colour chart or its equivalent.   It includes three variables of colour: hue, value and chroma.

Soil horizon:  A layer within the soil profile with distinct morphological characteristics which are different from the layers above and/or below.  Horizons are more or less parallel to the land surface, except that tongues of material from one horizon may penetrate neighbouring horizons.

Soil profile:  A portion of a soil exposed in a vertical section, extending usually from the land surface to the parent material.   In very general terms, a profile is made of three major layers designated A, B and C horizons.   The A and B horizons are those modified by soil development.  The C horizon is weathering parent material that has not yet been significantly altered by soil forming processes.

Soil texture:  The relative proportions of sand, silt and clay particles in a sample of soil.  The field assessment of texture is based on the characteristics of a bolus of wetted soil moulded by hand.  Six main soil texture groups are recognised

| Texture group | Approx. clay content (%) |
| --- | --- |
| 1. Sands | < 10 |
| 2. Sandy loams | 10 - 20 |
| 3. Loams | 20 - 30 |
| 4. Clay loams | 30 - 35 |
| 5. Light clays | 35 - 40 |
| 6. Heavy clays | > 45 |

Soil texture groups: The topsoil and subsoil texture classes were grouped according to Northcote (1979).

S	Sand, loamy sand, clayey sand

SL	Sandy loam, fine sandy loam, light sandy clay loam

L	Loam, loam fine sandy, silt loam, sandy clay loam

CL	Clay loam, silty clay loam, fine sandy clay loam

LC	Sandy clay, silty clay, light clay, light medium clay

MHC	Medium heavy clay, medium clay, heavy clay

Structure:  Describes the way the soil particles are arranged to form peds.  Peds are units of soil structure that are separated from each other by natural plains of weakness.  They differ from clods that are formed as a result of soil disturbance such as ploughing.

Structure is defined by three characteristics: grade, size and type.

1. GRADE measures the degree of development and the distinctiveness of the peds.  It varies depending on the soil water status and can be divided into five groups:

1. Single grained; loose and incoherent mass of individual particles (Referred to as structureless);

2. Massive; hardsetting coherent mass of soil (also referred to as structureless);

3. Weak; peds indistinct;

4. Moderate; peds are well formed and visible but not distinctive in undisturbed soil, adhesion between peds is usually firm and when displaced between one third and two thirds of the soil material consists of peds;

5. Strong; peds distinct in undisturbed soil, adhesion between peds is firm and when displaced, two thirds or more of the soil material consists of peds.

2. SIZE is measured and described based on the average least dimension of the peds.

3. TYPE of structure has been described throughout the glossary.  For example, prismatic, columnar, blocky structure.

A number of different grades and sizes of peds may occur within a horizon.  An example of this is when prismatic structure exists that then breaks down to small blocky peds.

Subangular blocky structure:  A ped bound by six faces intersecting round edges (i.e. like a rounded cube).

Subsoil:  The B horizon and its subdivisions, excluding the C horizon.

Texture:  The relative proportions of sand, silt and clay particles in a sample of soil.  The field assessment of texture is based on the characteristics of a bolus of wetted soil mould by hand.  Six main soil texture groups are recognised:

| Texture | Approx. clay content (%) |
| --- | --- |
| 1. Sands | < 10 |
| 2. Sandy loams | 10 - 20 |
| 3. Loams | 20 - 30 |
| 4. Clay loams | 30 - 35 |
| 5. Light clays | 35 - 40 |
| 6. Heavy clays | > 45 |

Uniform profile form:  A Primary Profile form of the Factual Key Classification (Northcote, 1979).  These soil profiles have little, if any texture change throughout the profile.  There is generally no textural boundary found within the profile, except for possibly a surface crust.

Vertic properties:  This term is used to describe a subsoil with a field texture of 35% or more clay which experiences significant shrinking and swelling resulting from drying and wetting.  This often results in the development of features such as surface cracking and gilgai formation.  Evidence of vertic properties include the presence of slickensides and/or lenticular peds in the subsoil.  The amount of swelling is dependent of the type of clay present.  These features are of significant importance for engineering purposes such as road construction.  (see Vertosols).

Vertosols:  A soil Order of the Australian Soil Classification (Isbell, 1996).  These clay soils with shrink/swell properties that display strong cracks when dry and have slickensides and/or lenticular structural peds at depth.

# Text boxes

Refer to the Shire of Campapse land systems map

Identify which land component/s occur within the area under assessment.

Refer to Section 3 Land Systems Descriptions and Capability Classes

Identify the land capability/suitability class for the relevant land use.  Also refer to Appendix E for further information on physical limitations.

If rating Class i or ii for agricultural land suitability or Classes i-iv for land capability:

refer to the Shire planning scheme for the relevant land use.

If rating Class iii for agricultural land suitability, or Class v for land capability:

Development should not occur without a detailed site assessment to determine if the major production or environmental limitations can be economically overcome.

If Class i for land capability/suitability and the area complies with the planning scheme, the land is suitable for development, given best management practice.

If Class ii for agricultural land suitability or Classes ii-iv for land capability, and the area complies with the planning scheme, management prescriptions are required to overcome the land and soil constraints (major physical limitations), to ensure sustainable development.

If area does not comply with the Shire planning scheme, development should not occur.